## Slide 1: 802.11a - High Speed PHY in the 5 GHz band PHY overview
Naftali Chayat, 802.11 TGa Chair
BreezeCOM Ltd., ISRAEL

## Slide 2: What is 802.11?
Finalized a standard for Wireless LANs in the 2.4 GHz ISM band in July 1997
  Single MAC, three PHYs: FHSS, DSSS, IR
  Connectionless services
Today the group works on
  High speed PHY in the 5 GHz band
  Higher speed PHY in the 2.4 GHz band
  Wireless PAN (Personal Area Networks)

## Slide 3: 802.11 TGa status
Task Group a formed in July 97
Modulation selected in July 98
Text finalized in Nov 98
First letter ballot issued Nov 98, processed Jan 99, 82% support after revision
Reconfirmation ballot issued Jan 99, to be processed in March 99, initially 92% support

## Slide 4: 802.11a - 5 GHz High Speed PHY Presentation Overview
Main parameters
OFDM basics
ECC, Modulations, Preamble design
Channelization schemes
Spectral mask requirements
Overview of cooperation with other standards bodies (BRAN, MMAC)

## Slide 5: Main Parameters
20 MHz channel spacing
  16.6 MHz signal bandwidth
Multiple data rates- 6 to 54 Mbit/s
  support of 6, 12 and 24 Mbit/s rates is mandatory
OFDM modulation
  BPSK, QPSK, 16QAM or 64QAM on each subcarrier
  pilot assisted coherent detection
802.11 multirate mechanism support

## Slide 6: OFDM Frame Structure
Carrier spacing is 312.5 KHz
Fourier transform performed over 3.2 microseconds
0.8 microsecond Guard Interval for ISI rejection

## Slide 7: Data and Pilot subcarriers
52 non zero subcarriers
  48 data subcarriers
  4 carrier pilot subcarriers
Center frequency subcarrier not used
  leakage in quadrature modulators may corrupt the data

## Slide 8: Error Correction Coding
ECC is a must - some subcarriers may fade
Bit Interleaved Convolutional Coding used
  more robust that trellis in Rayleigh fading
Industry standard K=7, R=1/2 code
  higher coding rates (2/3, 3/4) derived by puncturing
  tail zero bits added to message (trellis termination)
Interleaver spans one OFDM symbol
  latency and complexity considerations

## Slide 9: Supported Rates and Modulations
Modulation of the data subcarriers by either
  BPSK, QPSK, 16QAM or 64QAM
  1, 2, 4, or 6 bits/subcarrier, correspondingly
12 Msubcarriers/sec (48 subcarriers each 4 sec)

## Slide 10: Preamble Structure
Nine repetitions of short sequence in the beginning
  Signal Detection, AGC convergence, Diversity resolution, Timing estimation, Coarse frequency estimation
Two repetitions of long sequence with Guard Interval
  Fine frequency estimation, Channel Estimation

## Slide 11: Channelization in US

## Slide 12: Spectral Mask Requirement
The mask determines worst case ACI
The need to pass local regulatory requirements is explicitly mentioned

## Slide 13: Coordination with other Standards Committees
802.11 TGa cooperates with the European ETSI BRAN (Broadband Radio Access Networks) and with Japanese MMAC (Mobile Multimedia Advisory Council) to achieve commonality in PHY specifications
MMAC Wireless Ethernet group will adopt 802.11a
MMAC Wireless ATM group and BRAN agreed on basic parameters (52 subcarrier OFDM, channel spacing), but adapt some details such as preamble structure and rate signaling to their requirements