## Slide 1: Linkage of RF Generation and Time-base Clocking
Jamshid Khun-Jush
Ericsson Eurolab - Nürnberg
Co-ordinator of HIPERLAN-2 Standard Area &
Chair of Physical Layer Technical Specification Group

## Slide 2: Non-linked Sources
Worst case drift between carrier frequency source and timing clock source
    40 ppm
Tolerable phase shift for 16QAM
    (4*17o + 8*22,5o + 4*45o)/16 = 26.75o
Tolerable time shift
    Let the numbering of subcarriers be from -32 to 31
    A sampling time shift (50 ns) corresponds to 26/32*180o phase shift
    26.75o tolerable phase shift results in a tolerable time shift (50ns*26.75o*32)/(26*180o) = 9.15 ns
Maximum burst length
    9.15ns/40ppm = 229 us corresponding to 57 OFDM symbol
  It is too short and necessitates the use a (very) fast closed loop for tracking of symbol timing.
Notes: Page <number>
        <footer>
<header>
<date/time>
1

## Slide 3: Linked Source
Assuming a frequency acquisition accuracy in the order 2% of sub-carrier spacing
    With a max. frequency error 20ppm*5GHz, the 2%*(20MHz/64) frequency error after fine frequency acquisition corresponds to
  1.25 ppm frequency error which allows a much longer max. burst length and makes the use of a very slow closed loop for tracking of symbol timing possible
Conclusion: The linkage of clocks enables a reduced complexity receiver implementation