## Slide 1
The case for removing the HR/DSSS/FH option.
Phil Belanger - Aironet
Bruce Tuch - Lucent Technologies

## Slide 2
What is it?
HR/DSSS/FH is first and foremost an FH system.
  A HR/DSSS/FH station joins an FH BSS and “hops” with the rest of the BSS.
  CCA and “medium reservation” is done in a 1 MHz wide channel.
  High Rate transmission of the PDU consumes a 22 MHz channel.
It is an FH system that speeds up to HR DS when possible.
It is NOT a system that operates at high speed and falls back to 2 Mbps FH.

## Slide 3
Why remove it?
No Coexistence.
The HR/DSSS/FH mode interferes with all other 802.11 PHYs.
If approved, it will be the worst possible interferer that we have defined.
  Bad interferer for existing FH and DS systems
It doesn’t even coexist with it self.
  co located HR/DSSS/FH systems will not work well

## Slide 4
Why remove it?
It is a single cell system.
  Applications are limited
There is no migration path from existing FH to high speed DS.
It does not provide backwards compatibility from the high rate PHY to FH systems.

## Slide 5
Why remove it?
It is a new PHY.
It does not interoperate with the HR/DSSS PHY.
The charter for TGb states that we are to develop a single PHY.
  This clearly violates that charter.
Options in the standard are bad.

## Slide 6
Why remove it?
Adding this option causes confusion in the market.
  Creating two new incompatible PHYs
  802.11 should present a unified position
High Rate capability is expanding the market for WLANs.
Why repeat the same mistake we made with FH and DS in the 2.4GH band?
This option is yet another thing to explain.
  It becomes an obstacle to adoption

## Slide 7
Please vote to remove HR/DSSS/FH
it is technically ugly
  not well defined in current draft
it is not benign
  “electronic warfare”
it has limited application
it will be expensive
it slows the market adoption of WLANs
802.11b schedule issues