## Slide 1
Distributed access procedures for supporting real-time traffic: Blackburst

## Slide 2
Motivation
Wish to support real-time applications with QoS guarantees, e.g., voice, video
Basic access method - CSMA/CA
  Does not provide QoS guarantees
Centralized access method - polling
  Cannot operate simultaneously in adjacent cells
  Requires an access point

## Slide 3
Requirements
Three interframe spacings, as in the IEEE 802.11 standard
  TSHORT - acknowledgment minipackets
  TMED - real-time (RT) stations
  TLONG - data stations
Sensing capabilities, as in CSMA/CA
Ability of RT stations to send black bursts

## Slide 4
Basic operation
RT station has an access instant
  Transmits for at least TPKT s.
  Schedules the next access instant to DMIN s. in the future
RT station has a scheduled access instant
  If channel has been idle for TMED s., it transmits
  Otherwise, waits until channel has been idle for TMED s. and enters into black burst contention

## Slide 5
Black burst contention
Length of black burst is proportional to delay in accessing the channel
Access instants of distinct stations differ by at least TPKT black bursts differ by at least a black slot
Unique winner after a black burst contention period - the station that has been waiting the longest

## Slide 6
Example of operation

## Slide 7
Negative Acknowledgment
Upon reception of an RT packet, a receiver knows when to expect the next packet
Possibility of using a negative acknowledgment scheme
  Reduced overhead
  Robustness against hidden stations (implied RTS scheme)

## Slide 8
Properties
Compatible with IEEE 802.11
RT traffic has priority over data traffic
RT stations access the channel in round-robin order
RT packets are not subject to collisions
Supports RT stations with distinct bandwidth requirements
Robust against hidden stations

## Slide 9
Voice over 802.11 DS - Performance
2 Mbps 802.11 DS
Average data packet delay = 10 ms
Data Load = 22%
# of voice stations @ 64 Kbps = 14
@ 32 Kbps = 21 Data load = 41%
# of voice stations @ 64 Kbps = 8
@ 32 Kbps = 12

## Slide 10
Publications on Blackburst
João L. Sobrinho and A.S.Krishnakumar, Real-Time Traffic over the IEEE 802.11 Medium Access Control Layer, Bell Labs Technical Journal, Autumn 1996
João L. Sobrinho and A.S.Krishnakumar, Quality-of-Service in Ad Hoc Carrier Sense Multiple Access Wireless Networks, IEEE Journal on Selected Areas in Communications, Vol. 17, No. 8, August 1999