## Slide 1
Dynamic Frequency Selection and Transmit Power Control A potential project for the MAC Enhancement SG
By Jan Boer
Lucent Technologies

## Slide 2
IEEE802.11a and Europe
In the process to get 802.11a adopted as a European ‘HiperLAN’ standard, 802.11b should at least be conformant to European regulations
Draft ERC Decision ERC DEC 99(NN) has been provisionally approved that covers both HIPERLAN/1 and HIPERLAN/2 and defines the revised frequency bands and power limits. Some requirements are not addressed in 802.11.

## Slide 3
RF Power Limits
The requirements are also addressed in the HiperLAN2 systems overview (TR 101 683 V1.1.2 (1999-06))

## Slide 4
Dynamic Frequency Selection (DFS)
share with radar systems, some of which are mobile
requires dynamic adaptation (DFS) to local interference conditions
required to spread their emissions over the available frequency channels
  The requirement to spread is a statistical requirement that should be satisfied on a large scale rather than the scale of a single HIPERLAN system
  Spread across a minimum of 330 MHz, or 255 MHz in the case of equipment used only in the band 5470 – 5725 MHz
    Modem should work in the low and high 5 GHz band
  Details of such a mechanism are to be decided.

## Slide 5
Transmitter Power Control (TPC)
The objective of the TPC mechanism is to reduce the large scale average RF output by at least 3 dB relative to the RF output of systems not implementing TPC.
uplink and downlink

## Slide 6
MAC enhancements
‘hooks’ to implement DFS and TCP available in 802.11a PHY (?)
Mechanism in MAC required to control DFS and TCP
Proposed as project for the MAC enhancement SG:
  requirements
  design mechanism
  details for implementation