## Slide 1: Security Issues with IEEE 802.11
Bob Beach
Symbol Technologies

## Slide 2: Temptations of WLANs
Everything is available for the taking
Nonphysical access to corporate networks
  Bypasses corporate firewall
MU and AP technology readily available
New Technology
  Users still learning to install/use it
  Protocol is moderately defenseless

## Slide 3: Attacks and Attackers are Varied
Breaking into Enterprise
  Steal data, corrupt operation
  Collect IP addresses for other attacks
Simple disruptions are as bad as break-ins
  Fed Ex, UPS use wireless LANs for package sorting
Attackers are worldwide and organized
  Mischief/fun, ideological, commercial

## Slide 4: 802.11 Security Problems
Assumes a relatively benign environment
  Lightweight Authorization/encryption
Some Problem Areas
  Integrity of RF protocol
  MAC Address Forgery
  Detection of Unauthorized APs
  Interaction of 802.11 authorization mechanism and other mechanisms

## Slide 5: Integrity of RF Protocol
Generation of phony management frames
No means to verify identity of sender
May completely (or partially) disrupt network

## Slide 6: Some RF Protocol Attacks
Phony associate requests consume AP resources
Phony power management mode changes
Phony RTS/CTS Packets waste bandwidth
Phony Disassociate requests disconnect MUs
Phony beacons to consume MU battery power
Phony probe responses confuse MU roaming
Phony poll requests steal MU’s data

## Slide 7: RF Protocol Integrity Reqmts
Means to verify identity of sender
Means to prevent replay attacks
  capture and retransmission of “good packets”

## Slide 8: MAC Address Forgery
MAC Addresses are subject to Forgery
  Many Vendors NIC cards can be reprogrammed
  Buy development kits from vendors
Many vendors rely on Access Control Lists for security
Need means to verify MAC address/MU map

## Slide 9: Unauthorized Access Points
“AP in the parking lot”
  Same MAC address as real AP
  Attracts Mobile Units
Goal may be simple mischief or worse
  i.e. Disrupt operation of network
  Everything looks okay, but nothing works
Attack Mobile Unit weaknesses
  Connected to MU, break into it

## Slide 10: Casual User Access Points
User buys AP and attaches it to office LAN
  To Experiment/Play
  To assist others in breaking into corporate net
Once attached, the corporate net is wide open
System Admins are unaware of new AP
  and that corporate security has now been completely compromised

## Slide 11: Detection of Access Points
Need means to detect presence of AP
System Administrators can detect all APs
Cannot be disabled

## Slide 12: 802.11 Authentication Issues
There are enterprise authentication solutions on the horizon
  Windows 2000 uses Kerberos
  IPsec
Such mechanisms may support WLAN authentication and key distribution
802.11 authentication may interfere with such mechanisms

## Slide 13: 802.11 Authentication Issues
No levels of access
  All or nothing
The authenticate, then associate model prevents limited access framework
  MU may communicate with authentication servers but nothing else.
  For example, Kerberos may use Network Time Protocol to obtain timestamps

## Slide 14: Authentication Improvements
Different levels of access
  No access
  Access to authentication servers only
  Full Access
Separate out authentication and encryption functions
  Enterprise authentication, but WEP for privacy

## Slide 15: Conclusions
IEEE 802.11 was designed for a generally benign environment
WLANs are very tempting to hackers
  Increasing attached to corporate networks
  Many types of attacks
Lots of issues that need addressing
  More than just WEP key length