## Slide 1: INTERNATIONAL ROAMING
A SIMPLE APPROACH
FOR WORLD WIDE
DEPLOYMENT

## Slide 2: WHAT IS REQUIRED
MUST MEET REGULATORY REQIREMENTS.
    WILL GET HELP FROM INDUSTRIES TO BRING SOME COUNTRIES IN LINE
DESIRABLE NOT TO REV THE MAC
    KEEP IT SIMPLE
APPLICABLE FOR ALL PHY’S
    THE CURRENT MAC HAS SOME PHY SPECIFIC MANAGEMENT ENTITIES
APPLICABLE FOR IBSS
    BUT BE CAREFULL

## Slide 3: HOW IT WORKS
ACCESS POINTS KEEP THE COUNTRY INFO
    THEY MUST BE CONFIGURED
PASSIVE SCANNING USED ON MOBILE UNITS
    CANNOT XMIT TILL A VALID CHANNEL IS KNOWN
NEW ELEMENTS IN PROBE / PROBE RESPONSE
    PROBE FOR COUNTRY INFO
    RESPOND WITH COUNTRY SPECIFIC INFO

## Slide 4: CONFIGURATION
ONE STA (AP?) MUST BE CONFIGURED TO CORRECT COUNTRY.
A NEW MIB VARIABLE
    THIS ENABLES INTERNATIONAL ROAMING
    IF THIS VARIABLE IS SET, A STA WILL DROP BACK TO PASSIVE SCANNING IF IT LOSSES SYNC WITH IT’S CURRENT ESS.
    APPLICABLE FOR WIRELESS AP’S

## Slide 5: NEW ELEMENTS
IN PROBE
    REQUESTS COUNTRY SPECIFIC INFO
IN PROBE RESPONSE
    COUNTRY NAME STRING (NOT ABSOLUTELY REQUIRED, BUT GOOD FOR PROOF OF COMPLIANCE)
    PHY SPECIFICDATA
        DS, CHANNEL #S
        FH, HOP CHARACTERISTICS

## Slide 6: FH ELEMENT
FLAGS
    0 = 802.11, 1 = HOP DELTA
FIRST CHANNEL
NUMBER OF CHANNELS
TABLE - RANDOM TO INDEX TABLE
    LENGTH = NUMBER OF CHANNELS
    NOTE THAT HOP DELTA COUNTRIES DO NOT INCLUDE THIS TABLE

## Slide 7: DS ELEMENT
FIRST CHANNEL
NUMBER OF CHANNELS