## Slide 1
Streaming Support for 802.11b MAC
Dr. Rajugopal Gubbi
Nov, 1999

## Slide 2: Is Stream Different From (Async) Data?
Asynchronous Data
Little or no latency restrictions
Real-time delivery not an issue
All data frames are treated equally
Streams
Sensitive to latency in delivery
Network throughput is an issue as it controls how many streams can be effectively transported at any given time
Frames from different streams can NOT be treated equally

## Slide 3: What is a Stream?
Streams are virtual connections over the data frame based MAC/PHY services.
A stream is also a set of frames from one application requiring specific services and a specific range of parameter values for the required services. Some of the examples of the services are;
  Latency: How often the stream frames are transmitted independent of the network traffic conditions.
  Bandwidth: How many stream frames are transmitted per second independent of the network traffic conditions.
  Priority: How important is this stream compared to other traffic on the network
  Channel protection: How much error correction or retransmission is carried out on the frames of the stream.

## Slide 4: Why Streaming?
Some sources of streams requiring Qos over 802.11B LANs are
  Cable modem connections
  DSL connections
  WAN connections
Multimedia data generated inside home
  CD quality Audio
  MPEG or other Video streams from camcorders/PCs
If all these data are treated equally at 802.11B MAC, the effort of these layers to provide QoS will be undone at 802.11B MAC

## Slide 5: Some Delivery Requirements
  MPEG needs 4-5Mbps bandwidth for reasonable quality video and can afford latency of about 3 video frames (approx. 100msec).
  VOIP needs 64Kbps (or less) but has the latency requirements in the order of 10msec.
  Interactive games could have varying bandwidth requirement depending on the information exchanged but strict latency requirements.
  Number of retransmissions of a video or voice data frame is limited due to the required large bandwidth and/or the latency involved. Hence need good channel protection.
  When there are data frames of different types at the same STA, their transmission needs to be prioritized to provide better service to more important data.

## Slide 6
Different transmission requirements of different data types demand support for streams
Efficiency requires peer-peer communication during CFP
Interfacing to broadband needs preservation of Quality of service (Qos)
  Priority Classes, BW reservation , Bounded Latency
Interference in the wireless channel demands better mechanisms to improve the channel throughput
Multiple coordinators of different BSSs in a nearby locations need to share channel in an efficient, organized manner
Why is Enhancement Required?

## Slide 7
Simple support at the MAC level for streams and priority services
Collision free channel sharing by multiple overlapping BSSs
Reliable access mechanism for Beacon
Error correction based on type of stream
Demand based retransmissions based in type of stream
Channel agility to move over to a better channel from a severe channel
What are the Required Enhancements?

## Slide 8
YES. They are compatible. There is NO CHANGE to the existing DCF and PCF STAs
  Beacon, CFP and NAV currently exist in 802.11B
  Access mechanism for Beacon can be overlaid over DCF
  Error correction can be made available only for streaming
  More control frames or elements within them can be defined without affecting the compatibility with the existing STAs
Are These Enhancements Compatible?

## Slide 9
YES, because,
Simple stream enhancements to the 802.11 are possible
There are simple but efficient scheduling mechanisms available
Low complexity error correction schemes with little bandwidth overhead are available
Simple, low complexity selective retransmission mechanism is possible
Some form of channel agility is already present in 802.11.
Other required co-ordinations can be achieved by simple control information exchange between the devices based on the demand
Are the Enhancements Feasible?