## Slide 1: Proposal to use KPS to Enhance WLAN Security
Shinicihro Watanabe, Yutaku Kuchiki,
Kazuaki Naito, Masayuki Ikeda
Seiko Epson Corporation
March 2000
Notes: I would like to propose using the Key Predistribution System, or KPS, to enhance WLAN security.

## Slide 2: Introduction
Problems of the current WEP
KPS
Implementation
SEC9H: MAC Chip with KPS
Patents
Conclusion
Notes: Before I make my proposal, I would like to briefly summarize the problems of the current standard.
I will also present a new MAC chip, the SEC9H, which we developed at Seiko Epson Corporation. SEC9H includes the KPS, which we are proposing today.

## Slide 3: Problems of the Current Standard
Not specified how to control keys
Difficult to exchange shared keys
Secret data is stored in MIB, which is accessible by external users
Difficult to authenticate
Practically impossible to deliver unique keys to every STA pair in a system
Notes: Little is specified about the key control in the IEEE802.11 WEP standard.
802.11 WEP employs shared key cryptography. The sender and receiver must therefore exchange a shared key before they start to communicate. It is very difficult to safely exchange encryption keys between the parties.
Some secret information, such as the Default Key, often resides in a memory accessible from external buses. Once someone succeeds in accessing this, he can easily find out the encryption keys. This is a weak point of the system.
The current standard provides two methods for authentication. The Open System Method and the Shared Key Method. A shared key method is more secure. But, once the shared key, which is often stored in MIB, or Management Information Base, is stolen, the authentication can be broken. In a higher layer, one other method of authentication can be performed using public key cryptography. However, this generally requires complicated procedures.

## Slide 4: Default Key and Key Mapping
    Default Key System
    (MIB-aWEPDefaultKeys)
    Mapped Key System
    (MIB-aWEPKeyMappings)
Notes: In the current 802.11 standard there are two WEP options to select shared key(s). These are the Default Key System and the Mapped Key System.
In the Default Key System, all users share one default key, and in the Mapped Key System a unique key is assigned for each pair. .
In the Default Key System, if the Default Key is attacked, the attacker can eavesdrop on the communications of the whole system. In the Mapped Key System, even if one STA is attacked, communications between other STA pairs are still secure. So, the Mapped Key System would be ideal from the security viewpoint, ( From the security viewpoint, the Mapped Key System, that is each sender/receiver pair is mapped a unique key, is ideal.）
But the number of keys increases in proportion to the square of the number of STAs. When there are many STAs, it becomes very difficult to deliver and control the keys. It is practically impossible to handle many unique keys safely.

## Slide 5: Problems of the Current Standard
Not specified how to control keys
Difficult to exchange shared keys
Secret data is stored in MIB, which is accessible by external users
Difficult to authenticate
Practically impossible to deliver unique keys to every STA pair in a system
Key Distribution Problem
Notes: To summarize the problems of the current standard;
  Methods to control keys are not specified in the current standard.
  It is difficult to exchange shared keys for current WEP.
  Secret data is stored in MIB, which is accessible by external users.
  It is practically impossible to deliver unique keys to every STA pair when there are many STAs in a system.
All of these problems listed are the so called Key Distribution Problem. It is also very important to resolve the Key Distribution Problem, as well as to strengthen the cryptographies.
In order to resolve this problem, we propose KPS. KPS is not cryptography, but rather a method to distribute shared keys safely. KPS can generate and deliver unique shared keys for every sender/receiver pair without any contact between a pair before they start communication. It also saves the system administrator labor and trouble.
Induction of KPS to 802.11 standard is easy. It does not affect the implementation of current or future cryptography. Furthermore, authentication is performed by an inherent feature in the KPS.

## Slide 6: Basic Flow of the KPS Communications
KPS Center
System-ID
1. Setting a Private-ID
2. KPS Communications
Private-ID A
Public-ID A
(MAC Address A)
Public-ID B
(MAC Address B)
Private-ID B
Private-ID ｎ
Public-ID n
(MAC Address n)
(Procedure necessary only once)
Notes: This slide illustrates the basic flow of the WLAN system using KPS.
At first, each station is set a Private-ID issued by a KPS Center. The KPS Center generates the Private-IDs from each Public-IDs, which is a MAC address held by each station, by means of a certain operation between the Public-ID and a System-ID. The System-ID is a large matrix which consists of random numbers. The Private-ID will be stored in the embedded memory of each station. The embedded memory bus can be isolated from system buses to prevent access by attackers. This procedure must be performed only once, say, when it is manufactured.

## Slide 7: Basic Flow of the KPS Communications
1. Setting a Private-ID
2. KPS Communications
KAB＝KBA
Public-ID B
(MAC Address B)
KPS Center
System-ID
Private-ID A
Public-ID A
(MAC Address A)
Public-ID B
(MAC Address B)
Private-ID B
(Procedure necessary only once)
KPS Module
Private-ID A
KPS Module
Private-ID B
KAB
KBA
Receiver B
(MAC Address B)
Public-ID A
(MAC Address A)
Sender A
(MAC Address A)
(Generated Key is without connections)
Notes: The most important feature in KPS is that even between parties who have never met yet, they can start a ciphered communication with a shared key.
I would like to explain this process to start a ciphered communication in KPS.
At the start of first contact between A and B, sender A applies receiver’s Private-ID B, that is MAC Address B, to the KPS module to generate the shared key, KAB
Then, the receiver B input the sender’s Private-ID A to the KPS module to generate the shared key, KBA.
Finally, using these shared key, KAB and KBA they start their ciphered communications.
In this system both of the sender and receiver used only their party’s MAC-Address to generate a key. Nevertheless,, those generated keys are identical (and can be used as a shared key.)

## Slide 8: Principle behind KPS Communications
KAB = KBA
KAB ≠ KCA
for any of C; C ≠ B
KBA ≠ KCB
for any of C; C ≠ A
Notes: This slide illustrates the more detailed basic flow of the KPS.
The principle of KPS is hidden in the Private-IDs and KPS Algorithm. The KPS algorithm and the Private-IDs can be selected to generate shared keys between the receiver’s MAC address and the sender’s Private-ID, or sender’s MAC address and the receiver’s Private-ID. And it is also designed so that a user, whose Private-ID does not correspond to his or her MAC-Address, cannot generate a correct key. Needless to say, the algorithm is designed so that it is practically impossible to know the Private-IDs from the used information, such as Public-IDs and the generated keys. This slide shows a mathematical description, but please refer to the Appendix of document number 031 for more details.

## Slide 9: KPS Security (1)
HUB vs Switch
HUB
(MAC0)
NIC4
(MAC4)
NIC3
(MAC3)
NIC2
(MAC2)
NIC1
(MAC1)
Ethernet LAN (HUB)
NIC
:
Network Interface Card
NIC4
:
Network Interface Card
(
Attacker
)
:
Packet
(HUB
⇒
MAC1)
NIC3
(MAC3)
NIC2
(MAC2)
NIC1
(MAC1)
Switch
(MAC0)
NIC4
(MAC4)
Ethernet LAN (Switch)
Notes: The current WEP of IEEE802.11 MAC is designed to be as secure as a wired system. Now I would like to discuss how the KPS is secure in comparison with an ordinary wired Ethernet Local Area Network.
In an Ethernet LAN system a HUB does not filter packets, so every machine connected to the LAN system can monitor every packet. Packets will arrive at all NICs connected to a HUB. An attacker cannot eavesdrop unless he connects to the HUB. Yet once the attacker succeeds in connecting, he can eavesdrop on all packets.
Security can be greatly improved with a switching HUB. A switching HUB detects the MAC addresses of each NIC connected to the HUB and only sends packets to a particular NIC address. A packet addressed to NIC1 is not received by any other NICs, so it is much harder to attack.

## Slide 10: KPS Security (2)
WEP ｖｓ WEP + KPS
802.11WEP Only
802.11WEP + KPS
Notes: This slide illustrates the infrastructure BSS environment of a wireless LAN with one AP. When the WEP is off, everyone can eavesdrop within the range of the radio wave. When the WEP is on, an attacker needs to know the shared key. This is similar to an attacker being unable to connect to a HUB in a wired network. When an attacker knows the Default Key he can eavesdrop on any packet in the system.
In the WLAN with KPS, the KPS delivers a unique shared key to every sender/receiver’s pair. Therefore no receiver can receive packets not addressed to him. The KPS corresponds to the wired LAN with switching HUBs. Using the KPS, WLAN s are enhanced to be as secure as a wired system that includes switching HUBs

## Slide 11: Authentication
Masquerade
Notes: Authentication is easy because of the inherent characteristics of the KPS system.
This slide shows a case when an attacker C pretends that his MAC address is STA B
The generated shared keys will therefore be KAB and KCA. These two keys are not the same, so it is impossible for the attacker C to masquerade as someone else. The correct key KBA can only be generated by someone who has Private-ID B.
In the KPS system a successful communication means that both sender and receiver used the correct Private-IDs. A correct key can only be generated by the right combination of Public-ID and Private-ID. Therefore the establishment of a connection will lead directly to authentication. This is all that is required for authentication in the KPS system.

## Slide 12: Implementing KPS to 802.11 MAC
Parameters
  Public-ID: Apply the MAC address as it is. 48 bits length.
  System-ID: 1024 x 1024 x 40 bits.
  Conspiracy number 1024
  Private-ID size: 5 k bytes
  Shared key length: 40 bit (based on current standard)
MIB privacy group
  AKPS Invoked: 0: KPS is off (default) 1: KPS is on
Notes: Now I would like to speak briefly about the actual implementation of this proposal.
The implementation is so simple that few parameters need to be specified.
    As the Public-ID, the MAC Address is used as it is. Its length is 48 bits.
    The System-ID size is 1024 x 1024 x 40 bits. The conspiracy number is 1024, and the Private-ID size is then 5 k bytes.
    Based on the current IEEE802.11 WEP specification, we specified its length as 40 bits.
Only one item needs to be added in the MIB privacy group to specify that the KPS has been applied at the data transfer.

## Slide 13: KPS Module
KPS Algorithm
Private-ID
One-Way Schemes
RC4
PRNG
RC4
PRNG
Private-ID
KPS
Algorithm
One-Way
Scheme 1
One-Way
Scheme 2
40bit
×
×
×
×
×
×
×
40bit
40bit
40bit
40bit
40bit
40bit
40bit
1
0
1
1
0
0
1
・
・
・
・
XOR
10110
･････････････
10
Private-ID
(1024
×
40)
Input
(Effective-ID)
Output
1024
1024bit
RC4
PRNG
Public-ID(48bit)
Effective-ID(1024bit)
RC4 Key
RC4
PRNG
KPS Algorithm
Output
(40bit)
Fixed Data(Secret)
(40bit)
Default Key #0
(40bit)
Shared Key(40bit)
XOR
XOR
RC4 Key
Notes: The KPS module consists of a KPS Algorithm, two one-way schemes, that is the RC4 pseudo random noise generator, or PRNG, and Private ID. For the details of each block, please again refer to the document.
Among those blocks, the most important block I must mention is the Private-ID.
The Private-ID should be kept strictly secret. It should be stored in the safest place in each STA. Memories in which the Private-ID is stored should be physically isolated from external access. One can design the system to erase or write data to memory for the purpose of production, testing or after maintenance, but it should never be read other than by a KPS module. It should also be protected by a cryptographic mechanism in case the memory is read.

## Slide 14: Who should administrate the KPS Center
Private system: Each vendor can create System-IDs independently
Multi-vendor system:
  Idea 1: A public organization creates and strictly controls a System-ID. The public organization duplicates and ciphers the System-ID and delivers it with a KPS Center tool to vendors.
  Idea 2: A public organization creates and strictly controls a System-ID. It issues Private-IDs in response to demands from venders. The organization should inspect whether the demands are from the right vendors. We propose that 802.11 controls the KPS Center
Notes: A KPS Center knows every Private-ID, and so it must be controlled very strictly. KPS Centers are required to be robust against attack, and no one should be granted privileges.
In a private system, the system that cannot be accessed by any other systems, each vendor can create System-IDs independently.
For multi-vendor systems it is very important to control the KPS Center.
there are two ideas of how both conditions can be met at once.
Idea 1:
A public organization creates and strictly controls a System-ID. The public organization duplicates and ciphers the System-ID and delivers it with a KPS Center tool to vendors. The KPS Center tool deciphers the ciphered System-ID internally, and outputs Private-IDs corresponding to MAC addresses. It only works when the MAC addresses with a permitted vendor code are applied.
Idea 2;
A public organization creates and strictly controls a System-ID. It issues Private-IDs in response to demands from venders. The organization should inspect whether the demands are from the right vendors.
Idea 2 is more robust than idea 1, though the organization needs to do more.
One idea is to propose that the IEEE802.11 committee controls the KPS Center. We will give a presentation on the procedure in more detail on another occasion..
Seiko Epson Corporation can provide the System-ID generator tool and the KPS Center tool.

## Slide 15: SEC9H: MAC chip with KPS
SEC9H: MAC controller with KPS
GBT9: Hi-datarate BB processor
Evaluation board
Notes: Seiko Epson Corporation has developed a MAC chip with KPS, code named SEC9H. We can provide evaluation samples now.
This is a picture of SEC9H and its evaluation board. And this is a Base Band Processor developed by Seiko Epson Corporation. It has 802.11 compatible mode, in 1 and 2 Mbps, and a dedicated hi-speed mode of up to 12.7 Mbps.

## Slide 16: SEC9H: MAC controller with KPS
Target baseband processor
  HFA3860B (Intersil)
  GBT9 (Seiko Epson Corporation)
IEEE802.11b protocol compliant
Hi-data rate,
  5.5 M/11 Mbps with HFA3860B
  3.7 M/5.5 M / 7.3 M / 9.2 M / 11.0 M / 12.8 Mbps with GBT9
KPS: Automatic shared key generation
Dual host bus: ISA and PCMCIA
Low power consumption
Notes: This slide shows a brief spec of SEC9H. SEC9H supports 802.11b MAC standard. It supports up to 13Mbps. It supports a dual host bus, ISA and PCMCIA.

## Slide 17: About KPS
Inventor
  Prof. Tsutomu Matsumoto, Yokohama National University
  Prof. Hideki Imai, Tokyo University
Patents
  Japan:
  US:
      Patent Number 5,016,276 (May 14, 1991)
  Europe:
      Patent Number 0 277 247 (04．05. 1994)
Cipher Key Sharing Method
Patent Number: 1984390,
October 25, 1995
Owner of the patent: Advance Co., Ltd.
Notes: The KPS was invented by Professors Matsumoto and Imai. The patents have already been issued. Anyone can be a licensee of the patent owner, Advance Co, Ltd.

## Slide 18: Conclusion
Use KPS to enhance WLAN security. KPS solves the Key Distribution Problem.
Seiko Epson can provide evaluation chips and tools.
KPS Features:
  It distributes unique shared keys to every sender/receiver pairs without exchanging any secret data
  It performs authentication inherently, with no additional schemes
  It releases the system administrator from controlling encryption keys
  It does not require changing current security protocols to implement KPS
  It is easy to use and implement
Notes: Now for my conclusion, I propose to use the KPS to enhance WLAN security. KPS solves Key Distribution Problems, and enhances WLAN systems to be as secure as wired systems that include switching HUBs. Seiko Epson has developed a MAC controller with KPS. Seiko Epson can provide evaluation samples and KPS tools now.
KPS’s features are:
    The KPS distributes unique shared keys to every sender/receiver pair in a system, even without any prior contact.
    The KPS performs authentication inherently, with no additional schemes.
    It releases the system administrator from controlling encryption keys.
    It does not require changing current security protocols to implement the KPS.
    It is easy to use and implement.

## Slide 19: End
Robust
cryptography
KPS
Notes: We hope our simple and effective method will be adopted in the 802.11 standard to enhance WLAN security and widely used in in the WLAN market.
Thank you very much for your attention.