## Slide 1: HiperLAN type 2: A System with QoS Support
Jamshid Khun-Jush
Chairman ETSI Project BRAN
Ericsson, Nürnberg

## Slide 2: Agenda
Requirements
Application Scenarios
Protocol Architecture
  Convergence Layer
  DLC
  PHY
Security
Conclusions

## Slide 3: HIPERLAN/2 Requirements - 1
Support of IP transporting networks as well as ATM networks
Capable of supporting QoS based multimedia communications (802.1p, RSVP, ATM)
  Impact on the chosen medium access control (MAC) protocol
  An access point (or base station) based system
  But “Direct Mode” operation for peer-to-peer communications
Capable of offering access, switching and management functions within a large coverage area
Usage in indoor and outdoor environments
Capable of handling different interference and propagation situations

## Slide 4: HIPERLAN/2 Requirements - 2
Coverage of radio cell @ 25 Mb/s: 30-40 m in a typical office indoor environment, 150 m in a large open indoor or typical outdoor environment
  puts limit on the sensitivity of the modulation scheme to noise
Supporting asymmetrical traffic load fluctuating in up- and downlink and for different users
Scalable security
Low power consumption

## Slide 5: Wireless LAN Scenarios
SGSN
GGSN
IWU
Office
ISP
Home
GPRS/UMTS
Ethernet
Internet

## Slide 6: Wireless PAN Scenarios
PAN
Office
Home
Travel
EDGE
HIPERLAN/2
HIPERLAN/2
W-CDMA

## Slide 7: HiperLAN/2 Protocol Architechture
Standardization scope: air interface, service interfaces of the radio access system and the convergence layer functions

## Slide 8: Convergence Layer
Cell based
Packet based
ATM
Segmentation and re-assembly to / from 48 bytes packets
Priority mapping from IEEE 802.1p
Address mapping from IEEE 802
Multicast & broadcast handling
Flexible amount of QoS classes
PPP
Firewire
Ethernet
Multiple convergence layers
One single convergence layer active at a time
Mapping between higher layer connections/priorities and DLC connections/priorities
UMTS

## Slide 9: DLC: Medium Access Control - 1
TDMA/TDD with a fixed frame duration of 2 ms
3 transmission possibilities: AP to MT (Downlink), MT to AP (Uplink) and MT to MT (Direct Link)
Centralized scheduling (not specified)
  Air interface frame creation in the AP
  Resource allocation by the AP
  Resource requests from MTs
  Dynamic assignment of capacity in uplink and downlink - no fixed slot structure
  Could consider QoS and link adaptation modes
  Transmission of Data PDU and ARQ PDU without collisions

## Slide 10: DLC: Medium Access Control - 2
Random access scheme
  Association and resource request transmissions from MTs
  Random access in mobile stations: slotted ALOHA with exponential increase of contention window
  Processing random access in the AP: acknowledgements of random access in the next frame
Peer-to-peer and multicast support
Sector antenna support

## Slide 11: Basic MAC Frame Structure
A single sector system
A multiple sectors system

## Slide 12: Basic MAC Frame Logical Channels
BCCH (Broadcast Control CHannel)
  convey the necessary broadcast information concerning the whole radio cell e.g. Scrambler seed, Access point ID, Network ID, etc.
FCCH (Frame Control CHannel)
  convey information describing the structure of the MAC frame visible at the air interface (resource grant announcement)
RACH (Random Access CHannel)
  used by MTs in the uplink to send signalling data (resource request, association request) for DLC or RLC.
RFCH (Random access Feedback CHannel)
  informs the MTs that have used the RACH in the previous MAC frame about the result of their access attempts.

## Slide 13: DLC - Error Control
Selective repeat (SR) ARQ with partial bitmap
  retransmission efficiency as conventional SR
  Optimized overhead and delay of acknowledgements
Discarding capability
  efficient for real time applications
Short MAC frame (2 ms) allows re-transmission even for voice
Link Adaptation
  Code rate and modulation alphabet adaptive to current propagation and interference environments
  7 physical layer modes (modulation alphabet and code rate combinations)

## Slide 14: Link Adaptation
Link throughput versus C/I
  Link quality measurements (C/I) in access point and mobile terminal
  A channel with an rms delay spread 100 ns
  Selective-repeat ARQ,
  Mode with the highest throughput selected (ideal link adaptation)

## Slide 15: DLC - Radio Link Control
Connection handling
  Setup / release of DLC connections
  Peer-to-peer (ad-hoc)
  Multicast
Management functions
  Mobility
    Association / de-association
    Handover
    Location update
  Radio resource management
    Dynamic frequency selection
  Power management
    Sleep mode
    uplink and downlink power control
Security
  Authentication
  Encryption key distribution
  Alternative security negotiation

## Slide 16: Physical Layer
To a great extent aligned with 802.11a
  Carrier spacing: 20 MHz
  Coded OFDM (Orthogonal Frequency Division Multiplexing)
    Handles a large variety of delay spreads => No complex equalizer needed
    52 sub-carriers (48 for data, four for pilots)
    Guard intervals: 800 ns mandatory, 400 ns optional
    Symbol duration 4 s
    sub-carrier modulation: BPSK, QPSK, 16QAM, 64QAM (optional)
    FEC: A rate 1/2 convolutional mother code with constraint length 7, additional rates 3/4 and 9/16 by puncturing
    7 physical layer modes with bitrate (Mb/s) 6,9,12,18,27,36,54
Main difference to 802.11a: Preamble due to different multiple access

## Slide 17: Security Overview
Corporate
network
Authentication & encryption in public access
Authentication & encryption
Wired equivalency
Sufficient in business, residential and public access environments
Support negotiation of different security levels
Supports mobility (HO)
Low/moderate processing overhead
Exportable
Internet

## Slide 18: Security Features
Mobile identity protection
Link level encryption
  unicast, multicast, broadcast
  user data, signalling
  56 bit to 168 bit key encryption (DES)
Challenge/response based mutual authentication
  Optional pre-shared key or public key
Token based handover authentication
Diffie-Hellman exchange for key generation
Regular key refresh

## Slide 19: Conclusions
HIPERLAN/2 for Emerging Nomadic Computing
  User Security
    Encryption
    Authentication
  Mobile Datacom
    up to 54 Mbps
    Mobility
    Quality of Service
  Environments
    Office
    Public
    Home