## Slide 1
QoS Extensions to 802.11 MAC
Rajugopal Gubbi, Sharewave
Wim Diepstraten, Lucent Technologies
Jin-Meng Ho, AT&T

## Slide 2: History
  Several participants have generated proposals for QoS extensions to the 802.11 MAC standard
  In the interest of achieving a fast standard process
    We got together over the last month to see where we agree
    and to explore where and how we can compromise
  This presentation is the result of that joint effort

## Slide 3: Contents
Introduction
Context
Synergies
Channel Access Methods
  Access Mechanism (AT&T)
  Access Mechanism (ShareWave)
  Access Mechanism (Lucent)

## Slide 4: Introduction
What do we want to achieve
  Complete compatibility with the existing 802.11 devices
  Simple hooks in the MAC to enable QoS Extensions
    for suitable integration in a QoS system
    including IETF type of bandwidth reservation
  Scalable to Home and Enterprise networks

## Slide 5: Introduction
What is Covered
  Areas of commonality between three separate proposals
  Focus is on QoS extensions
  Access mechanisms under consideration
What is not Covered
  Security
    Both Privacy and Content Protection
    Security beyond 40-bit WEP
  Authentication
  IAPP: Multimedia-specific features will require inter-SG cooperation

## Slide 6: Context
  Streams are the unit for QoS guarantees.
    A stream is identified by Stream ID, which is unique in the context of originating station MAC address
    QoS parameters of each stream are known at all endpoints of stream and coordinator
  There is a coordination entity per BSS, but not necessarily with link to infrastructure (for AdHoc) and it can be collocated with the AP, PC and/or Portal
  Transmission Opportunities (TxOps) are granted to streams, but may be used, within defined time limits, for any available transmission under STA control

## Slide 7: Synergies
  Admission Control
    Priority Assignment
    Bandwidth allocation/reservation
    Guaranteed Latency Bounds
  Selectable Acknowledgement Types
  Dynamic Bandwidth Management
  Stream Synchronization Support
  Roaming and Connection Handling
  BSS Overlap Management
  FEC/Channel Protection
  Direct STA-to-STA Communication
  Reliable Multicast Streaming
  Dynamic Frequency Selection

## Slide 8: Admission Control
What is it
  Ability to control admission of streams to the network and to revoke stream admission or alter stream operation parameters due to network conditions
  Ability to assign different static priorities to different stream types at admission control
  Ability to allocate and reserve bandwidth as requested by a stream
  Ability to guarantee access latency within specified limits. The latency being defined as the delay from the time a frame arrives at the MAC of tx-device to the time it is delivered by the MAC of rx-device to its higher layer.

## Slide 9: Admission Control
Why is it needed
  To control the number of consumers of bandwidth in order to meet previously granted guarantees
  Priority assignment: Applications have different priority requirements for the streams they create
  To control BW allocation through negotiations at the time of stream admission. Dynamic changes to stream bandwidth is discussed in Dynamic Bw Mgmt
  To provide guaranteed bounds on latency as different streams have different latency tolerances

## Slide 10: Admission Control
What is proposed
  Device should be able to request a stream connection specifying the QoS parameters
  Coordinator must verify that the device is authorized to consume the stream
  Coordinator must be able to inform the requesting device of the QoS parameter values it can currently support. This enables negotiation between the coordinator and the requesting device.

## Slide 11: Admission Control
What is proposed (cntd)
  Coordinator should either admit or reject the request
    if the QoS of existing streams can be preserved
      if current stream priority can be supported
      if sufficient bandwidth is available
      if specified latency is achievable: can allow for multiple transmissions in a single Beacon interval
  Coordinator should be able to inform the requestor of decision

## Slide 12: Admission Control
What is proposed (cntd)
  Multiple priorities should be supported
    >=2 Isochronous priorities
    >=2 non-isochronous priorities (hi/med)
    Best effort (low, today’s 802.11 MSDU default)
  Stream admission requires exchange of one management frame (including priority, BW alloc and latency as parameters)

## Slide 13: Selectable Acknowledgement Types
What is it
  Ability to specify the ACK and Retry strategy based on the needs of the stream
Why is it needed
  Different streams have varying needs for ACKs and retries
    ACKs take time and require Tx-Rx turnarounds that reduce available throughput so should only be used when and as needed
    With some FEC and/or content protection codes an immediate ACK decision may be infeasible

## Slide 14: Selectable Acknowledgement Types
What is proposed
  Should be possible to negotiate re-transmission parameters between the tx and rx devices
  Rx device should be able to accumulate the retransmission requests and send as a combined response
    Within allowable time/buffer size bounds
  Tx device should be able to do selective re-transmission (as opposed to go-back-to-n)
  Negotiations must be part of stream admission control
  There should be a “DoNotAck” for use on frames which will not be retried by the sender
    May also be used on final retry attempts

## Slide 15: Stream Synchronization Support
What is it
  Ability for the receiving station to support synchronization of streams of different types (for example, audio and video)
Why is it needed
  Not all stream data are necessarily encoded within a single stream (i.e. gaming with voice-over)
  Useful for implementing time-to-live limits, buffer aging at intermediate relay entities, inter-BSS forwarding in ESS, etc.
  Higher layers do not take into account the latency of the WLAN access. So the MAC needs to provide hooks to compensate for that.
  Intended to provide timing support in the order of TU

## Slide 16: Stream Synchronization Support
What is proposed
  Each device must timestamp the outgoing stream
  Rx device must report the time information to higher layers to assist stream synchronization

## Slide 17: Dynamic Bandwidth Management
What is it
  Ability to accommodate VBR traffic without needing to reserve unused bandwidth
  To monitor bandwidth usage for stream
Why is it needed
  To allow streams to use unallocated or temporarily spare bandwidth as needed

## Slide 18: Dynamic Bandwidth Management
What is proposed
  Devices must periodically send out their bandwidth usage to the coordinator
  Coordinator must be able to respond to dynamic requests for bandwidth changes from devices
  Coordinator must be able to monitor bandwidth usage and renegotiate the unused bandwidth
  Coordinator must be able to renegotiate bandwidth from a lower priority stream to a higher priority stream

## Slide 19: Roaming and Connection Handling
What is it
  Ability to reassociate between BSSs in an ESS while maintaining QoS guarantee and established streams when moving to adjacent BSSs
    Acceptance of re-association contingent upon new BSS having sufficient bandwidth available to accept the new stream and its QoS limits
Why is it needed
  In order to allow QoS while roaming

## Slide 20: Roaming Connection and Handling
What is proposed
  Existing Re-association mechanism can be extended for smooth hand over while maintaining the QoS
  Beacons and Probe responses must contain an element for load indication
  Device must select coordinator for re-association based on the load indication and its own QoS requirement
  New Coordinator must obtain QoS parameters of the re-associating device from the old coordinator
  The coordinator must accept or reject re-association based on the requested QoS

## Slide 21: BSS Overlap Management
What is it
  Ability to accommodate overlapping BSSs on the same channel in a cooperative manner even when BSSs are not part of the same ESS and are not able to communicate directly via wireless or wired networks
Why is it needed
  Crowded environments (I.e. apartments) can easily exceed the number of distinct physical channels
  Also useful for installing and managing a full-coverage ESS in an enterprise environment

## Slide 22: BSS Overlap Management
What is proposed
  Devices must be able to send their measured channel statistics periodically to the coordinator
  BSSs should be able to detect the presence of another BSS or be informed by a STA in the area of overlap
  The BSSs should be able to negotiate their sharing of the bandwidth
  The overlapping BSSs should be able to conform to the negotiated portion of the shared bandwidth

## Slide 23: BSS Overlap Management
What is proposed (cont)
  The BSSs must be able to renegotiate QoS parameters of a stream to conform to new conditions using the already described DBM mechanism
  The sharing must be scalable to at least four overlapping BSSs
  Stations in area of overlap can relay shared info when the APs can not communicate directly

## Slide 24: FEC/Channel Protection
What is it
  Ability to detect and correct transmitted data in the presence of channel errors
Why is it needed
  Many stream type requirements require low BER (~1x10-8) in order to perform as users expect
  Additional study is being done to look at FEC gain in high interference and delay spread environments
  Additional study is being done for FEC for 802.11a PHYs

## Slide 25: FEC/Channel Protection
What is proposed
  The option of FEC is indicated by a capability bit
  Reed Solomon (255,239) code as base scheme for use with 802.11b PHY
  Rx device must be able to negotiate different code block lengths to improve the channel performance for each stream
  Tx and Rx device must be able to negotiate one from some number of defined FEC schemes for each stream using fixed code for first code block of MPDU

## Slide 26: Direct STA-to-STA Communication
What is it
  Ability for one STA to communicate directly with another STA in the same BSS without having to do so through an intermediary
    subject to stream admittance and bandwidth reservation/allocation limits
Why is it needed
  Bandwidth conservation in a bandwidth limited environment

## Slide 27: Direct STA-to-STA Communication
What is proposed
  Coordinator must be able to allocate bandwidth for Dynamic TDM-style transmission using the already described admission control and DBM mechanisms
  Device must be able to pre-negotiate bandwidth using the already described admission control and DBM mechanisms, and transmit frames in Dynamic TDM-style
  Rx device must be able to receive without necessarily ACKing immediately using the already described Selective Ack/re-tx mechanism

## Slide 28: Reliable Multicast Streaming
What is it
  Extend the existing multicast ability to include selective retransmission of frames by an arbitrary subset of STAs in the BSS
Why is it needed
  To enable selective, multicast distribution of media streams while maintaining QoS
    multicast conserves bandwidth versus doing separate bilateral transmission to each STA in the relevant subset of the BSS

## Slide 29: Reliable Multicast Streaming
What is proposed
  Devices must obtain permission from the coordinator to consume any stream in the BSS using the already described admission control mechanism
  Transmitting device must be able to collect retransmission requests from all the rx devices and appropriately retransmit. The request for retransmission and the retransmission process make use of the already described selective ack/re-tx mechanism

## Slide 30: Dynamic Frequency Selection
What is it
  Ability to choose dynamically the physical channel on which a single BSS should operate
Why is it needed
  To escape high severity in the current channel of operation
  To overcome overlapped BSS scenario to the extent possible
  This capability is required in the ETSI rules for the 5.2GHz band

## Slide 31: Dynamic Frequency Selection
What is proposed
  The coordinator must be able assess the channel condition using the channel statistics described in overlapped BSS management
  The coordinator must be able to achieve a short pause in BSS operation while looking for a better channel
  Coordinator must be able to inform all the devices in the BSS to change to the new channel

## Slide 32: Media Access Method Considerations
Collision Mitigation
  What mechanisms are used to avoid or minimize channel collisions
Channel Access Scheduling
  What mechanisms are used to schedule transmission opportunities & limit max TxOp to <2304 octets
Channel Efficiency
  What mechanisms are used to maintain a high efficiency in the use of the available channel bandwidth and allow practical sharing of channel with nearby BSSs if necessary

## Slide 33: Media Access Methods
AT&T MediaPlex
ShareWave WhiteCap
Lucent Blackburst

## Slide 34: MediaPlex QoS Extensions To 802.11 MAC
Jin-Meng Ho
AT&T Laboratories
180 Park Avenue
Florham Park, NJ 07932
(973) 236-6791
jinmengho@att.com

## Slide 35: Objectives
Guaranteed QoS service and efficient bandwidth utilization
Multimedia transfer (CBR, VBR, bursty,…)
Home and enterprise access and delivery
Simple extensions to base MAC
Fully backward compatible
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: Features
Virtual stream concept and QoS matching
Built on top of base PCF, DCF unaltered
Data access delay and channel throughput greatly improved over DCF and TDM
  Dynamic central scheduling--real time multidimensional coordination, BW best used
  Reduced contention under DCF--+++
  Contention needed only for reservation request --once per asynchronous data burst
  Contention centrally controlled--optimized
  Polling only if data available--small overhead
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: QoS Parameters
Acknowledgment Policy: Base, alternative, delayed, no acknowledgment
Flow Type: Continuous, Discontinuous
Priority Level: Orthogonal to Flow Type
FEC Code: No coding an allowable option
Privacy Choice
Delay Bound: Not always applicable
Jitter Bound: Not always applicable
Minimum Data Rate
Mean Data Rate: R
Maximum Data Burst: B
Max data size over T = R*T + B
Token bucket
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: Access Mechanisms
New control frames: CC, RR, Ext-Poll, Ext-Ack
New subfields of Duration/ID field : VSID (6), Size (4), Ack Policy(2)
Contention opportunities allocated for RR based on global demand
Collisions only with RR and resolved based on global history--optimized
Contention priority controlable for priority data access
Frame-by-frame scheduling: timely retries, reallocation of idle bandwidth
Multiframe-by-multiframe scheduling: STA-to-STA, batch transmissions
No or delayed acknowledgment: improves throughput & eases retries
Superframe (CFP repetition interval)
CI
B
SIFS
RR
CO
Dx = data frame sent by AP to STA x, Ux = data frame sent from STA x to AP, Sxy = data frame sent from STA x to STA y
TO = transmission opportunity, CC = contention control, CI = contention interval, CO = contention opportunity, RR = reservation request
CFP = contention free period (under PCF rules), CP = contention period (under DCF rules)
D1
+
Poll
U1
+
Ack
D2
U4
S4
RR
RR
RR
RR
CI
CP
Ext-
Poll
CFP
U1
Poll
CC
+
Ack
S13
Ack
+
Poll
CC
TO
TO
CF-
End
S28
S13
Ext-
Ack
Notes: <number>
<footer>
<header>
<date/time>

## Slide 39: Centralized Contention
* A centralized random access algorithm may be used to calculate the length of the next CI based on the contention outcome of the last CI and some other information.
* If the available bandwidth for the next contention is A and the calculated bandwidth is C, then pp = min(1, A/C).
* Contention Feedback contains the AIDs of STAs from which a RR frame was successfully received by the PC in the last CI.
Superframe
B
SIFS
CFP
CI
CO
RR
RR
CC
CC
RR
RR
CI
CP
B
CFP
CP
B
CC
+
Ack
CO
CI
RR
RR
RR
CFP
CP
CF-
End
Superframe
Superframe
Contention Control (CC) frame
Reservation Request (RR) frame
Notes: <number>
<footer>
<header>
<date/time>

## Slide 40: Centralized versus Distributed Contention
Fully distributed (without a PC):
  AP needs to contend, especially severe for asymmetric traffic loads.
  A large data burst needs to break down into a large number of MPDUs, each of which has to contend for transmission (resulting in lots of contentions if there are other data STAs sending data) and is likely to transmit beyond the TBT (bad for other time-bounded frames).
  Backoff for collision resolution is based on the contention outcome of the backoff STA itself, and is far from being optimal.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 41: Centralized versus Distributed Contention (Continued)
Partially distributed (with a PC):
  Contention and backoff under the DCF has the same shortcomings as noted above.
Centrally controlled:
  Any data burst needs to contend at most once to send a small RR frame, and its transmission is completely under the control of the PC (not getting impatient), with the contention never going beyond the TBT.
  Collision resolution is based on the contention outcome of all STAs and can be optimized.
  Significantly improved data access delay and channel throughput performance.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 42: Overlapping BSS Interference
Interference is asymmetric in W/LANs, especially so w.r.t. inter-BSS interference.
Transmission opportunities move from one STA to another-->Victims at t = t1 may not be victims at t = t2-->Inherent randomization for collision resolution.
Carrie sense reduces spatial reuse potential.
Statistical sharing at least gives a chance for high rate data transmission.
Deterministic partitioning may be good for low rate data, but gives no chance for high rate data.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 43: Interference Asymmetry
t = t1
Carrier sense unnecessarily inhibits the intended transmission when any STA in the green area is transmitting, or any other transmission from a STA in the green area during the intended transmission, especially so in a 3D environment.
OR
Changes of transmitters and/or receivers over time are similar to random backoff and provide some degree of inherent collision resolution. The asymmetric nature of interference allows for successful simultaneous transmissions.
t = t2
t = t2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 44: Virtual Streams
Served as “virtual pipes” to transport data with various QoS demands
  Defined by (VSID, VS origin address, VS destination address), VS destination group address allowed--> broadcast/multicast VSs
  Outgoing from a transmitting STA to a receiving STA or STAs
  Denoted as VDSs, VUSs, and VSSs if outgoing from a PC, from a non-PC STA to PC, from a non-PC STA to at least a non-PC STA, respectively
  Established session by session and attached with a QoS parameter set, except for the default VSs (VSID = 0)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 45: Application Session
Admission of VSs needed to connect the STAs that are to participate in the application
Frame classification to admitted VSs for transmission (non-classifiable frames directed to default VSs)
Activation of admitted VSs prior to bandwidth allocation to VSs by PC
Deactivation of activated Continuous VUSs/VSSs by non-PC STAs via piggybacking
Bandwidth allocation to activated VSs in accordance with the corresponding QoS parameter sets
Transmission to and receiving from VSs allocated bandwidth
Termination of admitted/activated VSs
Notes: <number>
<footer>
<header>
<date/time>

## Slide 46: Admission of Virtual Streams
Default VSs of associated STAs are always admitted.
End-to-end QoS reservation messages go through PC (STA-PC) or are sent to PC (STA-STA).
SME of PC extracts QoS parameters and identifies all VSs needed.
SME performs admission control or QoS renegotiations.
SME extracts frame classifiers for all admitted VSs.
SME provides the classification entity (above MAC SAP) with classifiers pertaining to the admitted VDSs and to be added to the classification table, if applicable.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 47: Admission of Virtual Streams (Continued)
SME provides the scheduling entity (below MAC SAP) with all admitted VSs and corresponding QoS parameter sets.
SME issues a primitive to MLME and causes a management frame, VS update, to be sent to each non-PC STA involved, if any.
  VS update contains a VS update code “addition”, a frame classifier pertaining to an admitted outgoing VUS/VSS of the addressed STA, and the corresponding QoS parameter set.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 48: Admission of Virtual Streams (Continued)
Each non-PC STA receiving such a management frame has its MLME provide the classifier to its classification entity, and the admitted VDS/VUS and the corresponding QoS parameter set to its scheduling entity, if any.
  Both PC and STA talk about the same VDS/VUS, essential for meeting QoS values.
The STA acknowledges receipt of the management frame.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 49: Update of Virtual Streams
The admission procedure is repeated for any QoS parameter changes (using update code “change”).
New QoS-based VSs may be dynamically admitted to an established application session if additional non-PC STAs participate in the application amid its session, as detected by the SME of the PC from the signaling “connection” messages reaching the PC. Part of the admission procedure is performed to the extent that reflects such dynamic additions.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 50: Frame Classification To Virtual Streams
A buffered MSDU is classified, based on the classification table maintained at the transmitting STA, to an outgoing admitted VS prior to its transmission.
  A classification table is a collection of classifiers provided by the SME of the PC
  A classifier is comprised of: VSID, VS Origin Address, VS Destination Address, Search Priority, IP Classification Parameters, LLC Classification Parameters, and IEEE 802.1P/Q Parameters.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 51: Classification Parameters
The IP Classification Parameters may be zero or some of such parameters as IP TOS Range/Mask, IP Protocol, IP Source Address/Mask, IP Destination Address/Mask, TCP/UDP Source Port Start, TCP/UDP Source Port End, TCP/UDP Destination Port Start, and TCP/UCP Destination Port End.
The LLC Classification Parameters may be zero or some of such parameters as Source MAC Address, Destination MAC Address, and Ethertype/SAP.
The IEEE 802.1P/Q Parameters may be zero or some of such parameters as 802.1P Priority Range and 802.1Q VLAN ID
Notes: <number>
<footer>
<header>
<date/time>

## Slide 52: Activation of Virtual Streams
A frame classified to a newly admitted VDS activates the VDS with the PC until termination of the VDS.
A frame classified to a newly admitted Continuous VUS/VDS activates the VDS/VSS with the transmitting STA, which sends a RR frame to the PC to activate the Continuous VUS/VDS with the PC (activated until termination of the Continuous VUS/VSS).
Notes: <number>
<footer>
<header>
<date/time>

## Slide 53: Activation of Virtual Streams (Continued)
When and only when there are frames classified to a Discontinuous VUS/VSS for transmission is the Discontinuous VUS/VSS activated with the transmitting STA.
A non-PC STA with one or more Discontinuous VUS/VSS activated with the STA but not yet with the PC sends a RR frame to the PC to activate the one with the highest Priority Level.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 54: Activation of Virtual Streams (Continued)
A RR frame is sent to the PC by centralized contention or by preempting a transmission opportunity given to another outgoing VUS/VSS of the transmitting STA that is of a lower Priority Level than the VUS/VSS seeking to be activated with the PC.
A Discontinuous VUS/VSS activated with the PC becomes deactivated from the PC after its last classified frame is sent, with the More Data and More Fragments bits set to 0.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 55: Bandwidth Allocation To Virtual Streams
Transmission Opportunities (TOs) in terms of start and duration times are scheduled by the PC for VSs activated with the PC in accordance with the QoS parameter sets.
TOs for VUSs/VSSs are given by polling.
  Base Poll frame: as currently defined.
  Ext-Poll frame: for sequential transmissions.
Polled VUSs/VSSs may give their TOs to other outgoing VUSs/VSSs of the same transmitting STA.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 56: Transmission to and Receiving from Virtual Streams
TOs given to VSs act as weighted tokens for data frames classified to the VSs.
Such frames are sent within the TO limit.
Acknowledgment is performed according to the Ack Policy subfield of the frame, except in cases where piggybacked ack is possible and is always used.
Retry policy is tied to ack policy:
  Immediate retry for base ack
  Alternative retry for alternative ack
  Delayed retry for delayed ack
  No retry for no ack
Notes: <number>
<footer>
<header>
<date/time>

## Slide 57: Termination of Virtual Streams
Default VSs of associated STAs are not terminated.
SME of PC detects end-to-end QoS “disconnection” messages going through PC (STA-PC) or sent to PC (STA-STA).
SME identifies all affected VSs and the correspinding classifiers and QoS parameter sets.
SME provides classification entity (above MAC SAP) with classifiers pertaining to the de-admitted VDSs and to be deleted from the classification table, if applicable.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 58: Termination of Virtual Streams (Continued)
SME provides the scheduling entity (below MAC SAP) with all de-admitted VSs.
SME issues a primitive to MLME and causes a management frame, VS update, to be sent to each non-PC STA affected, if any.
  VS update contains a VS update code “deletion” and a frame classifier pertaining to the de-admitted outgoing VUS/VSS of the addressed STA and to be deleted from the classification table of the STA.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 59: Termination of Virtual Streams (Continued)
Each non-PC STA receiving such a management frame has its MLME provide the classifier to its classification entity, and the de-admitted VDS/VUS to its scheduling entity, if any.
  Both PC and STA talk about the same VDS/VUS, essential for meeting QoS values.
The STA acknowledges receipt of the management frame.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 60: Termination of Virtual Streams (Continued)
QoS-based VSs admitted for an application session may be dynamically terminated,
  if the end parties they support quit the application, as detected by the SME of the PC from the signaling “disconnection” messages reaching the PC,
  if the admitted VSs stay deactivated from the PC beyond a timeout threshold, as determined, and reported to the SME, by the scheduling entity of the PC,
  if the QoS requirements of the admitted VSS can no longer be adequately met due to unexpected bandwidth shortage, as also determined, and further reported to the SME, by the scheduling entity of the PC.
Part of the above de-admission procedure is performed to the extend that reflects such events.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 61
Dynamic TDM, non-polled Channel Access
Rajugopal Gubbi
Sharewave, Inc.

## Slide 62: Contents
Overview of the proposed channel access mechanism
Transmission hierarchy
Use of channel
Advantages of the proposed channel access mechanism

## Slide 63: Overview of the proposed channel access mechanism
PCF based mechanism
Enhancement to PCF for non-polled, direct transmissions by devices
Coordinator divides the CFP into tx-slots for each device and conveys them to the requesting devices
Devices transmit their data within their individual allocated time in the CFP
Devices communicate their last packet transmission in their tx-slot so that the next device in line for transmission can take advantage of any temporarily left over bandwidth

## Slide 64: Transmission Hierarchy

## Slide 65: Use of channel
Channel access times are negotiated/allocated during the stream admission using the Admission control as described in the synergy section
PC provides tx-list during Admission control negotiation
Device assesses its bandwidth requirement for the stream and sends it as part of channel statistics. Further changes to channel access times are negotiated/allocated using the DBM mechanism as described in the synergy section

## Slide 66: Use of channel (contd..)
Beacon from PC is used for time reference
Device starts transmission at the beginning of its allocated time. The device can start early if it detects the last frame tx from the previous device in the tx-list
Device marks the last frame transmitted and finishes at or before the end of its allocated time

## Slide 67: Advantages of the proposed channel access mechanism
Very low overhead
Bandwidth changes are demand based (quasi-static)
Use of temporarily unused bandwidth of one device by the next device in the tx-list and hence not requiring frequent bandwidth re-negotiations
Timer based, simple implementation is possible

## Slide 68: Lucent Blackburst
Channel Access Scheduling
Collision Mitigation
Channel Efficiency

## Slide 69: Lucent Proposal
Lucent proposes BlackBurst as a distributed access mechanism that can satisfy QoS needs.
Blackburst is an extension of the DCF procedure.
  And is able to do collision free contention resolution between QoS contenders, and the DCF traffic.
  And automatically resolves BSS overlap.

## Slide 70: Black Burst uses a DCF extension
Three interframe spacings, as in the IEEE 802.11 standard
  TSHORT - response packets (SIFS)
  TMED - real-time (RT) stations (PIFS)
  TLONG - data stations (DIFS)
Sensing capabilities, as in CSMA/CA
Ability of RT stations to send black bursts
Which is Preamble modulation during a BlackBurst Slot duration.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 71: Basic operation
RT station has an access instant
  Transmits for at least TPKT s.
  Schedules the next access instant to DMIN s. in the future
RT station has a scheduled access instant
  If channel has been idle for PIFS, it transmits
    Best option is to always start BlackBurst contention.
  Otherwise, waits until channel has been idle for PIFS and enters into black burst contention based on “Wait duration”.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 72: Black burst contention
Length of black burst is proportional to delay in accessing the channel
Access instants of distinct stations differ by at least TPKT black bursts differ by at least a black slot
Unique winner after a black burst contention period - the station that has been waiting the longest
The channel access instant timing is reset after every successful contention / resynchronization.
Conclusion:
  No collisions, because there is only one winner
Notes: <number>
<footer>
<header>
<date/time>

## Slide 73: Example of operation
Notes: <number>
<footer>
<header>
<date/time>

## Slide 74: Negative Acknowledgment
Upon reception of an RT packet, a receiver knows when to expect the next packet
  After a certain timeout the receiver can send a CTS to invite the transmitter to repeat its last RT packet.
    The CTS will have a “Duration” that is consistent with the allocated bandwidth for this connection.
  This allows for recovery from “Hidden Station” problems.
CTS is used as a negative acknowledgment indication
  Robustness against hidden stations (implied RTS scheme)
  Using existing CTS makes it compatible with the current DCF.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 75: Multiple priorities in BB
Extra listen interval introduced per subsequent priority level to assess priority.
  Extra overhead of 1 slot on highest priority.
  And additional 2 slots per subsequent priority level.
Can also be used to resolve contention with the PCF.
Issue: How many “Access Priority” levels would be needed if any.

## Slide 76: Properties
Compatible with IEEE 802.11 MAC
  It is an extension of the DCF.
RT traffic has priority over data traffic
  Using a distributed mechanism.
  Working across BSS boundaries.
RT stations access the channel in round-robin order within the same priority level
RT packets are NOT subject to collisions
Supports RT streams with different bandwidth requirements
  Allows Burst of frames separated by SIFS.
Robust against hidden stations
Notes: <number>
<footer>
<header>
<date/time>

## Slide 77: BSS overlap situations
2 dimensional BSS overlap using 4 channels
  Clearly an issue for enterprise networks
  But also for dense apartment buildings
  Probably less in residential home area’s
Assumption is that cells are dimensioned for 11 Mbps operation

## Slide 78: Overlap at 11 Mbps
In practice need to maintain an approx. 15 dB SIR
  Which translates in roughly a 3:1 distance ratio between Signal and co-channel interferer
  So locations outside the circles are vulnerable for interference from the other cell.
  While within the circle the bandwidth could be reused
    If it does not interfere with the other network

## Slide 79: Overlap BB versus PCF
A DCF needs to defer for traffic in a range where it can cause interference.
  Which requires a “Conservative” defer threshold
A PCF needs to avoid overlap between the PCF in each BSS
  By synchronizing the CFP periods, avoiding overlap.
    Traffic within the circles could overlap, with certain traffic in other BSS.
    But also DCF traffic from the other BSS can cause interference.
  Synchronization needed over a distance beyond the 11 Mbps range.

## Slide 80: Overlap issues BlackBurst
BlackBurst needs a “Conservative” Defer Threshold.
  To assure 1:3 SIR distance ratio.
  And resolve contention between BSS’s
  Which does reduce the reuse typically possible for DCF
This makes BlackBurst “sensitive” for the PHY implementation.
  Radio Tx to Rx turnaround time not specified separately in the PHY standard.
    Which requires a BB slot to be SIFS+Slot
    While implementations can do that within a Slot.
  And the CCA threshold specification is inadequate to assure a 1:3 SIR distance Ratio.

## Slide 81: Overlap issues in PCF
PCF must “learn” which stations are vulnerable for BSS overlap
  And protect that by forcing silence in the other BSS
    which reduces the BW budget for the other BSS
  So every time a connection is being established.
    The BSS’s need to “Learn” the overlap, and establish a different CFP synchronization.
  This mechanism should scale across more overlapping BSS’s

## Slide 82: BSS overlap Conclusion
Blackburst is a very useful extension to the DCF standard.
  Allowing a fast implementation.
  But is sensitive to PHY implementation
  And does probably require PHY changes
PCF systems need CFP overlap control between BSS’s
  By “Learning” the overlap situation
  And synchronize BSS’s beyond direct communication reach.
  This makes it a COMPLEX system.
  The ShareWave proposal does describe mechanisms
  But are these scaleable for multiple overlap situations?

## Slide 83: BlackBurst Conclusion
In the interest to come to a fast QoS standard
Lucent is prepared to drop the BlackBurst proposal
  If scaleable solution can be achieved for the BSS overlap management in a PCF.