## Slide 1: IEEE 802.1X For Wireless LANs
Bernard Aboba, Tim Moore, Microsoft
John Roese, Ravi Nalmati, Cabletron
Albert Young, 3Com
Carl Temme, Bill McFarland T-Span
David Halasz, Aironet
Paul Congdon, HP
Andrew Smith, Extreme Networks

## Slide 2: Outline
Deployment issues with 802.11
Adaptation of IEEE 802.1X to 802.11
Summary

## Slide 3: Deployment Issues With 802.11
User administration
  Integration with existing user administration tools required (RADIUS, LDAP-based directories)
    Create a Windows group for wireless
    Any user or machine who is a member of the group has wireless access
  Identification via User-Name easier to administer than MAC address identification
  Usage accounting and auditing desirable
Key management
  Static keys difficult to manage on clients, access points
  Proprietary key management solutions require separate user databases

## Slide 4: Security Issues With 802.11
No per-packet authentication
Vulnerability to disassociation attacks
No user identification and authentication
No central authentication, authorization, accounting
RC4 stream cipher vulnerable to known plaintext attack
Some implementations derive WEP keys from passwords
No support for extended authentication
  Token cards, certificates, smartcards, one-time passwords, biometrics, etc.
Key management issues
  Re-key of global keys
  No dynamic per-STA key management

## Slide 5: Advantages of IEEE 802.1X
Open standards based
  Leverages existing standards: EAP (RFC 2284), RADIUS (RFC 2138, 2139)
  Enables interoperable user identification, centralized authentication, key management
User-based identification
  Identification based on Network Access Identifier (RFC 2486) enables support for roaming access in public spaces (RFC 2607).
Dynamic key management
Centralized user administration
  Support for RADIUS (RFC 2138, 2139) enables centralized authentication, authorization and accounting
  RADIUS/EAP (draft-ietf-radius-ext-07.txt) enables encapsulation of EAP packets within RADIUS.

## Slide 6: Advantages of IEEE 802.1X, cont’d
Extensible authentication support
  EAP designed to allow additional authentication methods to be deployed with no changes to the access point or client NIC
  RFC 2284 includes support for password authentication (EAP-MD5), One-Time Passwords (OTP)
  Windows 2000 supports smartcard authentication (RFC 2716) and Security Dynamics

## Slide 7: 802.11 General Topology
Authenticator
(e.g. Access Point)
Supplicant
Enterprise Network
Semi-Public Network /
Enterprise Edge
AuthenticationServer
RADIUS
EAP Over Wireless (EAPOW)
EAP Over RADIUS
PAE
PAE

## Slide 8: IEEE 802.1X Conversation
Ethernet
Laptop computer
Switch
Radius Server
EAPOL-Start
EAP-Response/Identity
Radius-Access-Challenge
EAP-Response (credentials)
Access blocked
Port connect
Radius-Access-Accept
EAP-Request/Identity
EAP-Request
Access allowed
EAP-Success
Radius-Access-Request
Radius-Access-Request
RADIUS
EAPOL

## Slide 9: Goals for 802.1X on 802.11 Wireless LANs
Minimal changes required to 802.1X and 802.11 specifications
  802.1X protocol same over 802.3 as 802.11
Client access control
  Support for both user and machine access control
Centralized user administration
  RADIUS client support on Access Point
Management of encryption keys
  Transmission of global/multicast keys from access point to client
  Dynamic derivation of unicast keys
Roaming support
Ad-hoc networking support

## Slide 10: 802.11 association
Access point configured to allow open and shared authentication
Initial client authentication
  Open authentication used, since dynamically derived WEP key not yet available
Client associates with access point

## Slide 11: 802.1X authentication in 802.11
IEEE 802.1X authentication occurs after 802.11 association
  After association, client and access point have an Ethernet connection
  Prior to authentication, access point filters all non-EAPOL traffic from client
  If 802.1X authentication succeeds, access point removes the filter
802.1X messages sent to destination MAC address
  Client, Access Point MAC addresses known after 802.11 association
    No need to use 802.1X multicast MAC address in EAP-Start, EAP-Request/Identity messages
  Prior to 802.1X authentication, access point only accepts packets with source = Client and Ethertype = EAPOL

## Slide 12: 802.11/802.1X State Machine

## Slide 13: 802.1X and Per-STA Session Keys
How can EAPOL be used to derive per-Station unicast session keys?
  Can use any EAP method supporting secure dynamic key derivation
    EAP-TLS (RFC 2716)
    EAP-GSS
    Security Dynamics
    Other
  Keys derived on client and the RADIUS server
  RADIUS server transmits key to access point
    RADIUS attribute encrypted on a hop-by-hop basis using shared secret shared by RADIUS client and server
  Unicast keys can be used to encrypt subsequent traffic, including EAPOW-key packet (for carrying multicast/global keys)
Per-Station unicast session keys not required
  If only multicast/global keys are supported, then session key is only used to encrypt the multicast/global key

## Slide 14: 802.1X and Multicast/Global Keys
How can EAPOL transfer multicast/global keys?
  A new EAPOL packet type can be defined for use in transporting multicast/global keys: EAPOW-Key
  EAPOW-Key packet type used to transmit one or more keys from access point to client
  EAPOW-Key packets only sent after EAPOW authentication succeeds
  EAPOW-Key packets are encrypted using derived per-STA session key

## Slide 15: 802.1X On 802.11
Ethernet
Access Point
Radius Server
EAPOL-Start
EAP-Response/Identity
Radius-Access-Challenge
EAP-Response (credentials)
Access blocked
Association
Radius-Access-Accept
EAP-Request/Identity
EAP-Request
Radius-Access-Request
Radius-Access-Request
RADIUS
EAPOW
Laptop computer
Wireless
802.11
802.11 Associate
EAP-Success
Access allowed
EAPW-Key (WEP)

## Slide 16: Re-authentication
Access points are allowed to force clients to re-associate at any time
  Default is 60 minutes
  The client responses transparently to the user
Access point sends WEP global key to client using 802.lX
  EAPOW-Key message used to send global key

## Slide 17: Roaming
Process (no pre-authentication)
  802.11 Re-association
  802.1X will re-authenticate but network access will be denied during re-authentication
Optional support for fast handoff
  Inter-access point protocol
    Handoff per client keys
    Use EAPOW-Key to update shared key
  Shared key pre-authentication
    Shared authentication using global WEP key
    If succeeds then allow immediate access to network
      i.e. 802.1X is put immediately into the authenticated state

## Slide 18: “Unauthenticated” VLAN Support
Potential extension to IEEE 802.1X
Designed to enable access to a registration server, enrollment server, etc. prior to authentication
EAP-Notification message can inform user of location of server to take credit card, enroll user, etc. prior to obtaining network access.

## Slide 19: 802.1X and Ad-Hoc Networking
What is ad-hoc networking?
  Station communicating directly with other stations
How does ad-hoc networking work with 802.lX?
  Both Stations initiate EAPOL conversation
  All stations authenticate with each other
    Otherwise mutual authentication required and algorithm to select authenticator
  RADIUS not used in ad-hoc mode
    Typically implies that user credentials are stored on Stations

## Slide 20: Key Management for Ad-Hoc Networking
Requirements
  Password-based mutual authentication
  Secure key generation
Evaluation of existing EAP methods
  EAP-TLS: supports mutual authentication, keying, but assumes both participants have a certificate
  EAP-GSS: supports mutual authentication, assumes “server” side is in contact with KDC
802.1X will work in adhoc mode if required
  Shared key is better for some user scenarios
  May need new EAP method for this purpose

## Slide 21: How 802.1X Addresses 802.11 Security Issues
User Identification & Strong authentication
Dynamic key derivation
Mutual authentication
Per-packet authentication
Dictionary attack precautions

## Slide 22: Summary of 802.11/802.1X Vulnerabilities

## Slide 23: Summary
IEEE 802.1X offers solutions to 802.11 deployment issues
  User identification
  Centralized user management
  Key management
Minimal changes required to 802.11 specification
  Additional MIB parameters for 802.1X/802.11 configuration
Implementation requirements
  Support for dynamically derived WEP keys + mutual authentication
  Support for ad-hoc networking
  Access-Point functions as RADIUS client
    Requires support for RFC 2138, 2139, draft-ietf-radius-ext-07.txt
  Access-Point functions as IEEE 802.1X authenticator PAE
Addresses most WEP security vulnerabilities

## Slide 24: Call to Action
802.1X
  Add changes required for 802.11
    Messages sent to destination MAC address for 802.11
    Add EAPOW-Key message
802.11
  Adopt 802.1X as an enhanced authentication and key management method
  Enable appropriate methods supported by 802.1X to be used for 802.11 authentication and key management
  MAC changes to improve encryption, integrity protection
  The IAPP work needs to consider security impact re STA mobility between APs.

## Slide 25: For More Information
IEEE 802.1X
  http://grouper.ieee.org/groups/802/1/pages/802.1x.html
RADIUS
  http://www.ietf.org/rfc/rfc2138.txt
  http://www.ietf.org/rfc/rfc2139.txt
  http://www.ietf.org/rfc/rfc2548.txt
  http://www.ietf.org/internet-drafts/draft-ietf-radius-radius-v2-06.txt
  http://www.ietf.org/internet-drafts/draft-ietf-radius-accounting-v2-05.txt
  http://www.ietf.org/internet-drafts/draft-ietf-radius-ext-07.txt
  http://www.ietf.org/internet-drafts/draft-ietf-radius-tunnel-auth-09.txt
  http://www.ietf.org/internet-drafts/draft-ietf-radius-tunnel-acct-05.txt
EAP
  http://www.ietf.org/rfc/rfc2284.txt
  http://www.ietf.org/rfc/rfc2716.txt

## Slide 26: Simplified Insecure Adhoc Support
Simple, insecure adhoc networking sometimes desirable
  Children playing games
  Need “plug and go” solution without security complications
  Not appropriate in business situations
How can this be handled with 802.1X?
  Clients assume network is un-authenticated
    An authenticated network will drop packets
  Clients drop received EAP-Start messages
    Clients think they are connected to a non-authenticated network
    Adhoc networking just works.

## Slide 27: Why Not Incorporate 802.1X into 802.11 authentication?
Possible to add 802.1X support in 802.11 authentication phase
  Requires additional authentication type for EAP
  Requires additional of new key management functionality in 802.11
Likely to result in duplication of effort
  Supplicants supporting 802.1X need duplicate code for 802.11 EAP
  Supplicant operating system sees 802.11 as 802.3
    Requires encapsulation/decapsulation in NIC driver to maintain transparency
Large changes required to 802.11 state machine
  802.1X state machine needs to be merged with 802.11 state machine
No additional security over 802.1X over 802.11 approach
  Associate/disassociate not encrypted or integrity protected so no additional security provided by doing EAP w/key derivation prior to 802.11 Associate
Un-authenticated VLANs cannot be supported
  Choice either authenticated or unauthenticated