## Slide 1: Wireless LAN QoS
Duncan Kitchin
Intel Wireless LAN Operation

## Slide 2: Requirements
Must have end-to-end signalling
  quality of service setup has to include whole network, not just the wireless LAN segment
  must interoperate with all existing networks
Must have application support
  has to work with existing protocol stack & applications
  QoS features in wireless LAN must be transparent - application should not know or care what the underlying transport is

## Slide 3: Proposed Solution
MAC provides statistical prioritization based on 802.1p tags
Real time connection setup handled at higher layers
  RSVP in the network layer for end-to-end signalling
  Subnet bandwidth management (SBM) uses RSVP state to attach 802.1p tags to packets

## Slide 4: End to end signalling
PHY
MAC
PHY
MAC
PHY
MAC
PHY
MAC
NWK
NWK
NWK
MAC layer doesn’t have the end to end picture
Lowest layer that can have end to end signalling is the network
Connections are established at network layer, with requirements pushed downwards into the MAC using SBM
NWK
Connection Setup

## Slide 5: Summary
Simple, incremental extension to 802.11
Works with existing protocol stack (TCP/IP)
Well defined IETF protocol (RSVP) allows access to QoS services transparently, ensures application support