## Slide 1: Proposal for Enhanced Encryption
Duncan Kitchin
Jesse Walker
Intel Network Infrastructure Division

## Slide 2: Purpose of This Proposal
40-bit RC4 (WEP) is rapidly becoming inadequate
A simple extension can be made (included in this proposal) to extend WEP to 104 bits
This solution will also become inadequate at some point
This proposal presents a long range solution (starting ~2 years out)

## Slide 3: Backwards Compatibility
Want to avoid an unstructured option space, forcing everybody to implement many options
Propose ordered list of encapsulations
  each is stronger than the one before it in the list
Limit the number of algorithms

## Slide 4: Proposed Encryption Algorithms

## Slide 5: Choice of AES
Replacement for DES
  algorithm not yet selected
  will be one of Rijndael, Serpent or Twofish
Will be 128 bit block cipher, supporting key lengths of 128, 196 and 256 bits

## Slide 6: Proposed Frame Formats
WEP-104 will be identical to WEP-40
Use of 104 rather than 40 bit RC4 by mutual agreement of pair of stations
Remaining formats use new “AES” data frame subtype

## Slide 7: AES Frame Format
IV
Sequence
Number
Payload
Pad
HMAC-SHA-1
Defeat interleaving attacks
Defeat replay attacks
Defeat eavesdropping

## Slide 8: Summary
Encryption algorithms should form an ordered list, each implementation required to support a contiguous range
Propose WEP-104 & AES algorithm list
Propose format for AES as described