## Slide 1
Tutorial on Achieving End-to-end QoS
Rajugopal Gubbi
Sharewave, Inc.

## Slide 2: End-to-end QoS
What is it
  Ability to preserve QoS semantics explicitly carried by a stream from/to the outside connection to/from any device in the BSS
Why is it needed
  In order to guarantee the QoS needs of a stream without having to guess at what those needs are
  In order to be able to analyze/pass the QoS request from wired connections between STAs

## Slide 3: End-to-end QoS
What is the Scenario
(Example-A, Home/Enterprise environment)
Gateway
A
H.323 Video Conferencing Unit
C
Kitchen WEB browser panel
D
Personal computer
B
Outside connections like,
DSL and Cable modem
Negotiate QoS
within 802.11WLAN

## Slide 4: End-to-end QoS
What is the Scenario
(Example-B, SoHo and Enterprise environment)
Gateway
A
H.323 Video Conferencing Unit
C
Portal
D
Personal computer
B
Outside connections like,
DSL and Cable modem
Outside connections another
set of wired devices
Negotiate Qos within 802.11WLAN
and pass the requirements further

## Slide 5: End-to-end QoS
How it can be achieved
  Device analyzes and converts the semantics of an outside QoS connection into similar semantics on the 802.11-WLAN
  Device negotiates the 802.11- WLAN QoS based on requests from an outside connection using the already discussed mechanism within 802.11-WLAN
  Device reject an outside connection or renegotiate the Qos, if the requested QoS cannot be achieved on 802.11-WLAN
  Device passes on the QoS requests from an outside connection through the 802.11-WLAN to the rx device for further analysis

## Slide 6: End-to-end QoS
RSVP type of Layer-3 messages for QoS
  Application to 802.11-MAC (at Layer-3) must handle the RSVP type of bandwidth requests and inform the MAC through an interface. 802.11-MAC must not handle/alter RSVP type of Layer-3 messages.
  The MAC must use the mechanism in our proposal to control the bandwidth usage and achieve QoS
  if the MAC can not achieve the required QoS, it should inform the application and also signal the achievable QoS.

## Slide 7: End-to-end QoS
RSVP type of Layer-3 messages for QoS (cntd..)
  The application must either disconnect the stream or generate RSVP response type of Layer-3 messages to inform the peer application.
  This retains the advantages of layering as defined and mandated by 802
  Ideally QoS Interfaces between the Layer-3 and MAC must be made generic so that similar QoS can be achieved on all QoS-aware MACs