## Slide 1
Tutorial on Achieving End-to-end QoS
Rajugopal Gubbi
Sharewave, Inc.

## Slide 2: Outline of presentation
Definition
How it can be achieved
Example Scenario-1 (RSVP)
  Layers and their functions
  Layers as in Windows
  Summary of negotiation process
Example Scenario-2

## Slide 3: Definition
What is it
  Ability to preserve QoS semantics explicitly as carried by a stream from/to the outside connection to/from any device in the BSS
Why is it needed
  In order to guarantee the QoS needs of a stream without having to guess at what those needs are
  In order to be able to analyze/pass the QoS request from wired connections between STAs

## Slide 4: How it can be achieved
  Device analyzes and converts the semantics of an outside QoS connection into similar semantics on the 802.11-WLAN
  Device negotiates the QoS over 802.11-WLAN based on requests from an outside connection using the already discussed mechanism within 802.11-WLAN
  Device reject the outside connection (or renegotiates the Qos) if the requested QoS cannot be achieved on 802.11-WLAN
  Device passes on the QoS requests from an outside connection through the 802.11-WLAN to the rx device for further analysis

## Slide 5: Example Scenario-1
Gateway
A
H.323 Video Conferencing Unit
C
Kitchen WEB browser panel
D
Personal computer
B
Outside connections like,
DSL and Cable modem
Negotiate QoS
within 802.11WLAN
RSVP request

## Slide 6: Layers and their functions (RSVP - send host)
QoS aware 802.11 enhanced MAC with Admission control and DBM
Layer-3, handling RSVP
QoS semantics conversion (Interface between Layer-3 and MAC)
Receives requests from QoS semantics conversion layer
Receives RSVP (rsv-req) packet
Analyzes the RSVP packet and
Calls the QoS Symantics conversion interface with the request for MAC
Receives requests from Layer-3
Converts the request into MAC interfaces
Calls the MAC with the request
Responds back to QoS semantics conversion layer
Receives Response from QoS semantics conversion interface
Sends out RSVP (rsv-ack or error) packet
Starts using the service for the stream, if admission is allowed
Receives response from MAC
Converts the response into semantics of Layer-3 interface
Calls Layer-3 interface with the response
Conducts admission control/DBM process

## Slide 7: Layers and their functions (RSVP - Recv host)
QoS aware 802.11 enhanced MAC with Admission control and DBM
Layer-3, handling RSVP
Semantics conversion (Interface between Layer-3 and MAC)
Receives requests from QoS semantics conversion layer
Send RSVP (rsv-req) packet
Receive RSVP (rsv-req-ack)
Calls the QoS Semantics conversion interface with the request for MAC
Receives requests from Layer-3
Converts the request into MAC interfaces
Calls the MAC with the request
Responds back to Semantics conversion layer
Receives Response from Semantics conversion interface
Sends out RSVP (rsv-error) packet if not admitted OR
Starts using the service for the stream, if admitted
Receives response from MAC
Converts the response into Layer-3 interfaces
Calls Layer-3 interface with the response
Conducts admission control/DBM process

## Slide 8: Layering - As applicable to s/w stack in windows
QoS aware 802.11 enhanced MAC with Admission control and DBM
Protocol drivers (including RSVP handling)
Semantics conversion (NDIS wrapper)
NDIS interfaces
to MAC
(a) Ideal Situation
QoS aware 802.11 enhanced MAC with Admission control and DBM
Semantics conversion (Interface between Layer-3 and MAC)
NDIS interfaces
(b) One currently possible implementation
NDIS interfaces
to protocol driver
Protocol drivers (including RSVP handling)

## Slide 9: Summary of overall negotiation process
  Gateway (Device A) receives an RSVP packet from an outside connection
  The Layer-3 at device A requests layer-2 (802.11-MAC) for the stream specifying the required QoS using the interfaces described earlier (e.g. NDIS interfaces)
  The 802.11-MAC at device A requests a tx-stream initiation using the admission control mechanism
  PC of the BSS accepts or rejects the stream
  802.11-MAC at Device A (and C) conveys the received decision to the layer-3 using the interfaces described earlier (e.g. NDIS interfaces)
  Device C starts using the stream service in the BSS

## Slide 10: Example Scenario-2
  Negotiate WLAN-QoS when RSVP-rsv-req is received from a wired connection
  Disconnect the stream and release the bandwidth when RSVP-error or tear-down message is received
Gateway
A
H.323 Video Conferencing Unit
C
D
Personal computer
B
Outside connections like,
DSL and Cable modem
Outside connections another
set of wired devices
Negotiate Qos within 802.11WLAN
and pass the requirements further