## Slide 1: IEEE 802.11 Quality of Service
Arun Ayyagari, Yoram Bernet, Tim Moore
Microsoft Corporation
aruna@microsoft.com, yoramb@microsoft.com, timmoore@microsoft.com

## Slide 2: Overview
QoS guarantees for real-time application data traffic is currently not available in IEEE 802.11
Bandwidth guarantees at MAC level is not required
Propose using prioritised data with resource based admission control as the means to provide QoS guarantee for IEEE 802.11

## Slide 3: 802.1p
802.1p supports prioritization of traffic on Ethernet
    Ethernet tag containing 0-7 levels of priority
    Requires queues at points of congestion
    Number of queues is implementation dependent
Guarantee bandwidth by using admission control to limit traffic sent on each priority level
  IETF defines how to use SBM with 802.1p

## Slide 4: Resource Based Admission
Subnet bandwidth manager does admission control so priority levels not overrun
  SBM extends RSVP to level 2 networks
  Designated SBM (DSBM) acts as the admission control agent
    Should be located at the point that knows most about the resources available
Resource reservation protocol (RSVP) signalling goes end-to-end in case any part of the network is interested.
SBM and 802.11
  DSBM functionality should be co-located with the Access Point for optimal admission control
Roaming
  Renewal of request every 30 seconds
    Client allowed to send a renewal if it believes it is required
      E.g. Re-association
  Roam to an access point with no resources left
    Renew of request fails
    Priority of requests supported

## Slide 5: 802.1p and 802.11
Access point should support 802.1p
  Sending onto the wire
  Sending onto the wireless
Clients should support 802.1p
  Modify DCF method
  Modify the minimum and maximum values of the Contention Window parameter to ensure that higher priority frames have statistically a greater probability of transmission over lower priority frames.

## Slide 6: Ad-hoc
802.1p priority works station to station
Each station needs to implement admission control for the wireless interface