## Slide 1: Polling-based PCF for Strong QoS Guarantees
Jim Mollenauer
Technical Strategy Associates
and Enrichnet Inc.
Zvi Ganz and Bob Pisacane
Enrichnet Inc.
IEEE 802.11e
May 2000

## Slide 2: A Polling Proposal for QoS
Goals
Compatibility with existing equipment
Mechanism for dynamic bandwidth management
Efficiency
Experience with Ethernet and home phoneline
Software/firmware implementation
Dealing with hidden stations
Fail-safe
Packet classification issues

## Slide 3: Goals of the Proposal
Strong QoS
  Deterministic mechanism, not statistical
  Stations don’t transmit until polled
Better efficiency
  No bandwidth loss or delays due to collisions
    Ethernet is 91% efficient in theory, 50% in practice
Enhanced reliability
  Mechanism to address hidden-station problem
Compatibility with existing equipment
  Non-QoS equipment operates as before

## Slide 4: Backward Compatibility
Existing 802.11 stations continue to function on best-efforts basis
  All units respect PCF interval even if they don’t use it
  DCF for remainder of the time
    Non-QoS, lowest priority
Software can be added to provide QoS for existing stations
New devices can implement at software or firmware/hardware level

## Slide 5: Dynamic Bandwidth Management
Point Coordination Function (PCF) is best way to provide strong QoS
Coordinator sets PC interval, then polls stations, specifying xmit time
  Transmit only when polled
  No collisions (except during registration)
Adaptive algorithm to set transmit interval and duration
  Interval varies depending on recent history of station
  Excess polling avoided
  No statistical (weak) QoS based on priority
    Chance arrival of large amounts of high priority traffic causes problems in collision-based systems

## Slide 6: Adaptive Polling
Polling specifies station’s transmission period based on:
  Explicit QoS requests
    Constant bit rate
    Variable bit rate, with minimum / maximum
  Classification heuristics
Station need not report its own usage
If full period is not used, next station may start early
In this case, polling frequency may be cut
  Alternatively, if all is used, allocations may be increased
Policy is not strictly an interoperability issue
  But other stations must be ready to pick up coordinator function

## Slide 7: Time Line
PCF-based, contention-free
DCF-based, contention period
BCN
Poll
A
B
D
E
F
Coordinator polls A, B, C, D, and E
A, B, D, and E send data
C has no data, so D starts early
F registers in DCF contention time
G has best-efforts data, uses DCF
G
coordinator
users

## Slide 8: Polling Efficiency
Efficiency of polling is much higher than collision-based systems
  Real-life Ethernet systems have low useful throughput
    Calculated asymptotic throughput for 802.3 is 91%, even better than “classical” CSMA/CD at 83%
  But…delays get long
    Shorter backoff for new entrants causes instability
  In real life, Ethernet is seldom run above 50% average load
Arguments against polling:
  Need to choose coordinator to do polling
  Need to provide for failure of coordinator
  Everyone needs to hear poll
  Overhead of polls
Solutions:
  Coordinator chosen from MAC address or manually designated
  All pollable stations contain coordinator code
  Super-poll reaches all stations
  Poll is ~20 bytes vs. average transmission of 500 bytes (inc. ACKs)
  Adaptive polling reduces excess polls

## Slide 9: Demonstrated Capability
EnrichNet protocol has been demonstrated over several network types:
    10base T Ethernet
    Home phone line networks
    802.11 DCF
Result is as desired:
  Video runs smoothly in the presence of large file transfers
    Unusable without EnrichNet layer

## Slide 10: Implementation
A traffic cop, saying who can go when
Can be implemented as a software shim layer
  Intercepts transmission calls
    Like remote file system intercepting disk calls
  In this case, independent of PHY or original MAC
    Wireless, twisted pair, fiber, power lines
  OS delays, but some compensation possible
    Start transmission early by amount of best-case OS delay
Embedded implementation: faster response possible
  In ASIC, but again above normal (DCF) MAC
  Or in control microprocessor

## Slide 11: Software Implementation
APPLICATION
OPERATING
SYSTEM
LAYER 3 AND 4
LAN QOS SOFTWARE
DRIVER
NIC CARD

## Slide 12: Hardware/Firmware Implementation
APPLICATION
OPERATING
SYSTEM
LAYER 3 AND 4
DRIVER
NIC CARD
MAC
QOS COORD/CLIENT
LAN NIC CARD
}

## Slide 13: Super-Poll Option
Attacking the hidden-station problem
Each station appends remaining polls to its transmission
If D is the coordinator, A is blocked by terrain and cannot hear polls
A hears poll from B, can transmit to B or C
A can’t transmit directly to D, E, or F, nor B to E and F
  We can’t repeal the laws of physics!
  Relay via B or C could be an option
HILL
A
B
C
D (coordinator)
F
E

## Slide 14: Super-Poll Structure
Header
A
B
C
A
F
G
D
E
Polling list: station address, transmit interval
Header
Data
B
C
A
F
G
D
E
Header
Data
C
A
F
G
D
E
Header
Data
A
F
G
D
E
Remaining polling list
Coordinator sends:
A sends:
B sends:
C sends:
Stations Respond:
Remaining polling list
Remaining polling list
Etc.

## Slide 15: Fairness
Stations later in list have more chances to receive the poll
Therefore coordinator varies the list from one poll to the next
  Random, or
  Cyclic: A,B,C,D then D,A,B,C…C,D,A,B…etc
When a station repeats the poll, it removes itself and repeats the list in the same order as received
Average probability of receiving poll is the same for all stations with the same traffic class
But if coordinator recognizes that some stations are in hard-to-reach locations, it puts them late in the list to increase the probability of poll being received

## Slide 16: Improving the Polling Process
With Super-Poll, probability of not receiving a poll goes down dramatically
Simulation shown for various group sizes and values of the probability P, the probability that a single poll is not received due to noise
References
A. Ganz, A. Phonphoem, Z. Ganz, "Robust SuperPoll with Chaining Protocol for IEEE 802.11 Wireless LANs in support of Multimedia Applications", Wireless Networks Journal, to appear in 2000.
A. Ganz, A. Phonphoem, Z. Ganz, ``Robust SuperPoll Protocol for IEEE802-11 Wireless LANs, IEEE Military Communications Conference, October 1998.

## Slide 17: Net Efficiency Improvement
Channel utilization U = user transmission time / total time
  If poll is not received, channel is idle and utilization suffers
Efficiency gain E = (Usuper-poll -U single poll)/Usingle poll
E as a function of G, the group size, for various values of P:

## Slide 18: Overlapping BSS
Stations may be in range of either or both BSS
Need to avoid interference, allow both systems to operate

## Slide 19: Full Overlap
All stations are in range of both coordinators
Behaves like single network
  One coordinator is chosen
  All stations work with this coordinator

## Slide 20: Partial Overlap
The more general case
Some stations hear both coordinators, some hear only one
Solution: one coordinator takes over fully
  Other coordinator relinquishes, sends registration list to first
  Super-poll mechanism polls all stations from one coordinator

## Slide 21: Fail-Safe
All QoS-enabled stations have coordinator code
Activated only in current coordinator
On failure of coordinator, another station takes on the role
  Hardware failure
  Communication failure
    Blockage by obstacles
    Persistent interference
    Out of range

## Slide 22: Packet Classification
An important topic but...
    Not our issue
Classification is independent of allocation mechanism adopted to provide corresponding level of service
Adaptive polling can operate with explicit or implicit (heuristic) classification
Must be applied end-to-end
  Not just LAN
  Not just access network
  Not just backbone network
Compatibility with IETF efforts for WAN is very important
  Coordinator should have SBM (Subnet Bandwidth Mgr.) capability
  Much easier with PCF than otherwise