## Slide 1: Hierarchical Structure to Enhance WLAN Security
Yutaku Kuchiki, Masayuki Ikeda
Seiko Epson Corporation
May 2000
Notes: We proposed to use KPS, Key Predistribution System, to enhance MAC security in the last meeting. There were also a few other proposals to enhance WLAN security.

## Slide 2: Overview
Security Requirements
Key Distribution Problem and its solutions
Authentication in MAC
KPS Features
Proposal of a Hierarchical Structure to Enhance WLAN Security
Notes: The majority of that presentation was spent to explain what is KPS. Please refer to Doc. numbered 031.
Here, I would like to discuss security requirements and the functional features of KPS, while taking into account the other proposed methods. Then, I will make a proposal for a hierarchical structure to enhance WLAN security.

## Slide 3: Security Requirements
111.222.33.44
123.45.67.89
12 34 56 78 9A BC
22 44 66 88 AA CC
Internet
Physical layer
Datalink layer
Transport layer
Network layer
Session layer
Presentation layer
Application layer
IPSec
SSL / TSL
KPS
Internet
From: Alice
To:Bob
Subject:
ABC….
From: Alice
To:Bob
Subject:
ABC...
PGP/PEM
Notes: In the last meeting, 802.1x was introduced to be used commonly with 802.3, 802.5, etc. Security protocols performed in the upper layers are flexible and robust.
In order for the upper layer protocols to work well, it should be defined clearly in which layer those procedures will work and also the interface between the layers should be defined.

## Slide 4: Security Requirements in MAC (1)
Fulfill Various Security level Requirements
  From Simple to Complex Systems
WLAN’s own Characteristics should be hidden within MAC
  Protocols in the upper layers rely on PHY and MAC security
  Wireless LAN is easy to eavesdrop and to masquerade
  Need to protect as secure as wired LAN
Notes: Let’s summarize the requirements in the 802.11 MAC layer for WLAN security.
First, it is necessary to fulfill a variety of security level requirements.
There might be a simple system such as one consisting of a PC and a digital camera, or a large, complex system consisting of several sub-networks. Security requirements and acceptable costs should be different for each system levels.
WLAN systems must look as equivalent as wired systems. Characteristics ｏｆ wireless is that anyone can receive and transmit signals within radio wave range. This can be a weak point from a security view point, therefore secure ciphering and authentication are required to cover these characteristics. WLAN characteristics should be covered within the MAC layer.

## Slide 5: Security Requirements in MAC (2)
Secure Key Management
  Difficulty of Per-User Key Management
  Allow eavesdropping if keys are stolen
Secure Authentication with Machine ID
  Easier for attackers to connect to WLAN systems
Notes: It was mentioned in a 802.1x presentation that the secure key management and secure authentication can be performed in the upper layers. But, we believe that this must be performed also in MAC in order to ensure security protocols in the upper layers, because wireless LAN is easier for an attacker to access within the range of the radio wave. We believe MAC in a wireless system should be protected by encryption with per user keys. Then, key management is also very important as well as cryptography.
An authentication with a user ID can be performed in the upper layer, but an authentication with a machine ID is a role of MAC that covers the physical layer.

## Slide 6: Key Management Problem(1)
Per-user Key system is ideal, but practically impossible to deliver many unique keys.
  Example; 10 NICs system needs 45 keys in total, 9 keys per each NIC.
Where is it secure to store the keys
  How to prevent from theft
  Write only ROM is not enough
  An attacker can illegitimately overwrite ROM
Labor of key generation and maintenance
  Too many keys; N-1 per each NIC
(NIC: Network Interface Card)
Notes: Let’s now discuss Key Management Problems;
An attacker would try to steal the ciphering key, when it is impossible or very difficult to break the cryptography. Protecting the ciphering keys from attackers is also very important.
Per user key system is much safer, but it requires many keys and then it is much more difficult to manage keys. In the current 802.11 MAC standard, the mapped key system is seldom used.
Storing keys somewhere in the system could be risky because it’s possible to be stolen or overwritten.
Generating and revising the keys is a burdensome job when the number of keys increases. For a per user key system consisting of 10 NICs, 45 keys should be managed safely. The keys need to be updated often or during times such as a reorganization.

## Slide 7: Solutions to Key Management
Implementation of Key Distribution Systems
    KDC: (Key Distribution Center)
    CA: (Certification Authority)
    KPS: (Key Predistribution System)
Notes: There are some solutions, so called key distribution system, to manage the ciphering keys safely.

## Slide 8: Key Distribution
KDC (Key Distribution Center)
  An effective method used in Kerberos etc.
  KDC can deliver session keys safely.
CA (Certification Authority)
  Risky to use a public key cryptography without certification.
  CA issues a certification to secure public key cryptography.
Notes: Key Distribution Center, or KDC is an effective method used in Kerberos etc. It can deliver session keys safely with so-called tickets.
Certification Authority, or CA, makes public key cryptography secure. CA issues a public key of the receiver with a certification to a sender. The certification is signed by CA.
Those two methods are generally performed by software. They are flexible methods to enhance security. However, the system becomes more complicated and there is a possibility to be attacked by software such as Trojan Horse or password cracking. Unless the physical layer and MAC layer are not protected securely, there still can be a security hole.

## Slide 9: Key Distribution -KPS
Unique key to each TX/RX pair.
  No intermediary as in KDC.
Simple protocol
Terminates within the MAC layer.
Low administrative cost
Simple H/W.
MAC Address A
MAC Address B
……….
………...…
NIC B
NIC A
KPS
B
MAC Address A
KAB
KPS
A
MAC Address B
KAB
Notes: Now I will explain KPS which we propose.
In the Key Predistribution System, or KPS, both sender and receiver generate a unique shared key independently without any transmission of secret data such as tickets or certifications in a case of KDC or CA.
A certain algorithm to generate shared keys is implemented in the NIC in advance, for example, when it is manufactured. This algorithm is different among each NIC because it includes the root data based on each MAC address. When communication begins, a shared key can be generated by applying the party’s MAC address to the algorithm. KPS generates per user keys because each different pair generates a unique key in this system.
As the MAC addresses are included in the MAC header of every packet’s frame, KPS does not require any modifications on the current 802.11 protocol. In this proposal a shared key will be generated during authentication. After that all data streams are ciphered, and it becomes unable for any third party to know the contents.
Please note that all these processes terminate within the MAC layer.
It does not require any intermediate device nor administrative labor. Users are also released from the burden of managing encryption keys because the NIC already has the algorithm to generate a unique key corresponding to any party’s MAC address.

## Slide 10: Authentication by KPS(1)
Authentication by only MAC-Addresses.
  No other information is needed other than a MAC-Address.
  It is negligible even if authentication is eavesdropped
Perfect Mutual Authentication
  Exchange MAC-Addresses between parties
  When one feigns another MAC-Address, authentication fails.
Robust against S/W cracking
  H/W protects from S/W attack, e.g. cracking applications
  Robust against Virus, Worm, Trojan horse, ...
Notes: In this proposal, the authentication can be performed with Challenge and Response using a shared key generated from each party’s MAC address.
Success of a ciphered communication with KPS means directly that both sender and receiver use a correct NIC with KPS, and it certifies that both of the parties use correct MAC address. Therefore a mutual authentication can be established. KPS does not allow anyone to masquerade as an invader.
In the case of security measures performed in the upper layer, process or data is generally transferred between layers or between various machines. It is more possible to be attacked by wrong doing software such as Trojan Horse. We intend to use KPS in hardware so attacking by software is impossible.

## Slide 11: Authentication by KPS (2)
User Authentication is not enough
  Someone with malicious intent
Machine Identification
  Ability to identify Unmanned Devices
  e.g. AP, Printer….
Authentication on IBSS
Notes: It is risky to depend on authentication based only on a user identification. Someone with malicious intent may transfer his personal IDs to other people.
Machine identification is indispensable for unmanned machines such as access points or printers.
KPS authenticates with machine identifications. It certifies the MAC address signaled by the NIC is right. So, the security programs performed in the upper layer can become more robust based on the integrity of one to one correspondence between the NIC and its MAC address.
KPS does not require KDC so it can work in IBSS mode, too.
KPS does not identify users. User authentication should be performed by procedures in the upper layers.

## Slide 12: Features of KPS
Key distribution Algorithm
Terminates within only the MAC Layer
Mutual authentication between machines
Impossible to masquerade
Usable also in a IBSS without an AP
Low/No management/administrative cost
Does not affect the cryptography in other layers
Notes: As a summary of KPS’s features;
KPS is not cryptography but rather a system to deliver shared keys safely.
It terminates in the MAC layer.
Completely symmetrical and mutual authentication can be performed between the NICs using MAC address. It is unnecessary to use any secret information to generate a key.
It prevents impersonating a false MAC address.
It does not require any specific intermediate units, so it is available for IBSS mode, too.
It is inexpensive and it releases the burden of key management.
It can be used with other security methods, and becomes much stronger.

## Slide 13: MAC Layer (1)
KPS terminates within only the MAC Layer.
  Best for security in the Datalink layer of a OSI reference model.
  Fits well with IEEE802.11 standard.
Physical layer
Datalink layer
Transport layer
Network layer
Session layer
Presentation layer
Application layer
Notes: Now let me explain how KPS is adequate to enhance MAC layer by the following. KPS terminates within the datalink layer, and therefore fits well with the 802.11 MAC standard.

## Slide 14: MAC Layer (2)
KPS improves the L2 security.
More than one method should be used for security enhancement
  KPS is in L2
  Robust cryptographies in the upper layer (network or transport layer, etc)
EAP, TLS and Kerberos do NOT cipher packets at authentication.
  KPS will resolve this problem within the MAC Layer
MAC
IP
TCP
Notes: The features of KPS can cover the WLAN’s own characteristics, and it enables upper layer processes to work effectively. As I mentioned at the beginning, more than one measure should be used in parallel. KPS does not impact any other measure, because it works only within the MAC layer.
Further, EAP, TLS and Kerberos do not cipher packets at authentication. This is their weak point. The WEP enhanced with KPS will resolve this problem.

## Slide 15: 802.11with KPS and 802.1x
Notes: Now I would like to compare KPS and 802.1x.
First of all KPS works only in the MAC layer. KPS does not wander between the layers. So, KPS can work in parallel with any higher layer protocol. Moreover it does not require a complicated system so it is usable even with such a simple system as one digital camera and one PC.
KPS identifies machines and mutually authenticates. The authetication with a user ID is expeced to be performed in the upper layer.
We suppose our proposal is performed by hardware. Hardware is more robust against the software attacks. Hardware costs required by KPS is negligible. It can be realized with a small number of gates and a small memory which is already used in the current WEP. Recently software tends to cost more than hardware.

## Slide 16: 802.11with KPS and 802.1x
111.222.33.44
123.45.67.89
12 34 56 78 9A BC
22 44 66 88 AA CC
Internet
Physical layer
Datalink layer
Transport layer
Network layer
Session layer
Presentation layer
Application layer
IPSec
SSL / TSL
KPS
Internet
From: Alice
To:Bob
Subject:
ABC….
From: Alice
To:Bob
Subject:
ABC...
PGP/PEM
Notes: As we mentioned each method has its features and is performed in different layers.
What we emphasize is that we can build a more robust system if we adopt various methods in parallel, and not by selecting one.
The KPS we propose enhances the MAC security. Security can be further enhanced in conjunction to upper layer security protocols.
A hierarchical structure of security enhancement makes it easy to fulfill a variety of security levels.

## Slide 17: Example of KPS Application
Locatio - PDA
GPS
Digital Camera
PCS / Cellular Phone
Authentication and Ciphering with KPS
Notes: Before I conclude, I would like to introduce an example of KPS application. Locatio, a very powerful PDA, which has been already in Japan market, uses KPS to generate keys for encryption and authentication. Locatio includes GPS, a digital camera and mobile phone such as PCS or cellular. There are many services provided for the users including location service, e-mail and e-commerce. KPS is so simple and powerful. It gives satisfactory results for enhancing security.

## Slide 18: Conclusion
Security is enhanced with a hierarchical structure
  KPS fits hierarchical structure for security enhancement
  Various security levels
  User identification on the higher layer
KPS guarantees:
  Ciphered communication with a Per-User Key.
  Mutual authentication
  Ciphering and authentication within the MAC layer.
Assurance in the upper layer
  No other NIC can listen the communication except the party’s NIC.
  The MAC-Address reported by the party’s NIC is right.
Notes: Now I would like to conclude that a hierarchical structure should be taken for security enhancement. It applies to various security level requirements. KPS is suitable for the hierarchical structure. It protects security in the MAC layer and ensures security methods performed in the upper layers.
The WLAN market will benefit from KPS. We believe that this simple method of KPS to enhance MAC security should be adopted in the 802.11 standard.
Thank you