## Slide 1
IEEE 802.11 QoS MAC Enhancements
Joint Proposal
AT&T, Lucent, ShareWave

## Slide 2: Why Add QoS Support to the 802.11 MAC?
Why is it necessary to add new functionality within the 802.11 MAC sublayer to support QoS over wireless links?
  Higher layers assume that a LAN rarely loses or delays packets.
    WLAN PHY error rates are 3+ orders of magnitude greater than wired.
      So 802.11, unlike other 802 LANs, retransmits unacknowledged frames.
      Retrys cause unpredictable delays of tens to hundreds of milliseconds, and often block transmission of subsequent, queued frames.
  Wireless links incur very high per-packet MAC & PHY overhead:
    802.3 framing+gap adds 3.2% to a 1500-octet MSDU.
    802.11B (11Mb/s) framing+gaps+Ack adds 32.6% (50.0% with RTS/CTS).
  CSMA/CA collisions and backoffs reduce usable bandwidth as the offered load in a BSS increases.
    Switching hubs cannot be used to isolate STA-to-STA traffic over wireless links.
QoS-aware coordination can reduce overhead, prevent collisions and prioritize queued frames to meet delay and jitter bounds.

## Slide 3: What is Being Added?
This joint proposal provides new services and frame formats to support higher-layer, end-to-end QoS mechanisms:
  A QoS Data Service supporting Virtual Streams (VS) with specified QoS parameter values and including priority, data rate, delay and jitter bounds.
  An enhanced PCF allocates bandwidth to virtual streams and asynchronous traffic:
    New forms of CF-poll allow precise dynamic control with reduced overhead.
    Persistent transmission scheduling provides QoS-friendly power save operation.
  An adaptive technique prevents interference among overlapping, point-coordinated BSSs operating on the same channel, while allowing non-interfering transfers to occur in parallel, even when the overlapping BSSs are not part of the same ESS.
  A centralized Contention Control (CC) facility is more efficient than DCF contention for sending Reservation Request (RR) frames for new bandwidth allocations.
  New management frame subtypes support QoS and BSS overlap management.
  New data frame subtypes for "stream data" contain a VS identifier (VSID) field.
  New acknowledgement policies reduce overhead for many stream data transfers.
  Direct station-to-station transfers are permitted in a QoS-capable BSS (QBSS).
  A dynamic wireless repeater function can extend the spatial coverage of a QBSS.

## Slide 4
How Does the QoS Support Operate?
This joint MAC proposal is based upon an enhanced point coordination function that understands QoS-related parameters:
  Each enhanced station (ESTA) has a classification entity (CLSE) above the MAC to identify the virtual streams for incoming MSDUs.
  Each QoS-supporting BSS (QBSS) is controlled by an enhanced access point (EAP) with an enhanced point coordinator (EPC).
    The EPC includes a time allocation management entity (TAME) that allocates transmission opportunities (TXOPs) to ESTAs.
    TXOPs have defined starting times and maximum durations. ESTAs make local decisions about which MPDUs to transmit during each TXOP.
    A QBSS may have ESTA(s) that operate as bridge-portals (BPs) to allow alternate or multiple points of connection to the infrastructure.
    Spatial coverage of a QBSS may be extended by dynamically-activated Repeater Point Coordinators (RPCs).

## Slide 5
Compatibility
The proposed QoS functions are a direct extension of existing 802.11 functions:
  Reserved bits in existing frame formats are defined for the new functions:
    Capability Information bit 8 indicates QoS (and EPC in conjunction with CF bits).
    Data subtype bit 7 is set to 1 to indicate "stream data" in QoS MPDUs.
    Duration/ID bits 0-13 contain QoS control information during the CFP (msb=10).
    Several QoS-related Control and Management frame subtypes are defined.
  Existing stations can communicate in a QBSS during the CP (under DCF).
  Existing CF-pollable stations may be polled by an EPC during the CFP.
  The BSS overlap mitigation procedure is effective (but non-optimal) for reducing interference between QBSSs and a non-QoS BSSs.
  All stations must be CF-conformant as specified in IEEE 802.11-1999.
The proposed QoS support is intended to operate with existing authentication and privacy mechanisms, as well as any enhanced security facilities adopted as part of 802.11E.

## Slide 6
Fully distributed (without a PC):
  AP needs to contend, especially severe for asymmetric traffic loads.
  A large data burst needs to break down into a large number of MPDUs, each of which has to contend for transmission (resulting in lots of contentions if there are other data STAs sending data) and is likely to transmit beyond the TBTT (bad for other time-bounded frames).
  Backoff for collision resolution is based on the contention outcome of the backoff STA itself, and is far from being optimal.
Centralized versus Distributed Contention

## Slide 7
Partially distributed (with a PC):
  Contention and backoff under the DCF has the same shortcomings as noted above.
Centrally controlled:
  Any data burst needs to contend at most once to send a small RR frame, and its transmission is completely under the control of the PC (not getting impatient), with the contention never going beyond the TBTT.
  Collision resolution is based on the contention outcome of all STAs and can be optimised.
  Significantly improved data access delay and channel throughput performance.
Centralized versus Distributed Contention (Continued)

## Slide 8
Stream Service Interfaces

## Slide 9
Stream Service Interfaces
QoS-driven virtual stream service interfaces reference model
  Relationships between higher and lower layers
  Transformation of WLAN into QoS network within end-to-end QoS context
RSVP/SBM roles--Macro management
  VDS: Sender outside BSS, receiver inside BSS
  VUS: Sender inside BSS, receiver outside BSS
  VSS: Sender & receiver inside BSS
QoS parameters
MAC (PCF) roles--Micro management
  Queuing discipline needed for QoS support even for point-to-point transmissions
  Transmission time allocation to VSs (up, down, side)

## Slide 10
NON-EPC ESTA x
CLSE
TAME
LLC
MAC
MLME
SME
E-MLME
NON-EPC ESTA y
VS Update
VS Update
End-to-end QoS signaling messages
SBM = Subnet Bandwidth Manager
DSBM = Designated SBM
CLSE = Classification Entity
TAME = Time Allocation Management Entity
SME = Station Management Entity
E-SME = Enhanced SME
MLME = MAC Sublayer
Management Entity
E-MLME = Enhanced MLME
PC = Point Coordinator
VS = Virtual Stream
VDS = Virtual Down Stream
VUS = Virtual Up Stream
VSS = Virtual Side Stream
SBM
End-to-end QoS signaling messages
QoS values
& classifiers
1
VS’s & VSID’s
2
VSID’s & classifiers
3
VSID’s & QoS values
4
3
4
5
5
VS Operation
Classifiers
QoS values
5
5
PLME
PLCP
PMD
VS Service Interfaces Reference Model
Frame
CLSE
QoS values
(designated by VSID)
TAME
Tx
CLSE
TAME
LLC
MAC
MLME
SME
DSBM
EPC
1
2
PLME
PLCP
PMD
E- SME
4
CLSE
TAME
LLC
MAC
MLME
SME
SBM
3
4
PLME
PLCP
PMD
E-MLME
5

## Slide 11
NON-EPC ESTA x
Path messages (To receiver)
QoS values
& classifier
1
VS & VSID
2
VSID & classifier
3
VSID & QoS values
4
RSVP/SBM--Only Receiver Inside BSS
Resv messages (From receiver)
Path messages (From sender)
Resv messages (To sender)
Virtual Down-Stream (VDS) Setup:
1. DSBM extracts QoS values and classifier from new Path/Resv messages for a down-stream session, and makes admission decision on the session (accounting for the channel status update from MAC).
2. If the session is admitted, E-SME establishes a VSID for a VDS to serve the session.
3. E-SME passes VSID and classifier for addition to classification table at CLSE (for frame classification).
4. E-SME passes VSID and QoS values for addition to TAME (for bandwidth allocation).
5. E-SME has MLME send a management frame, VS Update, containing VS Operation (add VDS) and QoS values for the down-stream session.
Virtual Down-Stream (VDS) Modification:
1. DSBM extracts modified QoS values from Path/Resv messages for an admitted down-stream session and decides whether or not to honor them.
2. If yes, E-SME updates TAME with new QoS values for the established VSID, and has MLME send another VS Update, containing VS Operation (update VDS) and new QoS values for the session.
Virtual Down-Stream (VDS) Teardown:
1. DSBM extracts classifier from Path/Resv teardown messages or timeout indication for an admitted down-stream session.
2. E-SME matches classifier to VSID established for the session.
3. E-SME passes VSID and classifier for deletion from classification table at CLSE.
4. E-SME passes VSID for deletion from TAME.
5. E-SME has MLME send another VS Update, containing VS Operation (delete VDS) for the session.
CLSE
TAME
LLC
MAC
DSBM
1
2
3
4
E- SME
EPC
VS Update
5
VS Operation
QoS values
Data traffic direction--down stream--for which DSBM makes admission decision
5
CLSE
TAME
LLC
MAC
SBM
E-MLME

## Slide 12
NON-EPC ESTA x
Path messages (From sender)
QoS values
& classifier
VS & VSID
VSID & classifier
VSID & QoS values
RSVP/SBM--Only Sender Inside BSS
Resv messages (To sender)
Path messages (To receivers)
Resv messages (From receivers)
For confirmation
only
VS Update
5
VS Operation
Classifier
QoS values
5
1
2
3
4
Virtual Up-Stream (VUS) Setup:
1 & 2 same as for VDS setup.
3. E-SME passes VSID and QoS values for addition to TAME (for bandwidth allocation).
4. E-SME has MLME send a management frame, VS Update, containing VS Operation (add VUS), classifier, and QoS values for the up-stream session.
5. Upon receiving the management frame, the addressed ESTA’s E-MLME acts like EPC’s E-SME for its own CLSE and optionally TAME.
Virtual Up-Stream (VUS) Modification:
1 DSBM extracts modified QoS values from Path/Resv messages for an admitted up-stream session and decides whether or not to honor them.
2. If yes, E-SME updates TAME with new QoS values for the established VSID, and has MLME send another VS Update, containing VS Operation (modify VUS) and new QoS values for the session.
3. Upon receiving the new management frame, the addressed ESTA’s E-MLME updates its TAME with new QoS values for the established VSID.
Virtual Up-Stream (VUS) Teardown:
1 & 2 same as for VUS teardown.
3. E-SME passes VSID for deletion from TAME.
4. E-SME has MLME send another VS Update, containing VS Operation (delete VUS) and classifier for the up-stream session.
5. Upon receiving the new VS Update, the addressed ESTA’s E-MLME passes VSID and classifier for deletion from classification table at its CLSE/TAME.
Data traffic direction--up stream--for which DSBM makes admission decision
CLSE
TAME
LLC
MAC
DSBM
1
2
3
4
E- SME
EPC
CLSE
TAME
LLC
MAC
SBM
E-MLME

## Slide 13
CLSE
TAME
LLC
MAC
MLME
SME
DSBM
EPC
CLSE
TAME
LLC
MAC
MLME
SME
NON-EPC ESTA x
Path messages (From sender)
SBM
QoS values
& classifier
1
2
VS & VSID
VSID & classifier
VSID & QoS values
3
4
5
PLME
PLME
PLCP
PMD
PLCP
PMD
RSVP/SBM--Sender/Receiver Inside BSS
For confirmation
only
CLSE
TAME
LLC
MAC
MLME
SME
NON-EPC ESTA y
VS Update
SBM
5
VS Operation
Classifier
QoS values
5
5
PLME
PLCP
PMD
Path messages (To receiver)
Resv messages (From receiver)
Resv messages (To sender)
1
2
3
4
E- SME
E-MLME
E-MLME
4
Virtual Side-Stream (VSS) Setup, Modification, and Teardown:
Similar to those for Virtual Up-Stream.
Data traffic direction--up stream--for which DSBM makes admission decision
VS Update
5

## Slide 14
Virtual Stream Management Interface
Virtual Stream Update Service Primitives
  MLME-VSUPDATE.request (VSID, VS Action, VS Subaction, QoS Parameter Set, Frame Classifier, VS Update Failure Timeout)
    Sent by DSBM to cause transmission of a VS-Update management frame with the specified parameter values. The QosParameterSet and FrameClassifier are sent using information elements.
  MLME-VSUPDATE.confirm (Result Code)
    Confirms transmission of VS-Update managagement frame.
  MLME-VSUPDATE.indication (VSID, VS Action, VS Subaction, QoS Parameter Set, Frame Classifier)
    Informs SBM of reception of a VS-Update management frame.
Channel Status Service Primitive
  MLME-CHANNEL-STATUS.indication (BWAvailable, BWUsed)
    Generated by TAME once per superframe to inform DSBM of the amounts of channel bandwidth available and in use for QoS transport.

## Slide 15
MAC Data Services
Two services are available at the MAC SAP
  Asynchronous Data Service, as defined in IEEE 802.11-1999
  QoS Data Service, for MSDUs belonging to virtual streams
MAC Data Service Primitives
  MA-UNITDATA.request (source address, destination address, routing information, data, priority, service class)
  MA-UNITDATA.indication (source address, destination address, routing information, data, reception status, priority, service class)
  MA-UNITDATA-STATUS.indication (source addr, destination addr, transmission status, provided priority, provided service class)
  For Asynchronous Data Service the Priority parameter contains either "Contention" or "Contention Free" (as currently specified).
  For QoS Data Service, the Priority parameter contains the virtual stream identifier (VSID), which is an integer in the range 1-4094.

## Slide 16
QoS Parameters--VSID
Acknowledgment Policy: Normal, alternative, delayed, no acknowledgment
Retransmission Delay: For delayed ack only
Flow Type: Continuous, Discontinuous
Priority Level: Orthogonal to Flow Type
FEC Info: No coding being an allowable option
Privacy Info
Delay Bound: May be zero
Jitter Bound: Parameter, Delay Bound
Minimum Data Rate
Mean Data Rate: R
Maximum Data Burst: B
Token bucket
Max data size over T = R*T + B

## Slide 17
Frame Classification
IP classification parameter subtable
----------------------------------------------------------
LLC classification parameter subtable
----------------------------------------------------------
IEEE 802.1 P/Q parameter subtable
LLC
Header
Packet
Header
Classification
Table
Search
Priority
Search
Priority
Search
Priority
Classification
Classification
For MA-UNITDATA.request
Unclassifiable frames treated as best-effort traffic, which requires no specific VS setup.

## Slide 18
Classification Parameters
The IP Classification Parameters may be zero or some of such parameters as IP TOS Range/Mask, IP Protocol, IP Source Address/Mask, IP Destination Address/Mask, TCP/UDP Source Port Start, TCP/UDP Source Port End, TCP/UDP Destination Port Start, and TCP/UCP Destination Port End.
The LLC Classification Parameters may be zero or some of such parameters as Source MAC Address, Destination MAC Address, and Ethertype/SAP.
The IEEE 802.1P/Q Parameters may be zero or some of such parameters as 802.1P Priority Range and 802.1Q VLAN ID.

## Slide 19
Proposed Channel Access Mechanism

## Slide 20: Proposed Channel Access Mechanisms
Enhanced frame format
Overview of proposed channel access mechanisms
Centralized contention and reservation requests
Transmission opportunities
  Scheduling
  Multi-poll
Delayed acknowledgement
Channel time allocation method

## Slide 21: Enhanced frame format (1)
Backward compatible Duration/ID field enhancements
  Ack policy, Non-final bit, Tx-op limit by EPC, VS size by ESTA, Priority limit and CCI length for CC frames
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 22: Enhanced frame format (2)
Sequence control is used per stream in “stream data” subtype frames
VSID in stream data type appears between the currently defined MAC header and the WEP-IV. VSID contains,
  12 bits of stream ID in the range of 1 to 4094
  1 bit information on whether a stream is a side stream
FEC Option
  Header FEC protects the header alone and provides a quick way for using the header contents even before the end of frame
  MSDU, WEP-ICV and FCS are FEC protected separately.
Max size of 2316
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 23
Time Allocation by TAME Algorithm
Central queueing of all data traffic
  Data arrivals to VDSs: Physically queued at EPC
  Data arrivals to VUSs/VSSs: Virtually queued at EPC
    Continuous VUSs/VSSs: Data arrivals are periodically queued at EPC, with arrival sizes predicted by QoS values (e.g., mean data rate and burst data size) and adjusted by VS size subfield amid data transmissions.
    Discontinuous VUSs/VSSs: Data arrivals are queued at EPC via VS size indication by sending STAs through reservation request or piggybacking.
Transmission opportunities (TXOPs) of queued data traffic
  Allocated by applying QoS-driven scheduling algorithm to all queued data arrivals in accordance with corresponding QoS values
  Conveyed to non-PC ESTAs by + CF-Poll, CF-MultiPoll, or CF-Schedule frames, (re)allocable locally
Buffered data size indications
  STA piggybacks buffered data size on a VUS/VSS via VS size subfield of Duration/ID field amid data transmissions.
  STA sends Reservation Request (RR) frames via centralized contention (CC) upon new burst arrival.

## Slide 24
Enhanced Access Mechanisms
Frames on VDSs are transmitted by EPC in lieu of their QoS values.
Frames on continuous VUSs/VSSs are given periodic (variable) TXOPs in lieu of corresponding QoS values and buffered data size indications.
Frames on discontinuous VUSs/VSSs are given bursty TXOPs in lieu of corresponding buffered data size indications and QoS values.
  When new burst arrives on such VUS/VSS, ESTA either begins sending the burst (and hence piggybacking the size info) by preempting TXOP given to another lower priority VS, or sends a RR frame on behalf of the new burst into such a TXOP or into one of the CCOPs following a CC frame.
  When buffered data size indication is zero (i.e., the burst has been completely transmitted prior to arrival of another new burst on the same VS), no more TXOPs are allocated to the VUS/VSS until the indication of another burst arrival.
Dx = data frame sent by AP to STA x, Ux = data frame sent from STA x to AP
Sxy = data frame sent from STA x to STA y, VSn = data frame sent from VSn
TXOP = transmission opportunity, CC = contention control, CCI = centralized contention interval, CCOP = centralized contention opportunity, RR = reservation request, CFP = contention free period (under PCF rules), CP = contention period (under DCF rules)
Superframe (CFP repetition interval)
CCI
B
SIFS
RR
CCOP
Sche-
dule
S4
(No
Ack)
RR
RR
RR
RR
CCI
CP
Multi-
Poll
CFP
U2
D1
CC
+
Ack
VS13
Ack
+
Poll
CC
TXOP
Scheduled
CF-
End
VS28
VS31
Dly-
Ack
D2
+
Poll
U1
+
Ack
TBTT
TBTT
Sche-
dule

## Slide 25: Summary of proposed channel access mechanisms
EPC uses the following mechanisms for Tx-ops
  Poll using CF-poll for backward compatibility
  Poll using data+CF-Poll for backward compatibility
  Persistent scheduling for efficiency and for power-saving
  Poll using enhanced CF-Multipoll for efficiency
ESTAs strictly follow the channel time allocated by the EPC
ESTAs make local decisions on which stream is transmitted in a Tx-op
EPC may monitor the channel to make sure ESTAs follow its directives
Superframe (CFP repetition interval)
CCI
B
SIFS
RR
CCOP
Sche-
dule
S4
(No
Ack)
RR
RR
RR
RR
CCI
CP
Multi-
Poll
CFP
U2
D1
CC
+
Ack
VS13
Ack
+
Poll
CC
TXOP
Scheduled
CF-
End
VS28
VS31
Dly-
Ack
D2
+
Poll
U1
+
Ack
TBTT
TBTT
Sche-
dule
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 26: Centralized contention and Reservation Request (1)
B
CC
+
(Ack)
CCOP
CCI
RR
RR
CFP
CP
CF-
End
Superframe
B
CC is used by EPC to solicit RR frames from the ESTAs with pending requests
CC frame indicates the number of opportunities for RR frames in CCI field
RR is used by ESTAs to submit the request for the extra bandwidth required
Based on the RR frames received, the EPC adjusts the channel time for the stream
RR
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 27: Centralized contention and Reservation Request (2)
Information provided in CC frame are:
  The limit on priority of the streams in the solicited RR frames
  Number of opportunities for RR frames in CCI
  Permitted probability with which the ESTAs can send RR frames. ESTAs use CCOP randomly with this probability. This reduces the number of ESTAs taking the same CCOP for their RRs
  Feedback: All the VSIDs for which the RR is already successfully received
RR frame indicates the current size of buffer awaiting transmission for a particular stream. This frame is used to obtain the channel time allocated dynamically from the EPC in an incremental fashion
Frame Control
Duration/
ID
BSS ID
Feedback Count (r)
Centralized Contention (CC) frame
Reservation Request (RR) frame
Permission
Probability
Feedback
VSIDs
Priority
Limit
CCI
Length
2*r
VS
Size
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 28: Transmission opportunities - CF-Schedule (1)
A transmission opportunity (Tx-op) can be scheduled to be persistent for a duration indicated in the Schedule frame
EPC uses this frame to schedule repetitive streams
EPC can change the allocation at any time by sending another schedule frame with altered allocation
All schedule times are relative to TBTT
B
CFP
CP
Superframe
SIFS
VS3
Sche-
dule frm
VS9
Sch time
CF-
End
B
CFP
CP
Superframe
SIFS
VS3
VS9
Sch time
CF-
End
B
TBTT
TBTT
TBTT
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 29: Transmission opportunities - CF-Schedule (2)
EPC can schedule Tx-ops for multiple ESTAs using a sch-frame
Each ESTA is provided with start time and a time limit on its Tx-op
The schedule records are arranged in the order of their occurrence
ESTA can not use this scheduled Tx-op after the expiration of its nominal life time
Initiation delay is for synchronisation of all related ESTAs with the current schedule. The schedule frame is repeated in successive super frames with the decremented delay in every transmission. The delay value is decided based on the prevailing channel conditions.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 30: Transmission opportunities - CF-Schedule (3)
Note that when the “Non-Final” bit in the Duration/ID field is cleared, then a next scheduled station is allowed to do opportunistic reuse based on the Tx-Op flags.
Tx-op flags are to indicate
  Early Start: the option of opportunistic reuse of channel time when the previous Tx-op is not fully utilised
  Need Wait: the necessity of ESTA having to wait for such an opportunistic reuse of channel time. This is required when a stream has multiple Tx-ops within a CFP and the devices corresponding to the streams following this stream has to wait for the right Tx-op of this stream before using the channel time opportunistically.
  Extend limit: the option of extending the Tx-op limit to the original end time when such an opportunistic reuse is allowed
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 31: Transmission opportunities - Multi-poll
The indicated times are relative to the CF-Multi-poll frame
EPC can schedule Tx-ops for multiple streams
The multi-poll records are arranged in the order of their occurrence
Each record contains a Tx-op time limit for a stream
The Multi-poll Tx-op is used ONLY in the current CFP
CF-Multi-poll
B
VS8
VS4
CFP
CP
CF-
End
Superframe
VS1
B
TBTT
TBTT
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 32: Delayed Acknowledgement
Acks for group of data frames of a stream are indicated in a record
Records corresponding to multiple streams can be sent in this frame
Multiple records corresponding to the same stream are allowed
The Vs-seq indicates the starting sequence number in the group of data frames for which the status is indicated in the rx bit map
The rx bit map contains a ‘1’ for a successfully received stream data frame
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 33: Channel Time Allocation Method
EPC knows (and remembers) the Qos parameters of the stream as supplied by DSBM and interfaces to higher layer
  Allocated bandwidth
  Continuous or discontinuous
  Quantitative or qualitative (RSVP or 802.1p)
EPC collects RR frames from each ESTA
EPC also knows (and remembers) the traffic route within QBSS whether it is VUS, VDS, VSS or going through Repeater-coordinator
EPC allocates the channel time as
  CF-poll for STA
  Efficient poll on request (RR) for ESTA
  Schedule for periodic Tx-ops for a nominal lifetime for ESTA
  CF-Multi-Poll with VSID for ESTA
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 34
BSS Overlap Provisions

## Slide 35
Introduction
BSS overlap management is essential for dense PCF coverage.
  QoS streams are highly time repetitive in nature.
    That means that the interference generated in an other BSS will be highly repetitive also, which can cause high failure rates.
  Under the DCF failures due to overlap are more random, but produces a higher retry rate, which translates into more delay and lower throughput.
    Bursty traffic is robust for that, but this is unacceptable for QoS traffic.
An EPC needs to coordinate its CFP with overlapping QBSSs.
  To prevent failures due to overlap interference.
  To allow sharing of the medium by multiple QBSS’s even if they are not connected to the same infrastructure.
The proposed mechanism allows substantial bandwidth reuse among nearby QBSSs for both DCF and PCF traffic.
  And lets a QBSS minimize impact of an overlapping non-QoS PCF.
  The proposed mechanism allows for different levels of implementation:
    Simple, less reuse-efficient solutions or Complex, more reuse-efficient solutions.
    Providing sufficient hooks to allow for different levels of BSS overlap sophistication.

## Slide 36
AP(A) can communicate
with AP(B) via Proxy (Pa)
at a low rate
802.11b radios need about a 3:1 distance ratio to achieve a desirable 15 dB SIR for proper 11 Mb/s operation.
While the distance over which other (lower) rates can operate will be around: (based on 10 dB per distance doubling)
  11 Mb/s SIR=15 dB assume 1
  5.5 Mb/s SIR=12 dB factor 1.2
  2 Mb/s SIR= 9 dB factor 1.6
  1 Mb/s SIR= 6 dB factor 2
So interference can be experienced from a station which we can not even see at 1 Mb/s.
Potential Proxy Stations are assumed to be in (low rate) range of the overlapping BSS to allow exchange of information.
Distance Ratios Summary
Traffic within this area
still possible independent
of BSS-B
AP-a does not “see” AP-b
Px=Proxy BSSx

## Slide 37
Basic Mechanisms
The overlap manager must dynamically configure the overlap situation.
  Since in many cases the EPC does not “see” the overlap BSS traffic.
  While it can generate significant interference if traffic overlaps in time.
  While in addition due to mobility of stations, the overlap situation can dynamically change.
ESTAs detect possible overlaps based on the error rates for the traffic of each virtual stream.
  And send this information to the EPC using an "Error and Overlap" management frame, on demand or unsolicited when a threshold is crossed.
  Stations can report the BSSID from overlapping BSS it sees.
    It can try to active Probe at a low rate, to solicit low rate response.
The AP can use this information for corrective actions, to prevent CFP overlap for that stream.
  Such a stream should be serviced in a part of the CFP that is coinciding with a forced silence period in the overlapping BSS.
A wireless communication channel must be available between overlapping QBSSs (which might not be part of the same ESS).
  An ESTA in an overlap region can serve as a Proxy for forwarding (overlap) management information.
  Each Proxy relays the management information to the other BSS in a Proxy Beacon, which also provides a timing reference point for the other BSS.
All overlapping QBSSs need to agree on the SuperFrame size.

## Slide 38
BSS Overlap Example
BSS-A does not experience interference of BSS-C and visa versa
Parts of BSS-A and BSS-C do experience interference from at least part of BSS-B
Parts of BSS-B do experience interference from parts of both BSS-A and BSS-C
General approach: The CFP needs to be subdivided into 3 time windows.
  TOL(X) that is servicing streams to the “Overlap sensitive area”
  TS, which is a forced silence period to prevent interference with TOL traffic from the overlapping BSS(es).
  TNOL(x) in which streams are serviced that are not sensitive to overlap (could be zero).
In this example traffic in BSS-A can run completely in parallel to traffic in BSS-C.

## Slide 39
Overlap Management Information
Like the access mechanism the overlap management is based on TIME, divided in “overlap Time” and “non-overlap Time”.
It is assumed that an EPC maintains the following information, based on its “Overlap feedback” from stations:
  Tnol(a) Amount of CFP time allocated to non-overlapping traffic
  Ttol Total amount of overlap traffic time.
    This is the total CFP time allocated to overlapping traffic.
  Tol(a,m-n),OBSSID Amount of CFP time allocated to traffic overlapping with BSS-x
    This is a list of (Time,BSSID) for BSSID x to n
    If a station is unable to distinct with which BSSID it does overlap for which time, then the Tol(x) value will be zero, but Ttol should be used.
This information is distributed to a neighboring QBSS via Proxy Beacon.
  This Proxy Beacon does also contain the Tol information (as described above) that is being received by this QBSS from all neighboring QBSSs.
  So a EPC can easily determine from this information that a neighbor QBSS does overlap with a QBSS that does NOT overlap with this QBSS which allows for TOL time allocation optimization.

## Slide 40
Steady State CFP Synchronization
All overlap management information is in the Proxy Beacon
There is NO centralized coordinator needed to manage this.
  Each EPC can derive its CFP time allocation parameters in a distributed way from the Proxy Beacons it receives.
    Can tolerate a certain amount of lost Proxy beacons (reasonably robust).
  Each EPC will adapt its TSF timer to the “Oldest” timestamp value from the Proxy Beacons it does receive (similar to an IBSS).
    Taking into account the TBTT-offset compared to the overlapping BSS.

## Slide 41
CFP Synchronization
After TBTT the EPC needs to schedule its “Overlap traffic” period (TOL) or one or more “Silence” period(s) TS.
  An “Overlap traffic” period TOL does always start with a Proxy Beacon.
    While Beacons are preferably send at the start of the TOL period.
  A “Rule” is defined that determines when the TOL period starts.
    Start with longest TOL that allows max TOL overlap between non-overlapping BSS’s (A and C)
    The same rule is used to schedule the Silence period (TS) in the other BSS.
  From the Proxy information EPC-A does see that QBSS-B does overlap with a QBSS (C) which does NOT overlap with QBSS-A (Likewise for EPC-C)
    From this information both EPC-A and EPC-C can independently determine that they can schedule the TOL traffic in parallel, and that that period can best be scheduled at the start.
Then the EPC is allocating its non-overlap traffic for the duration of TNOL .
  This bandwidth is used in parallel in each QBSS, independent of PCF and DCF activity in other BSS’s.

## Slide 42
Dynamic Overlap Configuration Approach
Every time a new virtual stream is established.
  The EPC can allocate its TxOP in the TNOL period.
    Assuming it can overlap.
    This info is distributed to the overlapping BSSs via the Proxy Beacon with an activation count indicating when the new time allocations take effect.
  If the stream is started, the ESTA starts gathering error statistics, and alarms the EPC when many errors occur.
    This can happen in the BSS that just established the new stream.
    Or in the overlapping BSS, where a stream in the TNOL period starts to experience failures due to the new overlap by the new connection.
  If this happens then the EPC (that receives the error reports) will reallocate the TxOP to a TOL period.
    Which is distributed to the other BSS prior to its activation.
    So that the new situation takes effect synchronously within all BSSs.
  The same actions will occur when a mobile station does move into an overlap vulnerable area.

## Slide 43
TSF Synchronization
TOL start is the reference point to send a Proxy Beacon.
  Which also contains the Timestamp information of the QBSS.
Each EPC adjusts its TSF using the above Tadjust formula
  But only if its calculation is positive (follow oldest QBSS).
  All stations adopt the TStamp of its own BSS.
The Delta(PBC) is the actual delay (of the timestamp sample point) compared to the TOL(B) reference point, which is TS(B) away from TBTT-B.

## Slide 44
Advantages of Proposed Method
Fully distributed synchronization approach.
All information is in the Proxy Beacon, and no other management interaction is needed for the purpose of overlap management.
  The relevant allocated bandwidth in the overlapping QBSSs, with which the EPC needs to share its CFP, is directly available to each EPC.
  The matter in which BW is budgeted for new connections is a matter of management policy.
Simple time synchronization of the TSF of each EPC.
  All the information needed to calculate the TBTT offset with the neighbor QBSS is in the Proxy Beacon.
Allows for bandwidth reuse for both PCF and DCF.
  Those QBSSs that do NOT overlap with each other can schedule their entire traffic in parallel (both TNOL and TOL).
This method is easily scalable for more simultaneous and more independent overlap situations.
  With big reuse advantages (especially for more independent overlaps)

## Slide 45
Overlap with Legacy DCF and PCF
Case: OBSS is using legacy DCF only.
  No PCF to coordinate with
  But Proxy Beacon can prevent DCF traffic by its CFDUR_Remaining parameter.
    CF-coexistence provisions in the existing standard will prevent overlapping traffic.
Case: OBSS is using a legacy PCF (and DCF).
  Coordination does not work as is.
  ESTA’s can report whether a Legacy PCF overlap exist in their “Error and Overlap” management frame.
  Can only be based on “CFDur_remaining” parameter in the PCF Beacon and Proxy Beacon.
    It depends on overlap mitigation procedure implemented in the legacy PCF, how effective this is.
  The QBSS is to adapt to the CFDUR_Remaining and the Time synchronization of the legacy PCF.

## Slide 46
802.11e Connectivity Model
The 802.11 Connectivity model
needs to be enhanced
to allow better use of the medium
for the high bandwidth requirements of QoS

## Slide 47
Connectivity Goals
A target environment is a home situation.
  Where a single BSS solution is important
  But the physical position of the access entity to the outside world is not likely the center of the BSS where you would like to have your coordinator placed.
    Phoneline or Cable are potential alternative media that you want to connect to.
  While in some instances an extension of the range of a BSS using a simple repeater function is desirable.
    This is called a Bridge Portal (BP).
  While some applications like video require high bandwidth requirements.
Therefore we would like to satisfy the following requirements
  Allow multiple DS connection points within a QBSS.
  Allow a Wireless repeater function.
  Allow using the most BW efficient connection using direct Station-to-Station instead of routing via the AP, where the conditions allows it.
    This is called Side Stream.

## Slide 48
Multiple DS Connectivity Model
The WDS frame format is used for all Virtual Side Streams
  To avoid a security problem using the To/From=00 being a class 1 frame.
  Further it makes all Side Streams (Also to the BP) using an identical mechanism.
802.11 can allow all the addressing modes shown
  So all these communication links are possible

## Slide 49
Extended Coverage Connection Model
The Repeater Point Coordinator (RPC) is a subsidiary Point Coordinator.
  A Probe Response of an RPC will contain a BSSID of the Primary QBSS to which it is associated.
Streams are setup and identified unidirectional end to end within the (extended) QBSS coverage area.