## Slide 1: Market Acceptability Throughput Issues for HRb
Mark Webster and Karen Halford
Intersil Corporation
May 2000
This Microsoft Powerpoint presentation has notes attached.
Please expand to “Notes Page View” mode.

## Slide 2: Data Rate Needs
AV from DVD
AV from digital VCR
Networked printer
Video gaming
Internet browsing
HDTV
6 - 10 Mbps*
4 - 8 Mbps*
4 Mbps*
4 Mbps*
2 Mbps*
20 Mbps*
There is typically a need for 2 or more
applications to run simultaneously.
* These numbers were taken from HomeRF’s technical requirements document.
Required Throughput:
20 Mbps
Notes: This data was taken from HomeRF’s technical requirements document.
It is clear from these needs that it is highly desirable to maintain a throughput of 20 Mbps or more. If we don’t provide at least 20 Mbps, it will not be possible to provide a high quality AV link (HDTV.) Also, it may be necessary to provide 2-3 of these types of services simultaneously. This boosts the required rate up to at least 20 Mbps as well.

## Slide 3: 802.11a Throughput Calculations
Sync
Header
MPDU: X Bytes
Ack
# Bits:
Rate:
Time:
8 usec
8 usec
8*X bits
R MBPS
8*X/R usec
112 bits
2 MBPS
56 usec
OFDM
Throughput = 8*X Mbps / (8+8+8*X/R+16+8+8+ 56)
Sync
Header
16 usec
8 usec
8 usec
Notes: These are the bit/time durations used in upcoming plots. The exact throughput calculation is shown below the sample frame. We assume an ideal scenario for our throughput calculations. No collisions are included, and we assume that there are no packet errors. Thus, this is more or less and “upper bound” on performance.

## Slide 4: 802.11b Throughput Calculations
Sync
SFD
Header
MPDU: X Bytes
Ack
Sync
SFD
Header
# Bits:
Rate:
Time:
128 bits
1 MBPS
128 usec
16 bits
1 MBPS
16 usec
48 bits
1 MBPS
48 usec
8*X bits
R MBPS
8*X/R usec
128 bits
1 MBPS
128 usec
16 bits
1 MBPS
16 usec
48 bits
1 MBPS
48 usec
112 bits
2 MBPS
56 usec
LONG PREAMBLE
Throughput = 8*X Mbps/ (128+16+48+8*X/R+10+128+16+48+56) usec
10 usec
Sync
SFD
Header
MPDU: X Bytes
Ack
Sync
SFD
Header
# Bits:
Rate:
Time:
56 bits
1 MBPS
56 usec
16 bits
1 MBPS
16 usec
48 bits
2 MBPS
24 usec
8*X bits
R MBPS
8*X/R usec
56 bits
1 MBPS
56 usec
16 bits
1 MBPS
16 usec
48 bits
2 MBPS
24 usec
112 bits
2 MBPS
56 usec
SHORT PREAMBLE
10 usec
Throughput = 8*X Mbps / (56+16+24+8*X/R+10+56+16+24+56) usec
Notes: These are the bit/time durations used in upcoming plots. The exact throughput calculation is shown below the sample frame. We assume an ideal scenario for our throughput calculations. No collisions are included, and we assume that there are no packet errors. Thus, this is more or less and “upper bound” on performance.

## Slide 5
Throughput Comparison of 802.11a for Rates of 12, 24 and 36 Mbps
Notes: This plot shows the throughput for 802.11a for rates of 12, 24 and 36 Mbps. The 20 Mbps throughput is marked in red. Notice that both rates 24 and 36 Mbps achieve the 20 Mbps throughput. In fact, the 36 Mbps rate achieves this throughput at about a length 600 byte packet, and the 24 Mbps rate achieves this throughput at around a length 1600 byte packet. Once again, we point out that this is an upperbound on the throughput, and a realistic system will have a lower throughput due to packet errors and collisions.

## Slide 6
Throughput Comparison of 802.11b for Rates of 11, 22 and 33 Mbps
Long Preamble
Short Preamble
Notes: This plot shows the throughput for 802.11b for rates of 11 and potentially 22 and 33 Mbps. The 20 Mbps throughput is marked in red. Notice that the only rate that achieves this throughput is 33 Mbps with a short preamble, AND this rate does NOT achieve a throughput of 20 Mbps until the MPDU is around 1600 bytes long. Recall also, that this is an upperbound on the throughput, and a realistic system will have a lower throughput due to packet errors and collisions. In a real system the longer packets can reduce the effective throughput because an error is more likely to occur in a longer packet. Thus, retransmissions are not only more likely, but also take longer.

## Slide 7
Throughput Comparison of 802.11a vs. 802.11b for Rates of 12 and 11 Mbps

## Slide 8
Throughput Comparison of 802.11a vs. 802.11b for Rates of 24 and 22 Mbps
Notes: Once again, the OFDM curve plateaus to a throughput close to the actual data rate when the packets are around 2000 bytes long. The Short Preamble curve doesn’t approach the actual data rate until the packets are close to 4000 bytes long. The only curve that achieves the 20 Mbps throughput is the OFDM 24 Mbps curve.

## Slide 9
Throughput Comparison of 802.11a vs. 802.11b for Rates of 36 and 33 Mbps
Notes: The OFDM curve achieves the 20 Mbps throughput for a packet length of about 500 bytes. The Short preamble curve achieves this throughput for length 1600 packets, and the long preamble achieves this throughput for length 2900 packets.

## Slide 10
Realistic Impairments and Considerations Not Included in This Analysis
Packet Errors cause retransmission.
PCF/DCF Modes
Packet collisions
Backoff mechanism to avoid collision
MAC Enhancements

## Slide 11
Conclusions
Effective throughput can be increased by shortening the preamble.
802.11a achieves 20 Mbps throughput for rates of 24 Mbps and higher.
802.11b achieves 20 Mbps throughput for rates of 33 Mbps and higher.
In an error-free environment, longer packets increase throughput. In realistic environment longer packets may reduce throughput due to more/longer retransmissions due to errors