## Slide 1: Brief Overview of Information Theory and Channel Coding
Steven D. Gray
1

## Slide 2: Outline
Information theory
  Gaussian channel
  Rayleigh fading channels
Two approaches for achieving the same rate
Convolutional encoding
Convolutional decoding
Hardware implementation of a Viterbi
Conclusions
2

## Slide 3: Brief Introduction to Information Theory
Encoder
Channel
Decoder
Message
Estimate
of Message
Is a codeword from an alphbet of size n (ex. A point in an 8 PSK consellation)
Channel capacity is the highest rate in bits per channel use at which information
can be sent with arbitrary low probability of error.
3

## Slide 4: A Little Information Theory Capacity for the Gaussian Channel
For a Gaussian Channel with Bandwidth, W
:
bits per second
4

## Slide 5: A Little Information Theory Capacity for the Flat Rayleigh Channel
Average Capacity
where
P is the average power and E is Euler's constant
Source: W.C.Y. Lee, "Estimate of Channel Capacity in Rayleigh Fading Environment,"
IEEE Transactions on Vehicular Technology, Vol. 39, No 3, August 1990.
5

## Slide 6: A Little Information Theory Capacity Region Comparison
For channels of interest (heuristically speaking)
- Gaussian capacity is an upper bound
- Flat Rayleigh capacity is a lower bound
6

## Slide 7: A Little Information Theory Gaussian Channel Capacity
Shannon Capacity vs. Existing 2.4 GHz Wireless LAN at 10-6 BER
7

## Slide 8: A Little Information Theory Conclusions
Shannon tell us that there is room for exploitation
Approaches should be pursued to exploit cases when the SNR is good
  With a good code, 20 Mbps is possible in the Gaussian channel when the SNR is 10 dB or less
  Good codes are available with reasonable complexity
8

## Slide 9: Two Approaches for Achieving Same Rate
Approach 1
  Uncoded BPSK modulation
    IEEE802.11a without convolutional coding
    Perfect synchronization and channel estimation
    Rate = 12 Mbps
  Additive White Gaussian Noise (AWGN)
Approach 2
  Coded QPSK modulation
    IEEE802.11a PHY with convolutional coding
    Rate 1/2, 64 state convolutional code
    Perfect synchronization and channel estimation
    Rate = 12 Mbps
  AWGN
9

## Slide 10: Two Approaches for Achieving Same Rate
10

## Slide 11: Two Approaches for Achieving Same Rate
Conclusion: Channel Coding can Improve Spectrum Efficiency
Bandwidth Reduction
11

## Slide 12: Convolutional Encoding
Data Source
+
+
Storage Element
Generic Rate 1/2 Encoder
00
11
01
10
S
0
S
1
S
2
S
3
11
11
11
11
10
01
10
01
00
01
00
00
00
00
11
00
11
00
10
10
01
01
01
10
11
10
Trellis Diagram
R=1/2
4 state
Start from all
zero state
12

## Slide 13: Convolutional Decoding
Optimal, bit error rate, decoding is achieved by maximizing the likelihood function for a given codeword
  Compare the received codeword to all possible codewords and pick output with smallest distance
Viterbi in 1967 published a dynamic programming algorithm for decoding
Complexity in decoding is proportional to the number of states and the number of branches into each state
  Example: 64 state code used in PBCC or IEEE802.11a
    128 metric calculations per transition in the trellis
13

## Slide 14: Hardware Implementation of Viterbi
64 state code from PBCC and IEEE802.11a
32 Add Compare and Select (ACS) units (32 butterflies)
Trace back length is 32 (should be 4 - 5 times constraint length)
Input is <3,2,t> and path metrics are <10,9,t>
Branch
Metric
Computation
Add Compare
Select
Trace Back
Unit
Set Initial
State
Store
Path
Metric
Branch
History
Bit Stream
Soft
Inputs
14

## Slide 15: Hardware Implementation of Viterbi
Register Transfer Logic (RTL) synthesis for Viterbi VHDL is done using Synopsys Design Compiler
Target for RTL is Xilinx Virtex 1000e Field Programmable Gate Array (FPGA)
Design complexity
  55.7K logic gates
  8Kbytes of Xilinx RAM (4 RAM blocks) for convience
  Actual required RAM is 500 bytes
15

## Slide 16: Conclusions
Channel coding is a means to improve spectrum efficiency over an uncoded system
Particularly for achieving rates above 20 Mbps, channel coding will make required SNR's reasonable
Hardware complexity is absorbed in the digital ASIC
  Impact on IC costs are small
  Engineering design costs are always a factor for a more complex design
16