## Slide 1
Jyri Rinnemaa, Jouni Mikkonen
Nokia
Slide 1

## Slide 2: Contents
Discussion on the current 802.11 security features
Summary of proposed enhancements and justifications
Conclusions
Annex: Example Network architecture scenarios
Slide 2

## Slide 3: IEEE 802.11 security features
WEP expects pre-shared secret keys between Station (STA) and Access Points (AP).
  This approach is not very scalable because station-to-station authentication is tied to the IEEE 802 MAC address which makes the user authentication device dependent. The current approach will not allow the user to "roam" by using different WLAN devices at different locations.
User authentication is not supported - only device authentication is possible.
  Nowadays WLAN systems are becoming widely accepted and deployed in public networks, such as airports and hotels. In these environments a device independent, globally unique authentication string would be beneficial.
Slide 3

## Slide 4: IEEE 802.11 security (cont'd)
RC4 algorithm with 40-bit key length could be increased to improve data confidentiality. To improve the radio link security longer keys up to 128 bits should be supported
Attacks against message integrity are possible when the plain text is known.
Negotiation of the optional security features is not supported between STA and AP.
  A dynamic capability set exchange is needed to overcome the compatibility problem with the old devices and to allow flexible future enhancements for the IEEE 802.11 security
Mutual authentication is not supported - only STA is authenticated in the association phase
Slide 4

## Slide 5: Summary of the Proposed Enhancements
Support for user dependent security keys which enables WLAN-to-WLAN network roaming capabilities and allows users to change the WLAN terminal device
Simple security capability information exchange to enable flexible security architecture and to allow the usage of alternative authentication methods but at the same time maintaining the compatibility with the existing legacy devices
Compatibility with widely used Internet security framework to allow deployment of existing internet authentication servers for storing also 802.11 security keys
Slide 5

## Slide 6: User ID and Key Management
Device independent User ID is needed to allow the user to roam between various WLAN devices and use his/her global identifier for the authentication
Internet protocols already define a good widely deployed candidate for routable identifier, i.e. IETF Network Access Identifier (NAI) [RFC 2486].
It would be beneficial to utilize NAI also as the IEEE 802.11 user identifier.
  This would allow the operator to utilize existing Internet key servers for storing the WEP keys.
Slide 6

## Slide 7: Authentication
Negotiation mechanism is needed to support different authentication mechanisms
As an Example following authentication mechanisms could be included to the current Authentication message:
Slide 7

## Slide 8: Conclusions
A generic identity type like NAI should be used as a STA identifier to the network, and
The authentication procedure should include a security capability information exchange to allow future improvements and the use of new security methods.
Slide 8

## Slide 9: Annex -- Example Network Architecture Scenarios
Slide 10

## Slide 10: 1. Pre-shared key based authentication
Slide 11

## Slide 11
Slide 12

## Slide 12: 2 Authentication Center based authentication
Slide 13

## Slide 13
Slide 14