## Slide 1: A Brief Summary of Codec Tests for IS-95A, IS-95B and IS-2000
Steven D. Gray
Slide 1

## Slide 2: Motivation
Discussions in March meeting attempted to define performance requirements for voice lacency and error
Two primary methods exist for encoding speech
  Waveform encoding (i.e., ADPCM)
  Parametric endoding (i.e., CELP)
Data summaring performance of contest is presented
  8 new codecs
  Enhanced Variable Rate Codec (EVRC)
Codecs Mean Opinion Score (MOS) are rated for
  Frame loss rate
  Average rate of codec
Slide 2

## Slide 3: Summary
MOS score can range from 1 - 5
Extensive tests were conducted by COMSAT Labs1 in September 1999 on new codecs for IS-95 based CDMA
Assumptions
  Variable rate operation
    8, 4, 2 and 1 kbps source encoder rate
    20 ms framing of data
    Error detection of bad frames (i.e., CRC)
Average results for all codecs
MOS
1. Frank Corcoran, "SMV-Selection Test - Preliminary Test Results," 3GPP2-C11-20000425-023, Seattle
Washington, April 25 - 28, 2000.
Slide 3

## Slide 4: Conclusion
Codecs designed for wireless channels target a frame loss rate with error detection for bad frames at 1 %
  20 ms frames
  8 Kbps for full rate
Codecs not designed for wireless channels could suffer severe error propagation at 1% frame loss
Slide 4

## Slide 5: Final Note
End-to-end latency in IS-95A networks
  Mobile-to-fixed terminal is approximately 120 ms
  Mobile-to-mobile terminal is approximately 180 ms
5