## Slide 1: Proposed Application for HRbSG Technology: Wireless Home Area Networks

## Slide 2: Visions of the Present:
The Connected Home

## Slide 3: Consumer Device Connectivity Today
Consumer devices are now communicating with each other in the home
  PCs to PCs and peripherals
  Data Gateways to PCs
  Entertainment Gateways to Set Top Boxes
  Personal Electronics to PCs and peripherals
  Personal Electronics to TVs, VCRs and STBs
  Home Entertainment Units to each other
Wired connections: USB, 1394, Ethernet, Analog

## Slide 4: Visions of the Future:
The Wirelessly Networked Home

## Slide 5: Consumer Device Connectivity Tomorrow
All devices can and will communicate wirelessly
  No interconnection cables
All devices can be networked
  All can talk to each other
One single network in the home
  Flexible, scalable and full featured
Devices remain consumer devices
  Extremely easy to use
  Inexpensive wireless connectivity
DCT-2000

## Slide 6: The Wirelessly Home Area Network Application
Enable the wireless interconnection of electronic devices within the home
  Low and high speed throughput
  Real time and non-real time data
  Support prioritization and guaranteed bandwidth, latency
  Multiple simultaneous connections
  Enable coexistence, interoperability, coordination between all home devices
  Coexist and interoperate with “visiting” or legacy devices designed to other standards

## Slide 7: Why Networked?
Coordination mitigates the Train Wreck
  802.11b WLANs will enter the home this year
  802.15.3 multimedia apps target the home
  Wherefore wireless VOIP phones?
  Still have Bluetooth, HomeRF, 2.4 GHz cordless phone interferors
Networking is the logical extension of
  Necessary device coexistence
  Desirable device interoperability
Will not add much cost

## Slide 8: The General Application Idea
A “Wireless Network Coordinator” (WNC), acts as a home radio spectrum traffic cop
The WNC controls transmissions from all 802.11b and 802.15.3 devices in the home, assigning priorities and allocating bandwidth as needed
Devices associate and communicate directly with each other
Signaling may occur at data rates exceeding 40 Mbps, providing multiple simultaneous links
HRbSG rate scales down to 802.11b
  The WNC is an 802.11 point coordinator

## Slide 9: Application Requirements

## Slide 10: Application Requirements: System

## Slide 11: Application Requirements: PHY

## Slide 12: Application Requirements: MAC

## Slide 13: Summary
One single, fat wireless pipe to service home connectivity needs
Any and all gateway, computing, CE, and telephony devices share the pipe in harmony
The wireless connectivity needs to be robust, full featured and extremely easy to use
The wireless connectivity needs to coexist with legacy technology
The wireless connectivity needs to be inexpensive