## Slide 1: HIPERLAN type 2 – Data transport
Date: May 8, 2000
Author: Gunnar Rydnell Ericsson Address: S:t Sigfridsgatan 89, S-412 66 GÖTEBORG, SWEDEN
Phone: +46 31 344 6320
Fax: +46 31 344 60 33
e-Mail: gunnar.rydnell@erv.ericsson.se

## Slide 2: Contents
HIPERLAN/2 protocol stack
Convergence layer
Error Control (EC)
Medium Access Control (MAC)
Radio Link Control (RLC) sublayer
Radio Network Functions
QoS support
Considerations and Suggestion

## Slide 3: The HIPERLAN/2 protocol stack
the PHY layer on the bottom,
the DLC layer in the middle and
one or more convergence layers on top.
Notes: 1

## Slide 4: BRAN H/2 protocol stack in the AP

## Slide 5: Convergence layer
Multiple convergence layers for interworking with IP
Ethernet convergence layer have been finalised.
3rd generation core network, ATM, IEEE 1394 convergence layers are not finalised.

## Slide 6: The Convergence Layer main functions
Adapting service request from higher layers to the service offered by the DLC. Mapping of different traffic types onto the different radio bearers. Address and priority mapping.
Convert the higher layer packets with fixed or variable size into a fixed-size SDU that is used within the DLC (SAR).

## Slide 7: Mapping of a higher-layer packet onto the layers of HiperLAN/2

## Slide 8: Error Control (EC)
Detection and recovery from transmission errors on the radio link.
Ensures in-sequence delivery of data packets.
A dedicated EC instance is assigned to each DLC user connection.

## Slide 9: Error Control modes
1 The acknowledged mode using Selective-Repeat (SR) ARQ. SR is an efficient ARQ mechanism for wireless transmission.
2 The repetition mode with repeating the data-bearing DLC PDUs. No feedback channel is available.
3 The unacknowledged mode provides an unreliable, low latency transmission.

## Slide 10: Medium Access Control (MAC)
A dynamic TDMA/TDD scheme.
The MAC frame appears with a period of 2 ms.
The allocation of resources is controlled by an AP.
The MTs report their buffer states in Resource Request (RR) messages to the AP.
The AP allocates the resources according to the buffer states on a fair basis and, if required, taking quality of service parameters into account.
RRs and RGs are defined on a per-connection basis.

## Slide 11: Channels
The Broadcast CHannel (BCH) contains control information that is sent in every MAC frame, mainly to enable some RRC functions.
The Frame CHannel (FCH) contains an exact description on the allocation of resources within the current MAC frame.
The Access feedback CHannel (ACH) conveys information on previous random access attempts.
The Random access CHannel (RCH) contains contention slots for random access attempts.
Downlink or uplink phase consists of data to or from MTs.
Traffic from multiple connections to/from one MT could be multiplexed onto one so called PDU train, where each connection contains 54-octet LCHs for data and 9-octet SCHs for control messages.

## Slide 12: MAC frame structure

## Slide 13: Whenever a MT has data to transmit on a certain DLC connection:
It initially requests capacity by sending a Resource Request (RR) to the AP.
The RR contains the number of pending LCH PDUs that the MT currently has for the particular DLC connection.
The MT may use contention slots to send the RR message based on a slotted ALOHA scheme.
By varying the number of contention slots (Random access CHannels, RCHs), the AP may decrease the access delay.
If a collision occurs, the MT will be informed about it in the ACH in the next MAC frame. The MT will then back off a random number of access slots.

## Slide 14: After sending the RR to the AP
The MT goes into a contention free mode where the AP schedules the MT for transmission opportunities (both uplink and downlink).
The scheduling of resources is performed in the AP, i.e. a centralised controller is used, which enables efficient QoS support.
From time to time the AP may poll the MT for more information concerning the MTs current pending PDUs.
The MT may also inform the AP about the new status by sending a RR via the RCH.

## Slide 15: Radio Link Control (RLC) sublayer
1 Association Control function handles authentication, association/disassociation, key management, and encryption seed.
2 Radio Resource Control (RRC) handles MT alive/absent, dynamic frequency selection, handover, power saving and power control.
3 DLC User Connection Control setups and releases user connections, multicast and broadcast. Each connection has a unique support for Quality of Service (QoS). At the connection setup the MT receives a unique DLC address that corresponds to that DLC connection.
Notes: Thus, the RLC is used for exchanging data in the control plane between an AP and a MT, e.g., the MT associates to the AP via RLC signalling. After association the MT it can request for a dedicated control channel that is used to a DLC connection. The MT can request multiple DLC connections, and each connection has a unique support for Quality of Service (QoS) that is determined by the AP. The connection setup does not result in an immediate capacity assignment by the AP. At the connection setup the MT receives a unique DLC address that corresponds to that DLC connection.

## Slide 16: Radio Network Functions
The HIPERLAN/2 standard defines measurements and signalling to support a number of radio network functions, e.g. dynamic frequency selection, link adaptation, handover, multi beam antennas and power control.
The algorithms are vendor specific.
The radio network functions allow efficient cellular deployment of HIPERLAN/2 systems with full coverage and high data rates in a wide range of environments.

## Slide 17: Dynamic Frequency Selection (DFS)
The system shall automatically allocate frequencies to each AP for communication.
The frequency selection is based on interference measurements performed by the AP and its associated MTs.
Dynamic Frequency Selection (DFS), allows several operators to share the available spectrum and avoids the use of interfered frequencies.

## Slide 18: Link adaptation
Based on link quality measurements, the code rate and modulation scheme is adapted to the current link quality.
Link adaptation is used in both uplink and downlink.
The AP indicates in the FCH which PHY mode that is used.

## Slide 19: QoS support
Different radio bearers are setup to each MT and treated differently by the AP during the transmission.
The AP can select to use appropriate error control mode and detailed protocol settings for each mode.
The AP determines which radio bearers shall have access to the medium and also how much data and control signalling that is going to be sent in each MAC frame.
Very short access delay for real-time services can be accomplished by e.g. polling the MT.
The link adaptation and internal functions to avoid overload situations (admission, congestion and dropping mechanisms) are also additional means to support QoS.

## Slide 20: Considering
that the physical layer of Hiperlan2 and IEEE 802.11a are successfully harmonized.
that the DLC approach is still very different between the Hiperlan2 and IEEE 802.11a standards, to the extent that full harmonization of the standards is not practically achievable.
that the IEEE 802.11 has recognised the importance of Quality of Service management and real time service support for future Radio LAN applications.
that a standardisation activity is initiated to specify a QoS capable MAC within the 802.11 family.
that the Hiperlan2 DLC for Ethernet applications including QoS management in Ethernet environment is already finalised.

## Slide 21
that the Hiperlan2 DLC is from start designed to support both best effort service and QoS managed services.
that the so far discussed requirements on the IEEE 802.11 DLC are fulfilled by the Hiperlan2 DLC.
that there is an opportunity gain lead time in specification work and to reach full harmonisation between one of the standards in the IEEE 802.11 family and Hiperlan2.

## Slide 22: Suggests
That the IEEE 802.11 should consider adoption of the Hiperlan2 DLC for the 802.11e version of the standard.