## Slide 1
Wireless MAC Multimedia Extensions
Albert Banchs, Witold Pokorski
NEC Europe Ltd.
Markus Radimirsch
University of Hanover

## Slide 2: IEEE 802.11 MAC Extension
Underlaying idea:
  to meet the QoS requirements of the different traffic types: VoIP, multimedia, elastic traffic,…
Design goals:
  to provide a simple and efficient solution with full backwards compatibility
  to provide an easy migration path from existing 802.11 products
Proposed solution:
  to provide a new scheduling with little changes to the existing MAC protocol. This new scheduling, combined with admission control, will provide the QoS needed by the different traffic types.

## Slide 3: Types of traffic and their QoS
We distinguish two general types of QoS-demanding traffic:
requiring immediate delivery of the present packets (within some maximal burst size limit)
requiring specific bandwidth

## Slide 4: Classes of Service
Note that these traffic classes are like the ones identified in the Differentiated Service WG of the IETF.
Therefore three classes of service should be present:
Premium Service:
    low delay and low jitter guaranteed
Assured Service:
    bandwidth guaranteed
Best effort:
    present type of service

## Slide 5: Classes of Service (detailed)
Premium Service:
  whenever there is a packet belonging to the Premium Service, it is transmitted before any packet belonging to another service
  if there are several Premium Service packets, preferably the FIFO rule is applied
  admission control is needed in order to make sure that the Premium Service traffic does not exceed some upper limit
Assured Service:
  the average bandwidth is guaranteed
  there is no guarantee on delay (though, on average it is expected to be lower than for the best effort packets)
  admission control is needed in order to avoid blocking of Assured Services

## Slide 6: Premium Service Scheduling
The channel access of Premium Service packets is done after the PIFS, preventing any other traffic from using the channel first
Immediately after the PIFS, a specific contention resolution needs to take place in order to allow multiple terminals to use Premium Service
Candidate contention resolution schemes:
  Black Burst (Lucent)
  Exponential Backoff as in DCF (probably with smaller CWs due to lower numbers of competing stations)
  HIPERLAN Type I Scheme: Modified Elimination-Yield Non-Preemptive Multiple Access (EY-NPMA) – packets are transmitted according to their lifetime; good way to achieve FIFO

## Slide 7: Assured Service Scheduling in WLAN
  use of existing DCF mechanism with only small modifications consisting of different contention windows for different services.
  by decreasing the contention windows for high priority services (or increasing for low priority ones) we can adjust the bandwidth available for a given stream according to specific needs. The new CWs can be calculated either statically by some Admission Controller or adjusted by each station dynamically.
  admission control is needed in order to guarantee that no stations is flooding the channel

## Slide 8: CW determination
Goal:
  we want to adjust the CW of stations having Assured Service traffic, in order to achieve the required bandwidth
Approach:
  we are currently investigating two methods:
    static, where the admission controller is aware of the requirements of all the stations and calculates the necessary CWs
    dynamic, where each station monitors the traffic and adjusts its Contention Window

## Slide 9: Simulation and analytical results
- we use NS-2 to simulate the following setup:
  4 stations transmitting Assured Service traffic and 16 stations transmitting Best Effort traffic
  each station has always a packet to transmit
  we change the CWs in order to obtain the desired bandwidth for the Assured Service
- we look at:
  bandwidth available for each of the Assured Service stations
  total throughput
- we compare the results with an analytical model where we assume a geometric distribution for the backoff times.

## Slide 10: Assured Service Bandwidth
Series 1 – simulation results CW_Best_Effort
Series 2 – analytical model Priority = _____________________
CW_Assured_Service

## Slide 11: Assured Service Bandwidth (in kb)

## Slide 12: Total throughput (in kb)

## Slide 13: Protocol Operation
time
prev. transmission
PIFS
Time bounded service
Time bounded service specific contention resolution
PIFS
DIFS
Contention slots I
PIFS
DIFS
Contention slots II
Other priorit. service
Other service
SIFS
Ack
Ack
SIFS
Stations with smaller contention windows win more often and get higher bandwidth on average.

## Slide 14: Remarks
1) The proposed architecture makes the following configurations possible:
  Premium Service + Assured Service + Best Effort
  Assured Service + Best Effort: in this case we avoid redefining PCF
  Premium Service + Best Effort: DCF is used unchanged
  Best Effort: no changes at all to existing products
2) The most logical place to do the admission control is probably at the Access Point (as suggested by Microsoft)

## Slide 15: Conclusions
the scheme is simple and requires only small changes to the existing standard
  it is a distributed scheme, therefore simple MAC internal scheduling needed
  can probably be implemented into existing products, i.e. the effort for new product development is very low
it can interoperate with the standard MAC
it distinguishes between two different classes of service: delay critical and bandwidth critical.
it provides soft QoS guarantees which is compatible to the scheme used in the backbone network