## Slide 1: Regulatory Update
HomeRF Petition to FCC (Nov. 1998)
  HomeRF requests 3 MHz and 5 MHz FHSS channels
  Proposed parameters
    3 MHz Channels
      20 Hz hop rate
      75 channels (overlapped)
      330 mW Tx power limit
    5 MHz Channels
      50 Hz hop rate
      75 channels (overlapped)
      200 mW Tx power limit

## Slide 2: Regulatory Update
FCC NPRM 99-231 (June 1999)
  FCC Proposes 3 MHz and 5 MHz FHSS channels
  Proposed parameters
    3 MHz Channels
      20 Hz hop rate
      75 channels (overlapped)
      330 mW Tx power limit
    5 MHz Channels
      50 Hz hop rate
      75 channels (overlapped)
      200 mW Tx power limit

## Slide 3: Regulatory Update
Period for Public Comment (closed 10/4/99)
Reply Comments (closed 11/19/99)
Ex parte Comments (ongoing)
Progress
  faster mandatory hop rate dropped
    faster hopping increases interference to other users
  overlapping channels dropped
    overlapping channels increases FHSS collision rate and severity

## Slide 4: Regulatory Update
Proxim Compromise (March ‘00)
  3 MHz channels
    2.5 Hz hop rate (minimum)
    330 mW tx power limit
    non-overlapping channels
    radios must span >75 MHz total BW
  5 MHz channels
    2.5 Hz hop rate (minimum)
    200 mW tx power limit
    non-overlapping channels
    radios must span >75 MHz total BW

## Slide 5: Regulatory Update
WECA Compromise (4/10/00)
  20 non-overlapping channels
    consistent with ETS 300 328
  2.5 Hz minimum hop rate
  60 mW power limit
    practical antenna gain is at least 1.5 - 2 dB (maybe more)
    approximately 100 mW EIRP
    consistent with ETS 300 328
    consistent with FCC ruling in 915 MHz proceeding
      FHSS power was reduced in proportion to square of reduction in minimum number of hopping channels

## Slide 6: Regulatory Update
WECA Compromise (4/10/00) - cont’d
  No minimum coverage requirement
    radios must use minimum of 20 channels
    total spectral coverage > (20 x channel width)
    No minimum channel width
      e.g. Bluetooth radios could qualify under WBFH rules
    FHSS and DSSS radios would not be required to collide
    *** MAJOR IMPLICATIONS FOR IEEE 802.15 ***
  WBFH Receiver Test
    FM receivers highly susceptible to ACI
    establish minimum ACI requirements for WBFH devices
    Fewer channels drives need for reasonable ACI performance

## Slide 7: Regulatory Update
What’s Next?
  Procedure
    OET drafts recommendation
    Recommendation is sent to Commissioners for review
    Commissioners can either:
      a.) Approve
      b.) Send it back down to OET for further consideration
  Timing
    OET is at or very near completion of draft
      draft could go to Commissioners within a few days, or at most, a few weeks
    Commissioners usually take 4 - 6 weeks to approve
  OET draft probably in late stages of Commissioner’s review by July meeting.