## Slide 1: Response to the UK-RA Strawman proposal for the use of RLANs in the 5 GHz band
Copyright, 1996 © Dale Carnegie & Associates, Inc.
From IEEE 802.11
Standards Working Group for Wireless Local Area Networks
and IEEE 802.15,
Standards Working Group for Wireless Personal Area Networks
Presented by Vic Hayes, Ombudsman for Regulatory affairs of IEEE 802

## Slide 2: Congratelutions!
IEEE 802.11 and IEEE 802.15 applauds the initiative of the UK-RA to change the situation in the 5 GHz band
  from an unused allocation
  into one which will shortly bring high data rates in the hands of the work force, educational institutes, the traveler and the home
It could only be improved by adoption throughout Europe

## Slide 3: 100 MHz Spectrum available for 8 + 2 years…. unused
Yet, the Strawman allocates 100 MHz uniquely to HIPERLAN/1 for another 2 years
For what usage? Search on the internet:
  one announcement for a product in April 1999
    no product yet
  one website: HIPERLAN/1 alliance
    evidence of a single meeting in May 1999

## Slide 4: Observations supporting removal of HIPERLAN/1
Spectrum is not used for 8 years
  In 1992 Spectrum was assigned for HIPERLAN (Recommendation T/R 22-06, Madrid 992).
  The standard was published October 1996 as ETS 300 652.
Standard is available for about 4 years, no products are available yet

## Slide 5: Observations supporting removal of HIPERLAN/1
No products on the market
  April 1999 one company announced HIPERLAN/1 product
  To date there is still no product actually available
  There is a single page website with HIPERLAN1 as title. No products mentioned.
Is it really required to reserve 100 MHz of spectrum for another 2 years?

## Slide 6: Conclusion for 5150-5250 MHz band
HIPERLAN Type 1 support is a continued under-utilization of spectrum.
802.11 supports addition of 802.11a and HIPERLAN type 2, but to remove HIPERLAN type 1

## Slide 7: Sugestion 1
Remove “HIPERLAN/1” from the 5150-5250 MHz

## Slide 8: Proposal to discontinue HIPERLAN/0
Support from IEEE 802.11 provided:
  The use of the spectrum is under some level of control to protect against interference from non-high-data-rate applications.
  This could be done by limiting the use to devices conforming to recognised standards, with a clear scope of high data rates such as HIPERLAN/2, 802.11, and so on

## Slide 9: Recommendation 2
Add ”HIPERLAN/2 and IEEE 802.11a” devices to the allocation of the 5150-5250 MHz
Do a regular review if more standards have met certain requirements

## Slide 10: Licensed Spectrum?
Agree with the considerata
Agree with the need for licensed spectrum
But not in the 455 MHz allocated to HIPERLAN/2 and 802.11a
  removal of the spectrum from the license exempt use will result in unacceptable performance and thus capacity degrades
  Note that the 455 MHz does include spectrum used by radars.
    A typical wideband radar used more than 100 MHz
  HIPERACCESS is a typical licensed band application
  has been moved outside the 5 GHz range

## Slide 11: Conserve spectrum for license exempt
  High data rates require a large signal margin and this in turn limits the tolerance for interference – including interference from the same system.
  For example, the re-use factor for the 54 Mb/s mode range is 67 – which means that 67 channels are needed to achieve the full 54 Mb/s on each channel in an arbitrarily large system
  If there are fewer channels the interference among channels will be larger and the maximum data rate can not be achieved

## Slide 12: Conserve spectrum for license exempt
  Therefore a large number of channels is needed to assure adequate capacity in high density systems
  The current 18 channels are about enough for most situations but we are at the cusp of the performance curve and further reduction will result in unacceptable performance. NOTE: HIPERLANs have always been positioned as user owned and operated.

## Slide 13: Conserve spectrum for license exempt
band partitioning is per definition wasteful - notably in short range systems like wireless LANs:
  in many cases, the “licensed“ spectrum would go unused even though there is an operator in sight.
  the places where an operator may want to provide services is not necessarily one where the private use is very dense. So, partitioning for these reasons leads to unused spectrum

## Slide 14: Alternative to licensed service
A better way may be found to give service providers some priority to use certain channels – for instance by allowing them NOT to employ DFS (whereas user owned and operated systems would be required to employ DFS)

## Slide 15: Recommendation 2
Allocate the entire band 5470-5725 MHz to licensed exempt
Consider to exempt service providers from the requirement to use DFS for certain channels

## Slide 16: Summary
Suggest removal of “HIPERLAN/1” from the 5150-5250 MHz band
Add ”HIPERLAN/2 and IEEE 802.11a” devices to the allocation of the 5150-5250 MHz
Do a regular review if more standards have met certain requirements
Allocate the entire 5470-5725 MHz band to licensed exempt

## Slide 17: Proposed Band plan