## Slide 1: 802.11 PCF Enhancements and Contention Free Bursts
Maarten Hoeben
NoWires Needed

## Slide 2: Introduction
NWN’s suggestions for MAC enhancements
  PCF based
    NWN actually implements PCF in their products
    Efficient and versatile platform
    However, some problems that need to be solved
  Focused integration with IETF integration
    Integrated Services over Specific Link Layers (ISSLL)
    802.1(p) priorities

## Slide 3: 802.1(p) Priorities
Standardized SAP between MAC and LLC
  8 priorities
  Subsets possible
  Used in 802.3
  Supported by IETF through ISSLL
  Supported by dominant OSs

## Slide 4: DCF and PCF (1)
2 access mechanisms: DCF and PCF
  Strength/weakness analysis
    DCF works well under low load situations, PCF works optimal under high load conditions
    DCF works better in networks were BSSs overlap, PCF is ideally suited for networks were BSSs are carefully planned not to overlap
    DCF has a relatively low implementation complexity, PCF is (said to be) complex to implement

## Slide 5: DCF and PCF (2)
  Strength/weakness analysis (continued)
    DCF does not allow explicit access control, PCF does
    DCF efficiency drops considerably in densely populated BSSs, PCF has no scaling problem
    DCF supports legacy stations, PCF only to some extend
The PCF weaknesses prevented vendors from implementing the PCF
  New interest because of QoS

## Slide 6: DCF and PCF (3)
Proposals focus either on DCF or PCF
  Better to approach it as an integrated system
    The CFP can only be sustained if the queues on the access point or stations are adequately backlogged
    Chicken-egg problem; polled to have medium access – medium access to get on polling list
    Some regulatory domains do not allow constant medium occupancy by one device
    Support of legacy devices may require an enhanced DCF
Systems always spend some time in the DCF

## Slide 7: DCF and PCF (4)
Simulations show gab between DCF and PCF performance
  Average loaded systems spend half of their time in DCF, half in PCF
  The service provided by the system should be linear throughout load profile

## Slide 8: This Proposal
Focus on PCF
  The ability of full medium control
  Optimal medium efficiency
  Not suffering from scalability problems
Solution for gab between DCF and PCF
  Performance
  Characteristics
No suggestions for DCF enhancements

## Slide 9: Requirements
Use 802.1p priorities
Use the 802.11 MAC PCF
  Solve the overlapping BSS problem
  Interaction between DCF and PCF
Backward-compatibility with legacy devices
  Use the currently existing frame formats
  Don’t rely too heavily on new mechanisms
Keep implementation complexity low

## Slide 10: PCF Deficiencies
Two issues limit the use of the PCF for QoS
  Section 9.3.4 and specifically clause 9.3.4.1 imposes strict rules upon the order in which stations are addressed or polled
  There is no mechanism (other than the More-Data bit) that allows a station to communicate its queue state(s) to the PC

## Slide 11: PCF Enhancements
Remove order rules
Use Duration/ID field for signaling
  Signal priority
  Tx time of next frame
    Preamble time + frame size / bitrate
  Piggy-backed on each To-DS frame
  PC can explicitly poll for update by sending Null frames

## Slide 12: Contention Free Bursts (CFBs)
CFBs solve following PCF problems
  Sustained CFP under average load conditions
  Overlapping BSSs problem
Current CFP needs to be one uninterrupted sequence of frames
CFBs solve this because
  Allows the PC to relinquish medium control to other BSSs in the same area
  PC can temporarily give-up medium control and defer control until new frames are available for transmission

## Slide 13: Enhanced CFP
Section 9.3.3 transfer procedures apply within CFB
CFBs have a maximum duration of CFBMaxDuration
The remaining duration is encoded in all From-DS data frames
Backoff procedure between CFBs
CFP
Beacon Period
Beacon or CF-End
Contention Free Burst
CP
CFB Backoff

## Slide 14: Contention between PCs
Remove restriction of NAV settings based on CFPDurRemaing in Beacon for APs
APs contend to start a CFB
  Legacy APs and stations don’t interfere because CF-conformance
  CFBs are protected through duration field in From-DS frames
CFP
Beacon or CF-End
Contention Free Burst
CFB Backoff
deferred backoff
CFP
BSS 1
BSS 2
CP

## Slide 15: Overlapping BSS Scenarios (1)
AP-1
AP-2
STA-1
CFBs work very well in situations where BSSs overlap and PCs are in range of each other

## Slide 16: Overlapping BSS Scenarios (2)
AP-1
AP-2
STA-1
STA-2
CFBs may suffer from the same problems as the DCF in hidden node situations
  Use RTS/CTS mechanism
  Use regular NAV in RTS/CTS frames
    Can be used by other PC to relinquish medium control

## Slide 17: Conclusions and Recommendations
Simple but efficient
  Easy to implement
  Good support for legacy stations
  Inline with what is standardized by other workgroups and standardization bodies
  Allow differentiation
DCF enhancements welcome addition
Simulations will prove concept
Some ‘loose-ends’ need to be worked-out