## Slide 1: Answer to QoS Questions
Amar Ghori
Steven Gray
Evan Green
Raju Gubbi
Maarten Hoeben
Greg Parks
Menzo Wentink

## Slide 2: Some Questions
What is QoS?
  Is it an action, behavior, or something else?
  Answer:
  In the simplest sense, Quality of Service (QoS) means providing consistent, predictable data delivery service1.
  There are a number of characteristics that qualify QoS1:
    minimizing delivery delay
    minimizing delay variations
    providing consistent data throughput capacity
  1. http://www.qosforum.com/about_background.htm

## Slide 3: Some Questions (cont.)
How is QoS measured?
  Can it be measured?
  Answer:QoS is measured by2:
    delivery delay (latency)
    delay variations (jitter)
    data throughput capacity (bandwidth)
    loss (frame loss)
  2. Microsoft Corp, "An overview of QoS", microsoft.com/technet/win2000/win2ksrv/technote/qosover.asp

## Slide 4: Some Questions (cont.)
What SAP primitives are used to request/control QoS?
  What protocols are on the other side of this SAP?
  Answer: traffic handling mechanisms include:
    802.1p
    Integrated services(intserv)
    UNI signaling

## Slide 5: Some Questions (cont.)
  What are the parameters that cross this SAP?
  Answer: the required parameters are dependant upon the protocols discussed in the previous question and the implementation of the QoS protocol at the MAC layer
How would current IETF developments work with this SAP?
  Integrated Services?
  Answer: support for intserv should be required of any QoS proposal.
  Differentiated Services?
  Answer: diffserv is currently focused on the core network elements. Currently, diffserv is not defined for operation over IEEE802 networks and should not be a requirement for QoS in the MAC.

## Slide 6: Some Questions
What upper layer protocols support/require QoS from the Data Link/MAC layer?
Answer: Signaling protocols (e.g., RSVP) needs DLC layer information for admission control and signaling concerning available resources. Priority specification (e.g., 802.1p) needs queuing and priority mechanisms in the MAC.
What about 802.1p?
Answer: Yes, see above

## Slide 7: Some Questions
How is QoS supported by existing OS APIs?
Answer: Windows 2000, NT server supports RSVP and 802.1p
What OS APIs are proposed to be added to support QoS at the MAC layer?
Answer: Windows2000 already has the required APIs.
  Who are we expecting to add these APIs?
    OS vendors?
    802.11 developers?
  Answer: See above for OSs currently supporting QoS

## Slide 8: Some Requirements
How can alternative proposals be evaluated?
  No simulation data
  No definitive impact statement on existing equipment
  No apparent demand for QoS in LAN space, let alone WLAN
  No defined interfaces
  What RFCs require/support the proposed services?
  What is the mapping to upper layer protocols?
  What are the concrete benefits provided by the proposed services?
Answer: A requirements document will address requirements. IEEE802.11-00/008r3 functional requirements section addresses some of these requirements.