## Slide 1: Channel Model Proposal for 802.11e MAC Simulations
Sunghyun Choi
Philips Research
Briarcliff Manor, New York

## Slide 2: Introduction
Don’t like to include the complicated PHY behavior for MAC simulations
Still need to incorporate the PHY behavior for MAC evaluation
  Error-free PHY assumption is too much
  Random error assumption does not reflect the reality
Two-state Markov channel model?
  Well accepted model for link layer evaluations
  Reflects the bursty error behavior of the wireless channel

## Slide 3: Two-State Markov Model
Two bit error probabilities:
  Pe,G (in good state)and Pe,B (in bad state)
Four transition probabilities (or rates in sec-1)
  PG,B, PG,G (= 1-PG,B), PB,G , PB,B (= 1-PB,G )
Stays in each state for an exponentially-distributed time

## Slide 4: Two Extreme Cases
Bursty error model
  Pe,G = 0 and Pe,B = 1
  Pkt 1 received in error / Pkt 2 received correctly
Random error model
  Start in Bad state and PB,G = 0

## Slide 5: Other Concerns
A channel behavior determined for each transmitter-receiver pair due to location-dependent channel behavior
  E.g., at time t, channel (STA A, STA B) in bad state while channel (STA B, STA C) in good state
  Can assume that channels (STA A, STA B) and (STA B, STA C) are independent for simulations
Realistic values of the probabilities?
  May want to ask the folks working in PHY in 802.11 WG