## Slide 1: Proposal for Extensible Security
Standardizing for Change
Bob O’Hara
Albert Young
Dan Nessett
Bofu Chen
Bruce Kendall

## Slide 2: Standardize for Change
Standardize a mechanism based on negotiation, rather than fixed requirements in the standard
Allow for ongoing adaptability and innovation
Provide processes that encourage/enforce exchange of information
Provide one (or two) starting points using the new mechanism

## Slide 3: Extensible Security
Optional enhancement of security for 802.11 devices
Three frames exchanged during negotiation
  Precedes actual authentication, but is part of authentication frame exchange
  Authentication fails unless successful security negotiation is completed

## Slide 4: Negotiation Frames
Frame 1 (requester to responder)
  Identity assertion
  Request for authentication (algorithm = 2)
Frame 2 (responder to requester)
  Identity assertion
  List of acceptable algorithms
Frame 3 (requester to responder)
  List of accepted algorithms

## Slide 5: Negotiated Algorithms
Key validity period
Authentication
Privacy
Key establishment
Message authentication
Sub-key derivation

## Slide 6: Security Negotiation Information Element
Element ID
Length
Key Validity Period
Registering OUI A (2)
Registering OUI A (1)
Registering OUI A (0)
Indicator A
Authentication Algorithm
Registering OUI P (2)
Registering OUI P (1)
Registering OUI P (0)
Indicator P
Privacy Algorithm
Registering OUI K (2)
Registering OUI K (1)
Registering OUI K (0)
Indicator K
Key Establishment Algorithm
Registering OUI M (2)
Registering OUI M (1)
Registering OUI M (0)
Indicator M
Message Authentication Algorithm
Registering OUI S (2)
Registering OUI S (1)
Registering OUI S (0)
Indicator S
Sub-key Derivation Algorithm
…

## Slide 7: Indicator Format
Bit 7: Preferred
Bit 6: Deprecated
Bit 5: Reserved
Bit 4: Authentication
Bit 3: Privacy
Bit 2: Key Establishment
Bit 1: Message Integrity
Bit 0: Sub-key Derivation

## Slide 8: Information Element Details
Responder sends
  Maximum acceptable key validity period
  All acceptable algorithms, at least one of each type
  May mark algorithms “preferred” and “deprecated”
Requester sends
  Key validity period no greater than that sent by responder
  List of accepted algorithms, only one of each type

## Slide 9: Success or Failure
At each step of the negotiation, success or failure is indicated in the status code field
  Just as in current authentication exchange
  Responder can refuse to use negotiated security in frame 2
  Requester can refuse the offered algorithms in frame 3 (if one or more of the algorithm types does not have an acceptable choice)
  Responder can refuse requester’s choices in the first frame of the subsequent authentication handshake (frame 4)

## Slide 10: Merits of Flexibility
Vendors can adapt quickly to changes in the security environment
The standard does not need to be changed for this reason in the future
The market can select the “correct” algorithms
Encourages both competition and interoperability within the scope of the standard

## Slide 11: Effects of Extensible Security
Inserts the negotiation before authentication exchange
  First authentication frame stays the same
  Adds new algorithm number for extensible security
Changes basic format of Authentication frame
  Adds new information element to second and third authentication frames
Allows independence of choice for all algorithms
Provides significantly greater identifier space
  Algorithm values are assigned independently to each OUI

## Slide 12: Recommendation
Adopt the text in document 00/163 to define the Extensible Security algorithm, frame exchanges and Security Negotiation information element
Define a registration procedure
  Registrant must have an IEEE-assigned OUI
  Complete algorithm and handshake protocol details must be provided, including external references (if any)
  In exchange for providing registration services, IEEE gets right to publish details (preferably on web site)
Include a pointer to the registration web site in the standard

## Slide 13: Registration Requirements
Define a registration process that allows anyone to petition the IEEE for a new value to be used in this field
  Exactly the same as the process used for OUI and Ethertype registration
    See http://standards.ieee.org/regauth/oui/index.shtml and http://standards.ieee.org/regauth/ethertype/index.html
Require full disclosure of information to enable multi-vendor interoperability

## Slide 14: Procedural Stuff
Write a proposal to IEEE Registration Authority Committee
  What is to be registered?
  Why should it be registered?
  What special procedures are needed?
Next RAC meeting is at this plenary
Work with IEEE staff to implement the procedures

## Slide 15: Additional Recommendations
Select one (or no more than two) algorithms for each algorithm type
  Register the algorithms
  Publish the registration information (OUI and algorithm number) in the standard
Require that the selected algorithms be implemented if the negotiated security option is implemented
  This provides an immediate base for interoperability

## Slide 16: Work To Be Done
Identify algorithms to be included in the standard
Add PICS update
Is there MIB stuff needed?