## Slide 1: Perspective on the QoS Problem
Keith Amann, Spectralink
Peter Ecclesine, Cisco
David Halasz, Cisco
Duncan Kitchin, Intel
Bob O’Hara, 3Com
TK Tan, 3Com
Steve Williams, Intel
Albert Young, 3Com

## Slide 2: Scope of the Problem
There is no “toll quality” in an ISM band
  Toll quality implies protected spectrum, professional installation
  Applying apparatus from a 10e-12 world to 10e-5 world is not worthwhile

## Slide 3: The Problem Must Drive the Solution
The Service Access Point (SAP) must be defined within the scope of 802 standards
  802.1D (802.1p) priorities
  802.2 LLC
  Interfaces direct to higher layers are not permitted by the 802 architecture

## Slide 4: The Problem Must Drive the Solution
The realities of the medium must be accepted
  Delivering “toll quality” on an unlicensed wireless channel is a pipe dream
  Applying mechanisms from an environment of 10e-12 BER to an environment of 10e-5 BER (or greater) is not a good engineering solution
Functions of higher layer protocols must not be duplicated in the MAC
  Higher layers already provide scheduling and admission control, duplicating these services is not required in the MAC (see last slide for a partial list of standards)

## Slide 5: The Problem Must Drive the Solution
The solution must scale to larger environments
  802.11e must operate with any 802.11 PHY
  Simple solutions are more easily scaled up to support greater loads and higher rates
    802.11a 54 Mbps
    802.11g(?) 20+ Mbps
    Future 100+ Mbps

## Slide 6: The Problem
The requirements document (00/137) states the problem to be solved
The requirements in that document should reflect the realities stated in this presentation
The disconnect between the requirements document and reality must be corrected
00/137 is currently the result of brainstorming sessions, i.e., no review of the content has been done (mostly)
  The first attempt at critical review resulted in 2 hours of discussion with no progress
  Indicates there is great distance between participants idea of the problem to be solved in the union of telecom and datacom

## Slide 7: Necessary Steps
Critically review the content of 00/137
  Reduce the result of the brainstorming sessions to a reasonable list of requirements
    See Bob O’Hara’s email to the 802.11 reflector of June 23, “Comments on the Proposed TGe Requirements”
      The requirements must not assume the form of the solution (peer to peer communication, support for error correction, support for overlapping BSS operation, provide redundancy of point coordinators, support for multiple priorities and QoS levels)
  Keep a firm grasp on limiting the task of the MAC to what is necessary
  Eliminate duplication of higher layer functions

## Slide 8: Higher Layer Standards
rfc1889 - RTP A Transport Protocol for Real-Time Applications
rfc2205 Resource ReSerVation Protocol (RSVP) -- Version 1 Functional Specification
rfc2210 The Use of RSVP with IETF Integrated Services
rfc2211 Specification of the Controlled-Load Network Element Service
rfc2212 Specification of Guaranteed Quality of Service
rfc2213 - Integrated Services Management Information Base using SMIv2
rfc2214 - Integrated Services Management Information Base Guaranteed Service Extensions using SMIv2
rfc2215 General Characterization Parameters for Integrated Service Network Elements

## Slide 9: Higher Layer Standards
rfc2216 - Network Element Service Specification Template
rfc2326 - Real Time Streaming Protocol (RTSP)
rfc2327 - SDP Session Description Protocol
rfc2474 - Definition of the Differentiated Services Field (DS Field) in the IPv4 and IPv6 Headers
rfc2475 - An Architecture for Differentiated Services
rfc2543 - SIP Session Initiation Protocol
rfc2597 - Assured Forwarding PHB Group
rfc2598 - An Expedited Forwarding PHB
rfc2705 - Media Gateway Control Protocol (MGCP) Version 1.0
rfc2814 - SBM (Subnet Bandwidth Manager) A Protocol for RSVP-based Admission Control over IEEE 802-style networks
rfc2815 - Integrated Service Mappings on IEEE 802 Networks

## Slide 10: Higher Layer Draft Standards
draft-ietf-issll-is802-framework-07 A Framework for Providing Integrated Services Over Shared and Switched IEEE 802 LAN Technologies