## Slide 1: A Proposal for IEEE 802.11e Security
IEEE 802.11 Task Group E July 2000 meeting
Prasad, Anand aprasad1@lucent.com
Raji, Alex araji@lucent.com

## Slide 2: Objectives
Improve network security capabilities
  Critical for business, home and Internet applications
Assure alignment with IETF
Improve Encryption scheme
Assure backward compatibility with the current standard

## Slide 3: Overview of 802.11 Security Vulnerabilities*
Compromise of encryption key
Theft of hardware is equivalent to theft of key
Packet spoofing, disassociation attack
Rogue AP
Known plain-text attack
Brute force attack
Passive monitoring
Replay attack
* Derived from Microsoft paper: IEEE 802.11-00/034r1

## Slide 4: Proposed 802.11 Security Solutions
Flexible/extensible security architecture with backward compatibility
Hardware as well as user authentication
Key management with support for per station/per session encryption key
Mutual authentication (defense against rogue AP)
Option to use other/better encryption algorithms
Per packet authentication (defense against replay attack and packet spoofing)

## Slide 5: Security Proposal Highlights
Enhanced encryption key exchange
  Support public key exchange (Diffie-Hellman)
  Improve WEP key distribution/management
Enhanced authentication
  Support user as well as machine authentication options
  Support extensible authentication protocol (EAP) over wireless with multi-protocol support akin to 802.1x
  Support for certificate authentication of hardware
Enhanced privacy algorithms
  Choice of packet authentication and/or encryption (AH, ESP)
  Add anti-replay measures (sequence #)
  Support multiple encryption algorithms

## Slide 6: 802.11e Dynamic Key Exchange

## Slide 7: Key Exchange Parameters
Support both shared key (WEP) and public key
Support infrastructure as well as ad-hoc modes
Backward compatibility with 802.11b
Address rogue AP vulnerability
Flexibility to negotiate a variety of security schemes
Adhere to known and trusted security industry practices
Assume a short key life
Negotiate a single encrypted tunnel per station

## Slide 8: Proposed Methodology for Key Exchange
Use internet key exchange (IKE, RFC 2409) standard as a model
Exchange keys ASAP to establish a secure tunnel (prior to association)
Overload KE messages over authentication frames
Link key exchange phase to the subsequent phases to prevent session hijacking
Provide a mechanism for protocol negotiation for later phases (Authentication and Privacy protocols)

## Slide 9: Advantages Public Key Exchange
Addresses the following vulnerabilities
  Compromise of the encryption key (each session has a new key)
  Rogue AP (via X.509 certificate authentication of the AP)
  Password cracking (allows encrypted session to be established before authentication)
Diffie-Hellman public key algorithm
  Well defined negotiation of a secret key between the end points
  Eliminates shared key requirement, simplifies management
Supports X.509 certificates
  Integrated one-way or two-way certificate authentication

## Slide 10: Public Key Exchange Requirements
Need a good pseudo random number generator
  Use MD5(x,y) or SHA(x,y) one-way hashing function
Ability to calculate exponential modulus of large numbers
  Gx MOD p where p is 768 or 1024 bits long
  Similar to me MOD n for RSA calculations
Ability to verify certificate digital signatures
  Digital signature standard verification (NIST FIP-186)
    Requires SHA(x,y), g-1 MOD p, and gx MOD p calculation
  RSA signature verification
    Requires SHA(x,y), and me MOD n calculation

## Slide 11: Example Key Exchange
Initiator
Responder
Proposal values, Key (g^x), IDi, Noncei
Selected proposal, Key (g^y), IDr, Noncer, Hashr
Hashi
Skey = Hash(Noncei+Noncer+g^xy)
g^xy = (g^x)^y MOD p
Hashr = Hash(g^xy+IDi+IDr+g^x+g^y+Noncei+Noncer)
Hashi = Hash(g^xy+IDr+IDi+g^y + g^x +Noncer+Noncei)
g^xy = (g^y)^x MOD p
Skey = Hash(Noncei+Noncer+g^xy)

## Slide 12: Example Key Exchange + Certificate Authentication
Initiator
Responder
Proposal, Key (g^x), IDi, Certificate Req, Noncei
Proposal, Certificate[BSSID,g^y,Signature], IDr, Noncer, Hashr
Hashi
Skey = Hash(Noncei+Noncer+g^xy)
Skey = Hash(Noncei+Noncer+g^xy)
Verify certificate signature

## Slide 13: Example Key Distribution (WEP)
Initiator
Responder
Proposal, Key (g^x), IDi, Noncei
Proposal, Key (g^y), IDr, Noncer, Hashr
Hashi
[Session key]Skey
Skey = Hash(Noncei+Noncer+g^xy)
Skey = Hash(Noncei+Noncer+g^xy)
RC4(Session key, Skey)
RC4(Session key, Skey)

## Slide 14: 802.11e Enhanced Authentication

## Slide 15: Enhanced Authentication Parameters
Support User and Machine level authentication
Support emerging 802.1x standard
Flexibility to support multiple authentication protocols (PAP, CHAP, etc.)
Compatible with popular AAA systems such as RADIUS
Compatibility with PKI and Certificate authentication
Authentication process itself must be secure

## Slide 16: 802.1x draft standard (EAPOL)
Extensible Authentication Protocol (EAP; RFC 2284) is a general protocol for PPP authentication
  EAPOL is adopted by IEEE 802.1x as an authentication mechanism for network port access control.
  EAPOL supports multiple authentication mechanisms.
The IEEE draft P802.1X/D5 describes the use of EAPOL in Port based Network Access Control in IEEE 802.11 wireless LAN infrastructures.
EAPOL communication occurs in an unsecured shared environment, so it is vulnerable to attack.

## Slide 17: Proposed Authentication Methodology
Negotiate a secret key prior to station authentication step to create a secure encrypted tunnel.
Negotiate a single authentication methodology (PAP, CHAP, etc.) during the key exchange process.
Use EAPOL as defined in IEEE 802.1x, only after the secure tunnel is established.
Authentication Number Field of Authentication Frame is used to identify the EAPOL protocol vs the legacy Shared Key or Open System.

## Slide 18: EAP Over Wireless LAN (EAPOWL)
Addresses the following vulnerabilities
  Theft of hardware enables unauthorized access
  Access control (enables user based authentication and filtering)
  Password cracking (provides the ability to limit the number of failures)
Provides additional benefits
  Enables tracking of lost/stolen hardware by logging the card MAC address while authenticating

## Slide 19: 802.11e Enhanced Privacy

## Slide 20: Enhanced Privacy Protocol Parameters
Support multiple encryption algorithms (DES, 3DES, etc.)
Support key per session
Backward compatibility with WEP/RC4
Support frame Authentication as well as Encryption
Include defense against replay attacks
Include defense against packet spoofing

## Slide 21: Proposed Enhanced Privacy
Use IPSec standard as a model (RFC 1826, 1827)
Negotiate a single packet security and privacy protocol for each station MAC address during the key exchange process.
Packet layout is the same as WEP except
  IV field could also become a 4 byte sequence number
  ICV field could also become the payload hash value
Optionally add authentication field to 802.11 control and management packets
Support WEP, as well as other encryption algorithms.

## Slide 22: Enhanced Privacy Packet Format
WEP encryption format
Enhanced privacy encryption format

## Slide 23: Enhanced Privacy Protocol Advantages
Addresses the following vulnerabilities
  Packet spoofing via frame authentication field
  Known plaintext attack via block cipher algorithms
  Brute force attack via longer keys / better encryption algorithms
  Passive monitoring via packet encapsulation
  Disassociation attack via control frame authentication field
  Replay attack via integrated sequence number field

## Slide 24: Comparing WEP to Enhanced Security Proposal
* Longer RC4 keys