## Slide 1: OFDM in the 2.4 GHz Band
Jan Boer, Lucent Technologies

## Slide 2: Why OFDM in 2.4 GHz
Standard is developing fast:
  2 Mbit/s in 1997
  11 Mbit/s in 1999
  PAR for >20 Mbit/s in 2000
What is next; can we go higher?
Yes; OFDM as specified in 802.11a can go up to 54 Mbit/s
  also in the 2.4 GHz band

## Slide 3: How?
Adopt 802.11a for higher rate in 2.4 GHz
Fully specified for 6, 12, 18, 24, 36, 48, 54 Mbit/s
Maintain 802.11b specifics:
  802.11b channelization scheme
  802.11b slottimes and SIFS (20 resp. 10 s)
Modify/adapt headers for 802.11b interoperability and coexistence

## Slide 4: Interoperability
802.11b is part of the higher rate standard:
  1 and 2 Mbit/s Barker
  5.5 and 11 Mbit/s CCK (+ optional PBCC)
  long and (mandatory?) short preamble
Higher rate falls back to 802.11b for interoperability
For coexistence the original OFDM header is preceded by a Barker based preamble:

## Slide 5: OFDM Header adaption 1
802.11b long preamble + header (192 s) followed by OFDM preamble
  Mandatory
  Receiver trains on preamble and detects content of header; changes to OFDM mode
  no coexistence issues (length field detected)
Drawback: overhead

## Slide 6: OFDM Header adaption 2
802.11b short preamble (96 s) followed by OFDM preamble
  Mandatory
  Receiver trains on preamble and interprets content of header; changes to OFDM mode
  no coexistence issues with 802.11b
    length field detected only by receivers capable of handling short preamble; all 802.11b receivers must cope with the short preamble by keeping medium busy high during the frame
Drawback: again overhead

## Slide 7: OFDM Header adaptation 3
30-40 s Barker preamble followed by OFDM preamble
  Any receiver does carrier detect on Barker preamble part
  Start of OFDM preamble to be detected and change to OFDM mode
  no coexistence issue
    All 802.11b radio's should cope with this signal in the same way as 802.11b radio's that do not support the short preamble
Minimal overhead

## Slide 8: OFDM channelization
802.11b channelization can be maintained
  also important for interoperability

## Slide 9: OFDM channelization
OFDM mainlob as wide as CCK
Frequency [MHz]
-20
-15
-10
-5
0
5
10
15
20
-25
Power Spectral Density [dB]
-80
-70
-60
-50
-40
-30
-20
-10
0
10
25
OFDM (6dB backoff)
CCK

## Slide 10: FCC
OFDM is essentially same as PBCC, but then over multiple carriers
If PBCC is approved then there is no reason not to approve OFDM
Simulations shows that OFDM can meet jamming test

## Slide 11: OFDM performance
SNR needed for 24 Mbit/s OFDM is comparable to 11 Mbit/s CCK
  at 50ns delayspread, 1000 byte packets and PER 10%
    SNR 24Mbit/s OFDM: 19 dB
    SNR 11Mbit/s CCK: 18dB
delayspread tolerance comparable:
  24Mbit/s OFDM 250ns
  11Mbit/s CCK no equalizer: 90ns
  with equalizer:300ns
distance of 24Mbit/s OFDM slightly smaller than CCK
  backoff approx 3dB worse (7dB compared to 4dB)
12 Mbit/s OFDM outperforms 11 Mbit/s CCK
54 Mbit/s in 2.4 band!

## Slide 12: Complexity
Gatecount OFDM baseband processing comparable (slightly more) to CCK (or PBCC) equalizer
  if CCK equalizer is replaced with OFDM core then the cost increase is moderate
    use 6 or 12 Mbit/s OFDM in stead of 5.5 or 11 CCK, if high delayspread tolerance is required

## Slide 13: Other benefits
802.11a standard exists:
  higher rate standard can be approved fast
Smooth migration to 5Ghz band
  development: same baseband processing in 2.4 and 5 GHz
  Possibility for dual band radio’s

## Slide 14: Conclusion
OFDM is a good candidate for the higher rate in the 2.4 band:
  technical feasible (interoperates and coexists with 802.11b)
  makes very high rates possible
  performance
  fast standard adoption
  migration to 5 GHz