## Slide 1: Dynamic Channel Selection (DCS) Scheme for 802.11
G. Cervello, S. Choi, S. Mangold*, and A. Soomro
Philips Research-USA
Briarcliff Manor, New York
*Aachen University of Technology, Aachen, Germany

## Slide 2: Introduction
Background
  CEPT requires DFS and TPC
  Nice to have DCS for some environments, e.g., home environment and offices in a building
  DCS first, if not working, work in overlapping BSSs
Need to define a DCS mechanism WITHOUT requiring any change in PHYs within TGe
  It should work with all the current and future PHYs
Implementation-dependent algorithms located in SME

## Slide 3: Basic Mechanism for Infrastructure BSS
Initiation of a new channel selection
Request of a channel measurement by AP
Channel measurement process of STAs
Measurement report from STAs to AP
Decision making by AP
Channel switch announcement by AP
Switch into the new channel

## Slide 4: 1. Initiation of Channel Selection
Three cases of channel selection initiation
  A BSS is formed by an AP (via MLME-START)
  AP and/or STA(s) experience bad channel condition persistently
  Overlapping BSSs detected
Channel measurement (Step 3) used to measure current channel quality in each STA
Need management frames for the channel status report from STAs to AP
When to initiate will be up to implementation

## Slide 5: 2. Channel Measurement Request
AP requests channel measurements to some STAs to find the best channel to run its BSS
  Those STAs will be considered as sleeping STAs
  Measurement by AP not desirable except for before the start of a new BSS
New management frames needed
  When to begin the measurement
  Which channels to measure
  How long to measure
  How to measure (explained next)

## Slide 6: 3. Channel Measurement Process
STA moves to channel(s) to measure as requested by AP
Three ways of channel measurements
  Detection of other BSSs running in the channel
  Measure RSSI and PER when BSSs detected
  Measure busy channel portion
Detection of other BSSs
  Using the “scan” service from MLME to SME
  MLME-SCAN.request and MLME-SCAN.confirm

## Slide 7: 3. Channel Measurement Process (Cont.)
Measurement of RSSI and PER
  RSSI value available to MAC via PHY_RXSTART after reception of a valid PLCP header
  Moreover, RSSI values not standardized
Measurement of busy channel portion
  Measure time and number of cases of PHY_CCA(BUSY) without PHY_RXSTART
  Will work unless .11b CS_ONLY CCA mode
  Can be used to measure alien devices, e.g., H/2, Bluetooth, and microwave

## Slide 8: 4. Measurement Report to AP
Measurement report of STA(s) to AP
If no BSS detected in a channel, the result of the third measurement is only meaningful
May be reported during CP or CFP (per being polled)
Need management frames
  Same frame type can be used for current channel status report for Step 1

## Slide 9: 5. Decision Making by AP
AP make a decision per hearing the measurement reports from STAs
  Whether to move or not
  To which channel if decided to move
  When to move, e.g., in which TBTT
Need to compare other channels with the current channel
Need to consider sleeping STAs to determine when to move

## Slide 10: 6. Announce of Channel Switch
Need to announce the channel move decision to STAs
The decision announced via beacon frames with a new information element
Announced several times to ensure the decision reception

## Slide 11: 7. Switch into New Channel
At the scheduled moment, e.g., TBTT, all STAs including AP change their channel
Can be done by changing PHY MIB dot11CurrentChannelNumber using PLME SAP primitives
  PLME-SET.request (MIBattribute, MIBattributevalue)
  PLME-SET.confirm (status, MIBattribute)

## Slide 12: Summary
Basic DCS mechanism proposed for infrastructure BSS of 802.11
Implementation-dependent algorithms located in SME
Three ways of channel measurements
Need two (new) management frames
Need to add a new information element in beacon frame
Can be defined WITHOUT any change in PHY