## Slide 1: Plug-n-Play Security in the Home & Small Business Ron Brockmann Intersil
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Requirements
Good security solution in an unmanaged environment (eg compare to configuration ease of Ethernet based network)
  No WEP keys, passwords etc
Limited implementation impact
Scalability: single client for use in various environments

## Slide 3: Example Scenario
Home user has DSL/Cable and two PCs
  Wants to create wireless home network
Typical Security Threats
  Neighbors try to access the broadband pipe
  Or steal files from PCs
User does not care for any extra passwords or software

## Slide 4: Solution Elements
Covered in other proposals
  Stronger encryption
  Diffie-Hellman based session key generation
  MAC address based Access Control List
  Extensibility/Negotiation
Specific element
  ‘Zero-Management’ MAC address authentication

## Slide 5: Outline
Single static random private/public key pair per MAC address
On first contact, APs, Stations learn MAC/PubKey pairs for other devices if they are on the Access Control List
On subsequent contacts, stored MAC/PubKey can be used to prove identity of other device

## Slide 6: Access Control List
ACL can operate usefully because MAC addresses can be authenticated
ACL could be managed through MIB
Or, learning mode also (eg learn next STA if button is pressed)

## Slide 7: Diffie-Hellman key exchange
Alice and Bob want to construct a private key over a public channel. Both agree on a public prime p and primitive root g modulo p.
Alice chooses a random value x Alice sends gx mod p to Bob Bob chooses a random value y Bob sends gy mod p to Alice Alice computes gxy mod p as (gxmod p)y mod p Bob computes gxy mod p as (gymod p)x mod p
Discrete logarithm problem: Given g, p, and gx mod p, find x. Diffie-Hellman problem: Given g, p, gx mod p, and gy mod p, find gxy mod p.

## Slide 8: Simplified Outline of Operation
STA derives its Public Key X’= gX mod p from its fixed Private Key X and sends X’ to AP over the air as part of the Authentication Request
AP checks MAC address and X’ to its records. If successful, AP derives Public Key Y’=gY mod p from its fixed Private key Y and sends Y’ to STA over the air
STA calculates ZSTA = (Y’)X mod p, and sends a hashed value H(ZSTA) to the AP over the air.
AP calculates ZAP = (X’)Y mod p. If the STA has knowledge of X and completed the calculation successfully, ZSTA equals ZAP and therefore H(ZSTA) equals H(ZAP). If this comparison fails, this points to a Rogue STA. Otherwise, STA identity is proven
AP and STA derive a session key from Z.Eavesdroppers can not derive Z or the session key.

## Slide 9: Detected Attacks
Trying to authenticate with MAC address not in ACL
Trying to authenticate with correct MAC address – different public key
Trying to authenticate with correct MAC address and public key – unable to calc session key (not knowing private key)
Authentication can be mutual!

## Slide 10: Attacks Not Addressed
‘Stolen’ STAs – access allowed until removed from ACL
Compromised private key
In targeted environments, ease of use more important than quest for perfect security

## Slide 11: Implementation Impact
Generation of static private keys
  At manufacture time (pre-calculated)
  Or on first start-up of AP/STA
Modular Exponentiation
  Scalable security by private key length
  Results may be cached
Non-Volatile Memory
  As low as 22 bytes per MAC/PubKey learned

## Slide 12: Some Details…
Broadcast/Multicast Key Management
  At authentication, AP sends key information to newly authenticated STA
IBSS mode
  Individual session-key/authentication per STA-STA link
Direct STA to STA traffic within a BSS?
  Only AP may have ability to authenticate STAs and has ACL. Possible solution: AP acts as Key Distribution Center for the BSS and generates and distributes session keys for direct STA to STA traffic within its BSS
Backward Compatibility
  Current WEP may still be used for traffic to legacy stations, if this support is required. Broadcast/multicast must use WEP also, then!
Session Key Lifetime
  A new session key may be generated at any required time, based on local policy decision