## Slide 1
Wireless MAC Multimedia Extensions
Albert Banchs, Xavier Perez, Witold Pokorski
NEC Europe Ltd.
Markus Radimirsch
University of Hanover

## Slide 2: Design Criteria of the proposed solution
  Support of the required QoS
  Backward compatibility
  Low migration effort from current products
  Interoperation with the backbone QoS architecture
  Soft QoS
  Fully distributed MAC protocol
  Connectionless MAC protocol

## Slide 3: Design Principle: DiffServ (I)
In the Differentiated Service architecture proposed by the IETF, the following scheduling combined with admission control provides the following service classes:
    Premium Service: low delay and low jitter guaranteed
    Assured Service: bandwidth guaranteed
    Best Effort: no guarantees

## Slide 4: Design Principle: DiffServ (II)
In our proposal, the scheduling provided by the MAC protocol is equivalent to the scheduling of DiffServ routers, with the difference that our protocol has to work on a distributed basis.
The reasons for basing our architecture on the principles of DiffServ are:
    Scheduling in DiffServ routers, together with admission control, meets the QoS requirements of the users.
    DiffServ does not keep per flow state on the core routers. This fits nicely to the goal of providing a distributed and connectionless MAC protocol providing soft QoS.
    Assuming a DiffServ backbone, our proposal makes the interoperation with the backbone straightforward.

## Slide 5: Proposed Architecture
The proposed architecture consists of two optional parts:
Premium Service
  redefines the PCF of the standard
  leaves the DCF untouched
Assured Service
  implies minor changes in the MAC layer of the DCF
  leaves the PCF as is
The fact that these two extensions are designed as different and independent modules gives the manufacturer the option to omit one of them; if one of the two service classes is not needed, the migration from the current standard is considerably simplified.

## Slide 6: Premium Service: Overview
  Premium Service packets should be given a higher priority than any other traffic class
  PCF receives a higher priority treatment than DCF by using a smaller IFS
  In our proposal we redefine the PCF function by allowing Premium Service traffic to access the channel after the PIFS while stations with other traffic types have to wait until the end of the DIFS.
  A contention resolution algorithm is still needed to avoid collisions between stations with Premium Service traffic
  In order to meet the low delay requirement, admission control is needed to keep the amount of traffic using this service sufficiently low

## Slide 7: Assured and Best Effort Services: Overview
  In the DCF approach, the throughput received by a station depends on its CW; the smaller the CW, the higher the throughput
  In our proposal, both Assured and Best Effort Services are supported by the DCF function of the current standard with minor changes in the computation of the CW
  The CW in each station is computed in order to give to the station its expected throughput according to the contracted service
  In order to allow backward compatibility, the stations conforming to the current standard should behave as Best Effort terminals in our approach
  Admission control is also needed, in order to ensure that the commitments for Assured Service can be met

## Slide 8: Protocol Operation

## Slide 9
Premium Service

## Slide 10: Overview
For Premium Service, the PCF was redefined
  Acceptable due to small penetration of the current standard‘s PCF in the market
Two schemes under investigation
  A scheme similar to HIPERLAN 1
    Simulation results available and presented here
  A scheme with a jamming burst and an adapted 802.11 Backoff scheme
    Still under investigation
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: Premium Service Mechanism 1
Two Elimination Bursts (EB) (similar to HIPERLAN 1)
One slot duration after each Burst for carrier sensing
Normal RTS/CTS and Ack Mechanism used

## Slide 12: Length of the Elimination Bursts
The length of EB 1 in # of slots is given by:
  n - number of slots, : probability parameter, : maximum # of slots
The length of EB 2 in # of slots is given by:

## Slide 13: Functional Description
All stations using this scheme start transmitting EB1 after a PIFS
Carrier sensing after EB1 for 1 slot duration
  If medium busy, withdraw, otherwise send EB2
Send EB2, afterwards carrier sensing for 1 slot
  If medium busy, withdraw, otherwise packet transmission
Packet transmission with RTS/CTS and Ack
Residual collision rate very low (depending on parameters, approx. 3.5%)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 14: Premium Service Mechanism 2
All stations using Premium Service send a Jamming Burst (JB) for 2 slot durations after a PIFS
All other stations set their NAV to EIFS ( 360 µs) and refrain from access attempts (in line with current standard)
Afterwards modified Backoff scheme: CWmin = 7, CWmax = 15
  max. Duration of Contention Phase: 17 slots = 340 µs

## Slide 15: Simulation set-up for EB1/EB2 scheme
Quality criterion: Max. Delay of 25 ms not exceeded by 97% of the packets
Packet length: 500 bytes
Total Number of stations: 20
2 Mbps W-LAN
All stations have CBR traffic. The Best Effort stations always have a packet to transmit

## Slide 16: General results for EB1/EB2 scheme
Saturation throughput approx. 1300 kbit/s
Premium Service stations get what they request as long as their total requested data rate stays below the saturation throughput
The Best Effort stations share the remaining data rate almost equally
  If saturation requested by Premium Service stations, Best Effort stations do not get any packet transmitted
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17
2 Premium Service stations

## Slide 18: Observations
  Data rate ranges from 64 kbit/s to 750 kbit/s
  The delay for all data rates remains below 10 ms in all cases except with 750 kbit/s
  The delay distribution is almost independent from the data rate but rises after the total data rate of the Premium Service stations exceeds the saturation throughput (=1.3 Mbit/s)
  Delay increases with data rate of 750 kbit/s but still meets the quality criterion
  At 750 kbit/s, Best Effort Stations get no data rate at all, Prem. Serv. Stations get approx. 650 kbit/s each
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 19: 6 Premium Service stations

## Slide 20: Observations
The delays are generally higher than with 2 Premium Service stations but still meet the quality criterion up to a data rate of 128 kbit/s
At 256 kbit/s per station, the saturation throughput is exceeded and the delay increases dramatically
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 21: 64 kbit/s per Premium Service station

## Slide 22: Observations
The quality criterion is met for up to 6 stations with 64 kbit/s.
It is not met for 8 Premium Service Stations and more
The delay of 8, 10 an 12 stations is higher
  the curves are very steep in the decisive region
  The delay remains reliably below individual thresholds (28 ms for 8, 35 ms for 10, 41 ms for 12 stations)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 23
As a rule of thumb, the admission control could allow not more than 6 stations with a maximum data rate of 128 kbit/s.

## Slide 24: Conclusions for Premium Service
The contention resolution scheme with two elimination bursts can meet the quality criterion defined for up to six stations with data rates up to 128 kbit/s for a 2 Mbps Wireless LAN
The delay distribution is very steep and has excellent properties
If the Premium Service Stations use in total more than the saturation throughput, the delays increase dramatically
  In this case, the service quality for all other stations drops drastically
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 25
Assured and Best Effort
Services

## Slide 26: Overview
For Assured Service, a new algorithm for computing the CW is proposed
  There is a direct relationship between the CW assigned to a station and the throughput that this station receives
For backward compatibility reasons, Best Effort stations behave exactly as the current standard
Two schemes under investigation
  CW changes dynamically during the session
    Simulation results available and presented here
  CW statically assigned at the beginning of the session
    Still under investigation
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 27: Contention Window Computation (I)
Basic idea: each station monitors the bandwidth experienced and modifies its CW in order to achieve the desired throughput
The following aspects should be taken into account in the CW
computation:
The CW should not increase above the values used by Best Effort terminals, since this would lead to a worse performance than Best Effort
If the low sending rate is the reason for transmitting below the desired throughput, the CW should not be decreased
CW should not decrease in such a way that the overall performance is negatively influenced
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 28: Contention Window Computation (II)
The CW computation algorithm works as follows:
The token bucket gets filled at the desired transmission rate. For each successful transmission the length of the transmitted packet gets substracted from the bucket.
The user has enough resources to transmit a packet if the bucket has enough bytes in it. In this case the CW is decreased.
If the transmission queue is empty, it means that the current CW satisfies the user sending need and the CW is not decreased.
If the channel is detected below its optimum limit of throughput due to small CWs, the CW should be increased.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 29: Contention Window Computation (III)

## Slide 30: Bandwidth Guarantee
In this example it can be seen how the adjustment of the CW leads
to the desired bandwidth in average (in this case, 500 Kbps):

## Slide 31: Simulations Assured Service
Simulations:
  Bandwidth Assurance
    CBR
    Bursty traffic
    TCP
  Impact of Best Effort stations
  Channel utilization
  Over and undercommitment
  Packet drops
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 32: Simulation set-up for Assured Service
2 Mbps W-LAN
Packet length: 1000 bytes
1, 2, 4 and 8 Assured Service stations
Total number of stations between 10 and 50
Amount of bandwidth assigned to Assured Service: 1 Mbps
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 33: Impact of Best Effort stations

## Slide 34: Observations
Since CW of Best Effort cannot be arbitrarily increased and CW of Assured Service cannot be arbitrarily decreased, it is impossible to avoid a certain level of impact
The bandwidth committed to Assured Service (1 Mbps) is realised for a low number of best effort stations, but decreases with the number of best effort stations
With 50 stations, the throughput received by Assured Service is one half of the requested
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 35: Channel utilization

## Slide 36: Observations
The channel utilization decreases with the number of Assured Service stations
With 4 and 8 Assured Service Stations the channel utilization is similar to the achieved by the current standard
With 1 and 2 Assured Service Stations we achieve a higher channel utilization than the current standard
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 37: TCP traffic

## Slide 38: Observations
With TCP traffic the architecture performs almost as well as with UDP CBR traffic
The channel utilization achieved is lower because of the congestion control of TCP
The TCP ACK of Assured Service stations need also to be treated as Assured Service traffic
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 39: Conclusions for Assured Service
Without Best Effort stations, the throughput guarantees are met for CBR, bursty and TCP traffic
Best Effort terminals do impact Assured Service, but this impact is rather low: it takes 50 terminals to reduce to a half the committed bandwith (and in this case each Best Effort station receives a very small throughput)
The packet drops always keep reasonably low (below 2%)
The channel utilization is not harmed by Assured Service as compared to the channel utilization of the current standard
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 40
Remarks and
Conclusions

## Slide 41: Remarks
The proposed architecture makes the following configurations possible:
  Premium Service + Assured Service + Best Effort
  Assured Service + Best Effort: we avoid redefining PCF
  Premium Service + Best Effort: DCF is used unchanged
  Best Effort: no changes at all to existing products

## Slide 42: Conclusions
the scheme is simple and requires small changes to the existing standard
  distributed and connectionless scheme
  low migration effort from current products
it can interoperate with the standard MAC (backward compatibility)
it distinguishes between two different classes of service: delay critical (Premium Service) and bandwidth critical (Assured Service)
Premium Service can support VoIP traffic
Assured Service works for both UDP and TCP
paper available at
  http://www.ant.uni-hannover.de/Mitarbeiter/Radimirsch/MMAC.ps.gz