## Slide 1: Notes from LinCom Wireless FCC Visit 6/30/2000

## Slide 2: Discussion of HRb like signals with FCC
The FCC is not entertaining any substantive discussions of potential Higher Rate Spread Spectrum certifications at this time
  Awaiting rulemaking related to NPRM 99-231
  Would be certified using CW jammer test, which may be changed
Seem to have a problem with high order modulation schemes
  Commented on it looking like “unspreading”
Give a sense that 11 Mbps in a 22 MHz bandwidth is about as far as they’ll go
  Spread Spectrum is like porn, “We (the FCC) know it when we see it”
  “If you want higher data rates go to 5 Ghz, that’s why we opened up the UNII bands”

## Slide 3: NPRM
Gave a clear indication that they are leaning to replace the CW jammer test with an as yet undefined Gaussian jammer test
Gave a sense that an acceptable Processing Gain calculation (for SS systems with less than 10 chips/symbol) may likely NOT include the sum of “bits per symbol spreading gain” plus any coding gain