## Slide 1: 5GHz Sky is Falling U-NII Spectrum Sharing
La Jolla 13 Jul 2000
Denis Kuwahara
Boeing

## Slide 2: 5 GHz U-NII
JPL paper on sharing spectrum (02328R- SARs & U-NII_Devices@5.3GHz)
Spaceborne Synthetic Aperture Radar SAR footprint = 181.5 kM2 approx 70 Mi2
Single U-NII emitter w/ conditions
Antenna Pattern and Power Output
Limited co-existence possible

## Slide 3: Single 100 mW Emitter
Xmt ant = -20dBi High Elevation Angle Gain (10 dBi Gain)
The WLAN signal is approximately 20 dB below sensor threshold

## Slide 4: Single 250 mW Emitter
Xmt ant = -4dBi High Elevation Angle Gain (6 dBi Gain)
The WLAN signal is approximately 1 dB above sensor threshold

## Slide 5: Single 250 mW Emitter
Xmt ant = -0dBi High Elevation Angle Gain (0 dBi Gain)
The WLAN signal is approximately 5 dB above sensor threshold

## Slide 6: Conclusion
Earth Sensor Satellite folks are pessimistic
Best case is a few WLAN emitters within an 8 X 8 mile square, using 10 dB antennas
No case for WLANs with lower gain antennas
Given that: WLANs / RLANs are currently only a footnote for 5.15-.25GHz in ITU-R Radio Regs
Could WLANs be eliminated from ITU regs?

## Slide 7: Required Action
Vendor participation is CRITICAL in ITU process to lobby for WLAN spectrum
Involvement in multiple regulatory regions
Participation in Working Parties, Task Groups, Joint Rapporteur Groups
RF Spectrum is a Shared Resource
Creation of a Joint International WLAN forum e.g. 3GPartnershipProject

## Slide 8: Questions
Thanks