## Slide 1: 802.11 MAC applicability for WirelessHUMAN
Tim Godfrey
Intersil
July 9, 2000

## Slide 2: Commonality with 802.11
802.11 has broad market acceptance, and a rapidly growing installed base.
802.11a WLAN devices will become available in 2001.
Economies of scale will reduce the cost for 802.11a and WirelessHUMAN implementations if they use comparable technologies.

## Slide 3
The 802.11a PHY is directly applicable to the Wireless HUMAN project.
  802.11a operates in the 5GHz UNII band.
  802.11a uses OFDM modulation with 52 subcarriers, providing excellent multipath performance.
  802.11a supports 8 data rates in the range of 6 to 54Mbps, which allows adaptation to various link conditions.
802.11a PHY Overview

## Slide 4
The 802.11A PHY

## Slide 5: Why is the 802.11 MAC appropriate for WirelessHUMAN?
The 802.11 MAC was designed to support a relatively unreliable RF link operating in an unlicensed band.
The protocol is extremely robust, and provides the level of reliability required by higher layer protocols.
The MAC provides a level of indirection which enables nomadic users, and hand-off between access points, without affecting higher layer protocols.

## Slide 6: What are potential problems with the 802.11 MAC for WirelessHUMAN?
The 802.11 MAC was not designed for node separation distances on the order of kilometers. At 5 kilometers, the propagation delay roughly equals the short interframe space (SIFS) of 16uS.
  Long propagation delays can result in failure of the CSMA/CA access mechanism, causing collisions.
  Use of the MAC’s Point Coordination Function prevents failure, although at a loss of efficiency.
  PCF enhancements described in 802.11E proposals provide further improvements to efficiency.

## Slide 7: Improvements to the 802.11 MAC
In September 1999, the MAC Enhancements study group was formed. Two PARs were generated.
Enhancements related to Quality of Service, Security, Authentication, and other internal MAC functions are being developed by Task Group E. The Task Group will produce a supplement to the 802.11 standard.
Enhancements related to the Inter Access Point Protocol are being developed by Task Group F. This protocol is outside the scope of 802 standards, so Task Group F will produce a Recommended Practices Document.

## Slide 8: Scope and Purpose of Project 802.11E
The PAR, approved in March 2000, defines the scope and purpose of the project:
  Enhance the 802.11 Medium Access Control (MAC)
  Improve and manage Quality of Service
  Provide classes of service
  Provide enhanced security and authentication mechanisms
  Consider efficiency enhancements in the areas of the Distributed Coordination Function (DCF) and Point Coordination Function (PCF)

## Slide 9: Why Enhance the 802.11 MAC?
Demand for Quality of Service over wireless LAN
  Voice over IP
  Multimedia
  Support for priorities and classes of service implemented in higher network layers.
Need for improvements in privacy and authentication.
  Weaknesses in existing WEP mechanism have been identified
  Changes in regulations regarding export of encryption.
  Desire to implement different authentication mechanisms in to correspond to differing security environments.

## Slide 10: Why doesn’t the existing Point Coordination Function provide adequate QoS?
The PCF provides a Contention Free Period (CFP), where access to the medium is completely controlled by the Point Coordinator (PC).
  The CFP begins with a beacon transmitted by the PC. The PC must contend for the medium using the DCF rules. Thus the beacon (and the CFP) may be delayed by other non-coordinated traffic.
  There is no unacknowledged unicast service.
  There is no standardized mechanism for controlling Point Coordinator bandwidth allocation policy.
  Stations attempting to associate or reassociate in a Point Coordinated BSS must contend under DCF rules.

## Slide 11: 802.11E QoS Proposal Comparison
A Polling Proposal for QoS
  TSA and Enrichnet - 061
MAC Enhancements Joint Proposal
  AT&T, Lucent, Sharewave 071
QoS Support in 802.11 WLAN
  Philips Research 110
802.11 PCF Enhancements and Contention Free Bursts
  NWN 113
IEEE 802.11 Quality of Service
  Microsoft 028
Wireless LAN QoS
  Intel 036
Use SBM for admission control
Use 802.1d VLAN tags to indicate priority



Change DCF rules to provide priority




Fix existing problems with the PCF


Enhance the PCF






## Slide 12: 802.11E QoS Proposal Comparison
PCF Enhancements

Mitigate the effects overlapping BSS on the same channel

Extend CFP polling ordering rules
Means to allow BW reservation without DCF Contention
Management interface for bandwidth allocation policy
New acknowledgement policies
Direct STA – STA transfers







A Polling Proposal for QoS
  TSA and Enrichnet - 061
MAC Enhancements Joint Proposal
  AT&T, Lucent, Sharewave 071
802.11 PCF Enhancements and Contention Free Bursts
  NWN 113
Proposals using enhancements to the PCF


New types of polling

?

## Slide 13: 802.11E CEPT Harmonization
One of the enhancements planned for 802.11E is the addition of support for Dynamic Frequency Selection (DFS) and Transmit Power Control (TPC) to the 802.11 MAC.
  Full implementation will require corresponding changes to the 802.11 PHYs.

## Slide 14: 802.11E Security Enhancements
The authentication mechanism will be extended to provide mutual authentication in both infrastructure and independent BSS’s.
Security enhancements will protect network traffic from eavesdropping to a reasonable level compatible with the state of the art.
Security enhancements will allow for authentication of the source of each packet, to prevent link hijacking or undetected insertion of rogue packets into the link.
Security enhancements will allow key distribution or derivation of per-link or per-session keys, and strongly protect keys and passwords from recovery by eavesdropper.

## Slide 15: 802.11E Project Timetable
July 1999 – Study Group formed by 802.11
November 1999 – MAC Enhancements PAR submitted
March 2000 – PAR Approved, Task Group 802.11E formed
  First set of proposals and papers on MAC Enhancements.
May 2000 – First meeting of Task Group E
July 2000 – 802 Plenary Meeting, La Jolla, CA
  Continuation of presentation of papers and proposals
  Refinement of Requirements and Evaluation Criteria
September 2000 – Selection of proposals
November 2000 – Target date for first letter ballot

## Slide 16: WirelessHUMAN system architecture
A multi-hop network (wireless distribution system) is not directly supported by the 802.11 MAC.
  Routing and forwarding could be handled at higher layers.
  Such a system would make support QoS with 802.11E MAC enhancements much more difficult.
From: 802.16hc-00/01 “Requirements for WirelessHUMAN Systems”

## Slide 17: Conclusion
The 802.11 MAC is already implemented and in use.
The 802.11 MAC is highly configurable.
  Significant changes in capabilities and characteristics can be achieved with changes to the MAC parameters
  If changes to the parameters are necessary for the WirelessHUMAN application, it does not affect the hardware implementation and thus does not reduce economy of scale advantages.