## Slide 1: DFS/TPC Proposal
Greg Chesson, greg@atheros.com
Bill McFarland, billm@atheros.com

## Slide 2: Outline
Objectives
ERC Requirements
  Hiperlan 2 references
Proposals
Analysis

## Slide 3: Objectives
Achieve ERC certification for 802.11a in European markets
  Identify and select technical methods
  No PHY changes
  Lobby as a group with
    European regulatory bodies (CEPT, UK-RA, etc.)
    802.11e
    ETSI

## Slide 4: ERC DFS Requirements
Goal: evenly distribute spectrum use to reduce average transmitted power “seen” by satellite.
Secondary goal: avoid BSS interference.
Methods:
  Sample channels for interference with AP sensing and remote station sensing,
  Select vacant channels,
  Move BSS and stations to alternate channels when channel is degraded.
  Spread 200mW EIRP/STA over 330 Mhz (14 channels)

## Slide 5: DFS Methods in the Hiperlan2 Specification
Detailed remote RSSI sensing
  3 modes of sensing/reporting
No procedure for channel selection
  Vendor dependent
Procedure for dynamic channel move
  Lengthy (safe) notification process
  Followed by cutover
Defined over 14 channels (330 Mhz)

## Slide 6: Proposed Approach DFS/DCS - AP Channel Sensing
AP listens at startup
  Selects channel with least interference, or
  Selects randomly from vacant channels
  No change needed in 802.11 MAC/PHY
AP moves all stations if channel degrades (optional)
  Would require new MGMT messages
  More relevant for BSS interference

## Slide 7: Proposed Approach DFS - Power/Bandwidth Trading
Provide a regulatory option for FCC-style (200 MHz, 50mW/20MHz with antenna gain cap):
  Trade equal spreading across 330 MHz and 200 mW transmit power for equal spreading across 200 MHz and 50 mW transmit power
Justification for the power/bandwidth trade
  Resulting power spectral density is even lower for the 200 MHz option. (330MHz/200MHz)*(50mW/200mW) = 0.4
  For terrestrial systems, adding antenna gain will decrease vertically-transmitted power that might interfere with satellite systems.
  FCC regulations were approved in U.S. to meet same satellite goals

## Slide 8: Benefits of the Proposed DFS/DCS Approach
AP channel sensing and random channel selection
  Sensing prevents buildup of energy in any one channel
  Random channel selection assures uniform channel occupation
  Allows for vendor differentiation (e.g. methods to prevent inter-cell interference)
Benefits of power/bandwidth trading
  Supports the market need for lower-cost, lower-power devices that aren’t forced to operate over very wide frequency range and in the upper 1W band.
  Supports the market need for devices that can operate globally

## Slide 9: ERC TPC Requirements
Goal: reduce total transmit power in primary service satellite footprint by 3dB (relative to 200 mW maximum transmit power)
Methods:
  Use low power when possible
  Use maximum power only when necessary

## Slide 10: Proposed Method for TPC - Static TPC
Transmit power, to be consistent with ERC regulations, would be limited to 60.6 mW EIRP
Achieve 3dB reduction from 200mW by always transmitting at lower power.
  200mW (ERC limit) * 0.5 (for -3dB TPC) * 200/330 (BW req) = 60.6mW EIRP
An FCC-style 50 mW transmitter with a 6dB gain cap is consistent with ERC regulations
  For a 50mW mobile unit, .83 dB antenna gain results in 60.6mW EIRP (in the direction of antenna gain)
  Typical mobile units have ~1.5dB antenna gain (70.6 EIRP from 50mW)
  6dB gain should be allowed, given that useful antennas would concentrate horizontal energy and reduce vertical radiation.

## Slide 11: Benefits of the TPC Approach
Offers reasonable performance in both central-control and distributed-control environments
Deterministic, rather than dynamic
  Dynamic TPC (DTPC) does not help inter-BSS interference issues
  DTPC not helpful for DCF
  DTPC benefits for PCF are questionable since PCF relies on DCF
DTPC applies to PCF uplink only
  Increases cost/complexity, limited benefit
  Significant IP issues to avoid
Simpler to implement
Static TPC more stable than DTPC
Better suited to ad hoc or direct STA-STA transfers

## Slide 12: Summary
DFS
  AP-centric approach
  8 channel power/bandwidth trading option
TPC
  Static TPC with antenna gain cap