## Slide 1: MPEG-2 High Rate Video over 1394 and Implications for 802.11e
John Kowalski
Sharp Corporation

## Slide 2: Outline
Introduction
MPEG-2 High Rate Video and Transport Stream Description (1394/ IEC 61883-4)
  Throughput
  Latency, Jitter Requirements
Issues for 1394 AV over 802.11
Appendix: Formats for 1394/IEC61883-4

## Slide 3: Introduction
Evaluation Criteria Group identified high rate MPEG as a data stream type for use in 802.11e.
High Rate MPEG is closely tied to 1394, and IEC 61883-4.
1394, although not strictly part of requirements, is “nice to have” capability for 11e proposals.
Hence this summary of high rate MPEG via 1394/IEC 61883-4.

## Slide 4: MPEG2 Data
MPEG2 ensures the data rate of one transponder.
  For CS, the actual data rate of one transponder is, for HDTV-like video 29.2Mbps.
  For BS Digital, the actual data rate of one transponder is 26.085Mbps.
Multiple streams are included in one transponder.
  3Mbps – 6 Mbps is used for bit rate of one channel.
For HDTV, one channel uses one transponder.
  Over 22Mbps is required as the data rate.
  About 24Mbps is upper limit because of their overhead.
Key requirement: 1394/IEC61883-4 uses isochronous, fixed length packets.

## Slide 5
TS Packet Transmission Rate
Maximum jitter is assumed to be about 311 s on transmit, and 50s from real time interface, from IEC 61883-4. Latency arbitrated in 1394.
60,160
5
48,128
4
36,096
3
24,064
2
12,032
1
6,016
1/2
3,008
1/4
1,504
1/8
Transmission rate (Mbps)
TS Packet / cycle

## Slide 6: Issues for 1394 AV over 802.11
1394/6883-4 wants to see isochronous streams. So a lean (low overhead, not complex) PCF is a must.
Small packet sizes of constant length (480 bytes +24 bytes O/H). With Breezecom’s (nonoptimized?) estimates for efficiency
(document 99-256) an efficiency of at best 47% can be expected in the PCF, for 400 bytes.
Buffering must be applied to compensate for 802.11 behavior which breaks the standard (as a recommended practice?)

## Slide 7
Issues for 1394 AV over 802.11 (cont.)
How to transfer the QoS information? Must map 1394 information into 802.1p/q priority tags.
How to allocate the bandwidth, jitter?
Efficiency- how best to format over 802.11
Power save requirements for portable AV equipment
    When does the equipment transfer the state?
    How to poll the equipments that is sleep mode

## Slide 8: Appendix: Formats for 1394/IEC61883-4

## Slide 9: 1394 MPEG2-TS Transfer
MPEG2-TS transfer sequence is defined in IEC61883 standard.
  Source packet header (4bytes) is applied to each transport stream (TS) packet (188bytes). (Source packet header consists of Reserved field (7bits), cycle count (13 bits), cycle_offset (12 bits). These field is used as time stamp.)
  Source packet (comprising source packet header and TS packet) is divided to each data block (24bytes).
  Several data blocks are put into one isochronous packet.
  Common Isocrhonous Packet (CIP) header and IEEE1394 header are applied to each isochronous packet.
  The isochronous packet is transferred.
  Empty packet (composed only CIP and 1394 Header) is transferred when there is no data to be transferred.

## Slide 10: 1394 MPEG2-TS Transfer (cont.)
Example of MPEG2-TS data transfer defined in IEC61883 is shown below.
188bytes
125us
Timestamp
188bytes
Header
TS Packet
Empty Packet

## Slide 11: TS Packet Transmission Rate
Maximum jitter is assumed to be about 311 ms on transmit, and 50ms from real time interface, from IEC 61883-4
TS Packet / cycle | Transmission rate (Mbps)
1/8 | 1,504
1/4 | 3,008
1/2 | 6,016
1 | 12,032
2 | 24,064
3 | 36,096
4 | 48,128
5 | 60,160

## Slide 12: Header
Data
CIP header and 1394 header is applied to each isochronous packet.
  CIP header is defined in IEC61883 standard, 1394 header is defined in IEEE1394 standard.
  The source packet header is applied to each TS packet.
IEEE1394 isochronous header
CIP header
Source packet header (shown in each TS packet)
data_CRC

## Slide 13: 1394 Header
Data
header_CRC
data_length: data block payload length 2 bytes
tag: high level label for format of data. 012 is defined as CIP header.
channel: isochronous channel 6 bits.
tcode: transaction code. Ah is defined as isochronous data block.
sy: Application-specific control field. (4 bits synch. code)
data_length
tag
channel
tcode
sy
data_CRC
The shaded field is defined by IEEE1394 (4 bytes/line).
CIP header

## Slide 14: CIP Header
00
FN
SID
DBS
QPC
s
r
10
FMT
FDF
The shaded field is defined by IEC61883. (4 bytes/line)
SID: Sender node ID
DBS: Data Block Size
FN: Fraction number
QPC: Quadlet padding count
SPH(s): Source Packet Header
DBC: Data Block Counter
FMT: Format ID
FDF: Format Dependent Field
r: Reserved
Data
1394 isochronous header
data_CRC
DBC

## Slide 15: CIP Header (MPEG2-TS)
Each field is defined as the followings for MEPG2-TS transfer.
  SID: depends on configuration
  DBS: 000001102 (6quadlets = 24bytes)
  FN: 112 (8 data blocks in one source packet)
  QPC: 0002 (no padding)
  SPH: 1 when source packet header is present
  DBC: 0 … 255
  FMT: 1000002 (Format type of MPEG2-TS)
  FDF: For MPEG2-TS transfer, most significant bit is defined as TSF, others are reserved. TSF indicates a time shifted data stream (1: the stream is time shifted.).

## Slide 16: Source Packet Header
Reserved
4bytes Source Packet Header is shown below.
  The time stamp in the source packet header is used by isochronous data receivers for reconstructing a correct timing of the TSPs at their output.
cycle_offset
cycle count
7bits
12bits
13bits

## Slide 17: DV Format (SD-DVCR)
DV video, audio data consists of 80 bytes (Digital Interface) DIF block.
1 DIF sequence consists of 150 DIF blocks.
1 video frame consists of 10 DIF sequences (in case of NTSC) See: http://www.chumpchange.com/parkplace/Video/DVPapers/dv_formt.htm ._
H0 | SC0 | SC1 | VA0 | VA1 | VA2
A0 | V0 | V1 | V2 | V3 | V4
V129 | V130 | V131 | V132 | V133 | V134
H0 | SC0 | SC1 | VA0 | VA1 | VA2
…
…
V129 | V130 | V131 | V132 | V133 | V134
DIF Sequence 0
DIF Sequence 9
…………
0
1
249
…………
80bytes
480bytes

## Slide 18: 1394 DV Transfer (for reference)
Example of DV Data transfer defined in IEC61883 is shown below.
125us
480bytes
Header
480bytes
480bytes
480bytes
Empty Packet

## Slide 19: DV Format Rate (SD-DVCR)
DV video rate is calculated by the followings.
  DV data size of one video frame 80 (byte/DIF block) * 150 (DIF block/DIF sequence) * 10 (DIF sequence/video frame) = 120,000 bytes
  120,000 (bytes/video frame) * 29.97 (frame/s;NTSC) = 3.43 (MB/s) = 27.44 (Mbps)
      (1M = 1024*1024)

## Slide 20: CIP Header (SD-DVCR)
00
FN
SID
DBS
QPC
s
r
10
FMT
r
SYT(Timestamp for DV data)
IEEE1394 isochronous header of DV transfer is the same as the one of MPEG2-TS.
In CIP header of DV transfer, the SYT field is defined. Other fields are the same as MPEG2-TS.
Source packet is not used since time stamp is applied as SYT field.
Data
1394 isochronous header
data_CRC
DBC
50/ 60
STYPE
FDF field

## Slide 21: CIP Header (SD-DVCR)
Each field is defined as the followings for SD-DVCR transfer.
  SID: depends on configuration
  DBS: 011110002 (120quadlets = 480bytes)
  FN: 002 (Not divided)
  QPC: 0002 (no padding)
  SPH: 0 (no source packet is used)
  DBC: 0 … 255
  FMT: 0000002 (Format type of SD-DVCR)
  FDF
    50/60: Field system (0: 60 field, 1: 50 field)
    STYPE: Signal type of video signal.
  SYT: Time stamp of the video frame synchronization.

## Slide 22: DV Format Rate of 1394 transfer
The DV data is transferred in every 125us.
The transferred DV data consists of 1394 header (12 bytes), CIP header (8 bytes) and DV data (480 bytes).
  DV data packet size = 12+8+480 = 500 (bytes)
  500 (bytes) / 125 (us) = 4(MB/s) = 32 (Mbps)
      (1M = 1024*1024)