## Slide 1: Evaluating the Performance of HRb Proposals in the Presence of Multipath
Steve Halford,
Karen Halford, and Mark Webster **
Intersil Corporation
September, 2000
Note: This power point documents contains notes. Set view to Notes pages to see the notes.
**With assistance from Chris Heegard of Texas Instruments

## Slide 2: Goals
Multipath is recognized as major WLAN impairment
  To select best waveform, must include multipath performance
Multipath Model was left as TBD by teleconference
  Want a model close to 802.11b model
  Want a model well-defined
    Compare proposal against the same measure
    Cross-validate multipath performance numbers
  Want a model that is fair to all proposals
  Want a model that reflects real radio conditions as much as possible
Notes: The HRb Teleconference group recognizes that multipath is a major channel impairment and in order to select the best waveform, the performance of each proposal must be examined in multipath. To speed along the teleconference, the committee left the details of the multipath model as a To Be Determined item.
Although no model was selected, there were several “wants” expressed. Specifically, the multipath model should be as close to the exponential channel model used by the 802.11b group. While there are many other models possible, the exponential model is familiar and is consider adequate for modeling the wireless LAN environment. In order to have a consistent comparison among the proposals, the parameters of the exponential model need to be very well defined. In addition, we want the model and its parameters to be selected in a way that is fair to all proposals independent of data rate and bandwidth. Finally, we want to select the model parameters so that the model reflects realistic radio conditions

## Slide 3: Overview
Multipath Models for WLAN
  Motivation
  Exponential Channel Model (IEEE 802.11b model)
    Truncation to FIR model
    Sample Rate
    Normalization
  Rayleigh Fading Model
  AWGN with multipath
Use of Channel Model : Block Diagrams
  Non-normalized
  Normalized
Summary of Proposal
Sample Code
Notes: In order to compare IEEE 802.11 HRb proposals, participants must agree on a consistent method for comparing competing waveforms with respect to multipath and additive white Gaussian noise. This presentation discusses these performance criteria and proposes that we continue to use the exponential channel from the IEEE 802.11 b standard to compare multipath performance. In order to have consistent use of the model, we will discuss the truncating the model to a finite length, the sample rate used to generate the channel, and the normalization procedure. In addition to the exponential channel model, we propose that a Rayleigh fading model be added. Finally, we propose that all multipath simulations be conducted in the presence of additive white gaussian noise. To summarize, we will show a proposed simulation test bed.
We conclude with a summary of our proposal and sample Matlab code.

## Slide 4: Multipath in WLAN
Notes: When a communication signal is transmitted through the air to a receiver, that signal will likely take several different paths before it reaches the receiver. Because the transmitter does not know precisely where the receiver is, it must transmit in several different directions. However, the direct path from the transmitter to the receiver is not the only signal that is received. Reflectors in the environment (filing cabinets, computers, etc.) reflect aberrant signals back to the receiver. All of these signal paths are combined at the receiver to produce a signal that is a distorted version of the transmitted signal.
This demonstrates distortion produced by these multiple signal paths. Notice that the received signal has a different appearance from the transmitted signal. As shown at the bottom of the illustration, these distortions can be represented by a single channel model. This channel model is then used to simulate the distortions encountered in similar wireless environments.
In this simple example, the received signal can be modeled as 3 combined signals arriving at different times and with different amplitudes. The delay and amplitude of each path is largely a function of the length of the path; however, other factors such as the how much of the signal is absorbed by the reflector and movement of the reflector also impact the delay and amplitude of a given signal path.

## Slide 5: Exponential Model
Used by Task Group b for 802.11 (see docs 97/96, 97/125, 97/157r1)
Taps are independent complex gaussian variables with average power profile that decays exponentially
where
Truncate to FIR
Normalize Average Power to 1
Notes: There are a plethora of channel models described in the literature; however, 802.11 TGb chose the exponential channel model because it is easy to generate and is a reasonably accurate model of the real world. This model is also appropriate for comparing the high rate proposals. Not only is this consistent with the old standard, but it will also provide an accurate yet relatively simple model for higher rate waveforms. The exponential channel model provides a good compromise between simplicity and reality. The taps in this model are complex, zero mean Gaussian random variables with variances that decay exponentially (hence the name “exponential channel model.”)
The parameters are the sampling period (which is the spacing between taps) and the rms delay spread . (In this presentation, when we refer to delay spread, this always means root mean square or rms delay spread.) The normalization factor, o, ensures that the sum of the average power profile is one. Theoretically, there are an infinite number of taps in the exponential model; however, the magnitude of the taps decays rapidly. Therefore, it is reasonable to truncate the taps at some point which is given by kmax.
References:
    1) IEEE 802.11-97/96, Naftali Chayat, September 1997.
    2) IEEE 802.11-97/157r1, John Fakatselis, November 1997.
    3) IEEE 802.11-97/125, Richard van Nee, November 1997.

## Slide 6: Exponential Channel Model
Average Power Profile
Sample Realization
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
Ts
2Ts
3Ts
4Ts
5Ts
6Ts
7Ts
8Ts
9Ts
10Ts
11Ts
time
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0.4
Ts
2Ts
3Ts
4Ts
5Ts
6Ts
7Ts
8Ts
9Ts
10Ts
11Ts
time
Notes: An actual realization of the exponential channel profile (shown on the right) will look very different from the averaged model (shown on the left). We point out in the sample realization that the largest path actually occurs at a delay of two sampling periods rather than at a delay of zero.

## Slide 7: Tap Truncation
Truncate to represent with an FIR model.
Value of last tap in truncated exponential channel:
Exponential channel is monotonically decreasing
Unmodeled taps are insignificant.
Therefore, remaining unmodeled taps
Notes: In the 802.11b channel model, the taps are truncated to kmax We show that this is an appropriate truncation for our purposes. Since the exponential channel is decaying monotonically, if the last tap is small, then we know that the channel is sufficiently long. Since , the value of the last tap in the 802.11b model is always 4.5e-5, a reasonably small number, we conclude that truncating at has not significantly altered our exponential channel model.

## Slide 8: Sample Rate and Exp Model
Sample rate determines “resolution” of taps
11 MHz Example
44 MHz Example
Only a problem at
low sample rate and
low multipath delay.
Notes: A second problem with this channel model is that the actual delay spread seen is not necessarily equal to the theoretical delay spread, . This occurs when the sampling rate is low relative to the rms delay spread, . In this case, the theoretical rms delay spread is not the same as the actual rms delay spread generated by the channel model. We illustrate this problem in the above example. In the left figure, the sampling rate is 11 MHz; thus the sampling period is 91 nsec. This figure shows the channel profile of an exponential channel with a delay spread of 30 nsec (less than the sampling period), but it is clear that the resolution of the channel is very poor. The actual delay spread of this channel is 21 nsec. The figure on the right shows a channel that has a sampling rate of 44 MHz or a sampling period of 23 nsec. In this case, the actual delay spread is 29 nsec which is much closer to the desired 30 nsec delay spread.
The figure in the lower right shows the theoretical vs. actual delay spread for various sample rates. The black line shows the ideal delay spread. Sample rates of 44 and 88 MHz yield an actual delay spread that is reasonably close to the theoretical delay spread as low as 10 nsec. However, a 22 MHz sample rate doesn’t start to produce an accurate actual delay spread until 30 nsec, and an 11 MHz sample rate doesn’t perform well even at 50 nsec.
We conclude that in order to achieve an actual delay spread that is approximately equal to a theoretical delay spread in the range of 10 to 50 nsec, the sampling rate should be at least 44 MHz. This statement is not intended to require a certain sampling rate; however, if we intend to compare performance of waveforms at these low delay spreads, the sampling rate should be reported.

## Slide 9: Normalization: Flat Fading & ISI
Channel model is normalized in an expected value sense
This normalization assumes an finite number of taps (unlike 802.11b model)
Channel Model includes flat fading & Intersymbol Interference
Power varies on a per trial basis
Average gain is one
Notes: The existing exponential channel model is normalized in the expected value sense. In other words, individual realizations do not necessarily have a power gain of 0 dB, but when taken over the ensemble of realizations, the average power gain is indeed 0 dB. This expected value normalization is due to the selection of the parameter20.. We note that this is not the same as generating the channel model and forcing each realization to have an average power gain of 0 dB. Consequently, this exponential channel model includes both intersymbol interference and flat fading.

## Slide 10: Flat Fading & ISI: Block Diagram
Exponential
Channel Model
Transmitter
Model
Packet Length
Data Rate
Sample Rate
Delay Spread
Receiver
Model
Measure
Packet Error
Rate
Packet Error
Rate
Measure
energy per bit
Calculate Noise Power
(N0)
Generate
Noise
Multipath results should include
  Eb/N0 Setting
  Channel Sample rate
  Delay spread
  Packet Length (1000 bytes)
  Packet Error Rate
Notes: This slide shows a suggested block diagram for a testbed to test a waveform’s performance in the presence of multipath. The items in red italics are the inputs to the test procedure. The output of the test procedure is the observed packet error rate.
For practical implementation, the energy per bit does not need to measured for each simulation run but rather can be derived theoretically. The purpose of the measurement in the this block diagram was to show at what point in the system the energy should be measured.
All simulation results should include the inputs and packet error rate.

## Slide 11: Normalization: ISI Only
Want to evaluate the proposals for ISI robustness w/o flat fading
  Need to normalize the relative gain (loss) of exp channel
  Care must be taken to ensure fair application of model
Potential Approach
If we force each channel realization to unit gain
Problem: Inconsistent results across channel sample rates
Normalization applies to entire bandwidth…not signal bandwidth
Example
Sample Rate = 88 MHz
  Normalized power of each realization
Power Gain for 22 MHz signal
  Shows the power variation
Penalizes samples rates >> bandwidth

## Slide 12: ISI Only: Suggest Approach
Exponential
Channel Model
Transmitter
Model
Packet Length
Data Rate
Sample Rate
Delay Spread
Receiver
Model
Measure
Packet Error
Rate
Packet Error
Rate
Generate
Noise
Measure
energy per bit
Calculate Noise Power
(N0)
For consistency -- Need to normalize at output of the channel
  Normalizes the signal bandwidth rather than entire channel bandwidth
Notes: In the past, many 802.11b multipath results which used the exponential channel model also normalized each realization. In other words, the forced each channel realization to have an average gain of 1 and consequently removed the flat fading component of the channel model. While this is appealing because it isolates the effects of intersymbol interference. This presents two main problems. One, it is not realistic since multipath naturally causes the relative power gain to fluctuate. Also, without additional specification, the per realization normalization is not consistent across all possible combinations of data rate and bandwidth. A simple Matlab realization is used to demonstrate this.
One solution to this is to normalize the received power after the channel. In other words, one measures the energy per bit at the output of the channel. This would then remove the variations in power seen out the output of the channel independent of the the sample rate and bandwidth. However, this requires more simulation complexity because the energy must be measured after generation of the channel and filtering.

## Slide 13: Rayleigh Fading
Classic model for multipath components with delay much less than sample rate
  Amplitude has a Rayleigh Distribution with uniform random phase
  Memoryless -- affects all signal frequencies the same (“flat fade”)
For convenience, can consider to be a limiting case of exponential channel
  Single tap channel with 0 RMS delay spread
    fix kmax equal to one
  Single tap will scale and rotate the received signal
    affect all frequencies in the same way since it is a multiplication not a convolution
Notes: When the relative power delay is much less than the sample rate, the receiver cannot resolve or doesn’t see the individual paths. A common channel model for this scenario is the classic channel model of Rayleigh Fading. Note that Rayleigh fading model assumes there is no direct line of sight path between the transmitter and receiver. This is realistic for wireless LANs and should be addressed in evaluating the performance.
To simplify the testing procedure, we propose that the Rayleigh fading case be consider as a subcase of the exponential channel model where kmax is fixed to 1 and the RMS path delay is fixed at zero. Practically, the variance of the noise used to generate the fixed at 1/2 for the real and imaginary component (i.e., 0 = 1). This results in a single tap channel model or multiplication of the signal by the value of the type.

## Slide 14: Multipath with AWGN
Additive noise can have a major impact on multipath performance
  Example: Zero-forcing & MMSE equalizer have same performance w/o noise
    Performance can be vastly different in presence of noise
Realistic to include both impairments simultaneously
  Sweep Packet Error Rates across a range of noise & multipath values
Q: Does HRb include additive noise in multipath comparisons?
A: Yes.

## Slide 15: Summary of Proposal
Propose using the current exponential channel model
  Identical to IEEE802.11b
    Truncate using
    Sample rate used to generate channel should always be given
    Normalization: Include both normalized and un-normalized results
      Normalization must be done at output of the channel
    Rayleigh fading included as special case of exp model
Showed suggested block diagrams
Recommend using PER with 1000 byte packets
  Include noise with multipath
  Vary levels of both noise and multipath
Cross-Verification: Include description of equalizer type
        (not required to give design details)

## Slide 16: Matlab® Code for Exponential Channel
Notes: This a Matlab function which implements the exponential channel model. The function requires the user to input the sample rate in megahertz and the desired RMS delay spread in nanoseconds. When the user enters a 0 nanosecond delay, the function generates a Rayleigh fading model.