## Slide 1: Spectral Mask Considerations for 802.11 HRb
Mark Webster and Karen Halford
Intersil Corporation
September, 2000
This Microsoft Powerpoint presentation has notes attached.
Please expand to “Notes Page View” mode.

## Slide 2: Overview
Present historical background leading current 802.11b spectral mask.
Describe modern digital spectral shaping techniques.
Identify an exploitable margin provided by current mask.
Examine impact of power amplifier on transmit spectrums.
Suggest that small changes to current spectral mask might be useful.

## Slide 3: Historical Origin of 802.11b Mask
11 MHz
Chip Rate
QPSK Signal
NRZ
Filter
5th Order
Butterworth Filter
Filtering the 11 MHz QAM signal with a 5th-order Butterworth Filter allows signal to fit in mask.
IEEE 802.11 Mask
Power Spectrum
Power Spectrum
Based-upon
Analog Techniques
Notes: The 802.11b mask is a carry-over of the 802.11 DSSS mask. The motivation for the mask was to allow simple implementations. Older systems used primarily analog filtering, as shown here. Square pulses, which create a SINC spectrum, are tapered by an analog filter.
It appears that a 5th order Butterworth filter is sufficient to meet this spectral mask.

## Slide 4: Modern Transmit Pulse Filters Example: Root Raised Cosine Filter
11 MHz Chip Rate
QPSK Transmitter
Root Raised
Cosine Filter
Excess BW = 50 %
Excess BW = 12.5 %
Excess BW = 0 %
Root Raised
Cosine Filter
Receiver
Frequency Response
of End-to-End Raised Cosine Filter
Log Scale
Linear Scale
Based-upon
Digital Techniques
Notes: More modern filters use digital pulse shaping.
A Root Raised Cosine Filter is a more sophisticated filter than the Butterworth filter. This filter will yield a signal with better spectral qualities. Here we show the Frequency response of a root raised cosine filter for various excess bandwidths. The larger excess bandwidth filters have smaller sidelobes while the main lobe has a wider bandwidth.

## Slide 5: Root Raised Cosine Filter
11 MHz Chip Rate
QPSK Signal
Root Raised
Cosine Filter
Allows one to either
Stack more channels
Or, increase chip rate.
Wasted
Bandwidth
12.5% Excess Bandwidth
Power Spectrum
IEEE 802.11 Mask
Notes: Here we show that a signal passed through a root raised cosine filter has a much smaller bandwidth than the mask. We could either add more channels or increase the data rate with this additional bandwidth.

## Slide 6: Increase Chip Rate using Root Raised Cosine Filter
18 MHz Chip Rate
QPSK Signal
Root Raised
Cosine Filter
12.5% Excess Bandwidth
Power Spectrum
Notes: Here we show that an 18 MHz chip rate QPSK signal passed through a 12.5% excess bandwidth root raised cosine filter fits within the mask! That’s a gain of 7 MHz!

## Slide 7: Impact of Power Amplifier?
RAPP Model
for PA
Ref. IEEE802.11-97/123
AM/AM Distortion
Notes: What impact does a power amplifier have on a transmitted signal?
Here we show the Rapp Model which models the nonlinearity of a power amplifier. It is commonly accepted that the Rapp Model with a parameter of p=2 or 3 is a good model for realistic PA’s. The plot shows a linear characteristic.

## Slide 8: 1 dB Compression Point vs. Full Saturation
-10
-9
-8
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
8
9
10
"p" parameter
Output Power
(dB)
Output Power at 1
dB Compression
Point
Saturation Point
dB Units
Notes: This plot shows the characteristic in dB vs. dB. The bottom right plot shows the saturation point and the 1 dB Compression Point for various values of p.

## Slide 9: Effect of Power Amplifier
11 MHz Chip rate
QPSK Signal
NRZ
Filter
5th Order
Butterworth Filter
Rapp PA (p = 2)
3.5 dB Output Backoff
Power Spectrum
Power Spectrum
after PA
Historical
Signal
Notes: The power amplifier has a nonlinearity which increases the bandwidth of the signal. In fact, this 11 MHz chip rate QPSK signal with a 5th order Butterworth filter is able to just meet the mask for this particular PA with a backoff of 3.5 dB.

## Slide 10: Effect of Power Amplifier for Higher Rate Signals
18 MHz Chip Rate
QPSK Signal
Root Raised
Cosine Filter
Rapp PA (p =2)
3.5 dB Output Backoff
Power Spectrum
after PA
Power Spectrum
12.5% Excess Bandwidth
Modern
Signal
Mask
Violations
Notes: The 18 MHz chip rate signal with a RRC filter certainly does not fit in the mask after the PA. But, the violations may not be significant from a system’s viewpoint.

## Slide 11: 802.11 HRb OFDM
802.11a
BBP
Rapp PA (p =2)
3.5 dB Output Backoff
22 MHz
CLK
Mask Violation
Similar to 18 MHz
QPSK
Notes: This slides shows the impact of the PA non-linearity on an OFDM. The mask violation between 22 MHz to 33 MHz is about the same as the QPSK on the previous slide. The violation is a little worse between 11 MHz to 22 MHz.

## Slide 12: Adjacent Channel Interference
802.11a
Rate ADJ Non-ADJ
6 16 32
9 15 31
12 13 29
18 11 27
24 8 24
36 4 20
48 0 16
54 -1 15
HiperLan2
Rate ADJ Non-ADJ
6 21 40
9 19 38
12 17 36
18 15 34
27 11 30
36 9 38
54 4 23
802.11: 35 dB Adjacent channel rejection with 30 MHz channel spacing.
802.11b: 35 dB Adjacent channel rejection with 25 MHz channel spacing
Data rate dependent spec seems superior.
20 MHz
channel spacing
?
Notes: 802.11 HRb should probably specify adjacent channel rejection similar to the 802.11a spec, where the requirement varies with the data rate. 802.11b adjacent channel spec is the same as the 802.11 spec. This seems overly restrictive.
802.11a has channels which are only 20 MHz apart, so if 802.11 HRb uses channels 25 MHz apart, a tighter HRb spec seems possible.

## Slide 13: Summary
Single carrier systems can have similar spectral behavior to OFDM’s
Advantages provided by minor mask violations may out-weigh the small loss in adjacent channel interference immunity.
Recommend spectral characteristic be part of the evaluation criteria.