## Slide 1: A IEEE 802.11e Proposal to support efficient MM streaming
Srinivas Kandala
Sharp Laboratories of America, Inc.
Camas WA 98607
E-Mail: srini@sharplabs.com

## Slide 2
Introduction:
Several proposals have been submitted for the consideration of the group towards enhancing the MAC to support QoS.
We consider most aspects in the joint proposal favorably.
However, for reliable and efficient isochronous data transfer with tolerable delay and jitter, the proposal needs to be further enhanced.
What exactly are we looking for?
  Address this in the presentation.

## Slide 3
A consumer electronics company with expertise in AV products.
Intends to deliver AV data from several sources to sinks in a home environment.
Intends to integrate the above with other services such as Internet, telephony etc.
Views IEEE 802.11 MAC with QoS enhancements as one of the key technologies in the home.

## Slide 4
Type2
Wireless LAN with
MM data Transfer
QoS
Multi Source
Multi Destination
Error Correction
Type1
Wireless LAN
Can be used in
MM applications.
Enterprise
world only
Technology Progression
IEEE 802.11 can help towards this progression.

## Slide 5
Multimedia Applications:
MM applications, involving audio and video data transfer are sensitive to delay, jitter and packet loss.
Need large amount of bandwidth.
A network level (such as IP) controlled MM data transfer
  increases the delay and reduces the throughput due to the overhead involved in processing and addition of headers.
  imposes restrictions on the implementation of schemes for efficient transport.
  the concept of delivering MPEG2 over IP is still not fully developed.
Several proposals seem to recommend interacting with the higher layers to administer QoS support.

## Slide 6
Multimedia Applications:
We suggest an approach where the QoS support is provided at the MAC layer and:
  allows for efficient MM streaming by allowing non-TCP/IP implementation
  TCP/IP based reservation can still be built on top of the MAC.
  does not interact with higher layer for bandwidth assignment
  does not tie to any particular technology

## Slide 7
Proposed Interface Reference Model
LLC
CE
BME
MAC
MLME
PLCP
PMD
PLME
STA
LLC
CE
BME
MAC
MLME
PLCP
PMD
PLME
E-SME
AP
DSBM
SE
(data, priority)
RME
E-SME

## Slide 8
List of Abbreviations:
AP - Access Point
BME - Buffer Management Entity
CE - Classification Entity
CTS - Clear To Send
DCF - Distribution Coordination Function
DSBM - Designated Subnet Bandwidth Manager
E-SME - Enhanced Station Management Entity
LLC - Logic Link Control
MAC - Medium Access Control
MLME - MAC Layer Management Entity
PCF - Point Coordination Function
PLCP - Physical Layer Convergence Protocol
PLME - Physical Layer Management Entity
PMD - Physical Medium Dependent
RME - Resource Management Entity
STA - Station

## Slide 9
QoS Operation:
The higher layer(s) will determine the priority of the data that needs to be transmitted through a Classification Entity (CE) which will provide the relevant IEEE 802.1Q priority tag.
  Necessitated by the fact that the IEEE 802.2 can transfer only a user priority.
The priority assigned along with the data, address and other parameters are passed down to the MAC through the LLC.
STA examines the data and its priority in its buffer using the buffer management entity (BME) and sends a bandwidth reservation request frame.

## Slide 10
QoS Operation (Cont’d.):
The Resource Management Entity (RME) in the AP will process the request using the Scheduling entity (SE).
  AP will submit its own requirements directly to the SE.
If sufficient resources are available, SE will schedule a transmission opportunity for the STA.
High Priority data will be scheduled in PCF.
Low priority data may be scheduled either in PCF or in DCF with a transmission of CTS by the AP.
If sufficient resources are not available, AP will send a RR Reject frame for the STA.

## Slide 11
QoS Operation (Cont’d.):
STA will transmit in its transmission window. The receiving STA may announce the size of its buffer window along with ACK to prevent overloading.
Policing function is performed by RME in AP.

## Slide 12
Classification Entity (CE):
Will translate the QoS parameters into a IEEE 802.1p priority level.
  Use a default class as suggested in RFC 2815 issued by IETF.
  Allow the possibility of AP changing the classification dynamically.
The translation will be based on a maximum data size over a time period (token bucket), delay, jitter and the actual priority.
The application (or a higher layer) will input the QoS parameters to obtain the priority level. It will then propagate the priority level to the LLC.

## Slide 13
Schedule Entity (SE):
This entity residing in the MAC layer will have an algorithm to determine the optimum scheduling of the data based on the requirements as well as the channel usage.
Manufacturer dependent.

## Slide 14
Providing support to RSVP protocols:
Subnet Bandwidth Manager (SBM) will reside at L3.
A STA desiring an RSVP based service will send the PATH message to the DSBM.
The Designated SBM (DSBM) located at the L3 of the AP will propagate the PATH to the destination.
Upon the receipt of the RESV message from all the routers in the path, the DSBM will use the services of RME to determine if there is enough bandwidth available.
  If enough bandwidth is available it will forward the RESV (with appropriate changes) to the STA. The required transmission window will also have been scheduled.
  This determination can be performed before the propagation of the PATH message.

## Slide 15
Support of RSVP Reservation (Cont’d.):
If the incoming PATH message comes from outside the LAN, DSBM will again use the RME to determine the bandwidth availability.
DSBM can use the services of RME for policing.

## Slide 16
Advantages of the Scheme:
QoS support becomes higher layer agnostic.
The above allows reduction of overhead and enables
  makes the MAC suitable for efficient streaming of Multimedia data.
  allows for the implementation of efficient higher layer protocols which keep the delay and jitter at tolerable levels for some applications.
The support will not be restricted to RSVP based schemes like IntServ.
  It will not be affected by the changes in any particular higher layer reservation scheme either.

## Slide 17
Reservation Request:
Provided in the same manner as described in the “Joint” proposal. However,
  a CCI (Centralized Contention Interval) should start only after all the outstanding data transmissions have been completed.
  To avoid possible loss of channel control to a (non-conforming) hidden node or to a non-compliant network, it is our recommendation to have all CCIs scheduled just before the CF-End.
  Allow the transmission of the Reservation Request frames in the DCF mode as well.

## Slide 18
Data Frame Processing by STA:
The STA MAC formats the data that it received from LLC by adding:
  IEEE 802.1Q priority and/or VLAN tags.
  Add the optional header FEC.
  Add the optional payload FEC.
  Compute the FCS.
Maximum size
of 2316 octets
MAC
Header
IV
802.1Q
Tag
Header
FEC
MSDU
Payload
FEC
FCS
ICV
24 or 30
0 or 4
0 or 16
0-2142
(0-9)*16
0-4
4
4 or 36

## Slide 19
Scheduling in DCF mode:
DCF should always be present.
DCF should be long enough to allow:
  Authentication and association services.
  Legacy equipment operation.
For some priority levels or if the load in the PCF mode is very high, the SE may decide to schedule some transmissions in the DCF mode:
  May control the scheduling/access by using different values for CW parameters for different priorities.
  Will announce the schedule of the transmission by transmitting CTS, whence the STA will start transmitting.

## Slide 20
Scheduling in DCF mode (Cont’d.):
Example:
CFP
RR
CTS
STA-AP
ACK
CP
Beacon
The above mechanism will also provide the capability of providing centralized QoS support without implementing the PCF.
Announcement of
the schedule
CTS

## Slide 21
Scheduling in PCF mode:
The mechanism proposed in the “Joint” proposal can be used.
However, the hidden node problem needs to be addressed.
Nodes that are hidden from each other may be scheduled to be transmitted in sequence, either through the Schedule frame or through Multi-poll:
  Almost impossible for the SE (TAME in Joint Proposal) to avoid this sequencing, as nodes may become hidden and visible with time.
  May result in a collision or failure of transmission by a hidden node.
  May even result in loss of channel access if a non-compliant device operates on the same channel.

## Slide 22
Scheduling in PCF mode (Cont’d.):
Example:
Schedule
Beacon
Sx - Sy
CF-End
CFP
CP
Next scheduled node z
is hidden. Will result in
silent period or a collision.
Scheduled

## Slide 23
Scheduling in PCF mode (Cont’d.):
Solution:
For “schedule” type of transmissions:
  For transmissions to the PC, PC shall always send an ACK or NULL (based on the acknowledgement policy) at the end of the transmission, but not necessarily at the end of every frame.
  PC shall always send a NULL at the end of every peer-to-peer communication.

## Slide 24
Scheduling in PCF mode (Cont’d.):
Solution:
Schedule
Beacon
STA-AP
CF-End
CFP
CP
ACK
AP-STA
ACK
STA-STA
NULL
ACK
Scheduled

## Slide 25
Scheduling in PCF mode (Cont’d.):
Any similar fix for multi-polling will increase the overhead and makes it less efficient than individual polling. We suggest dropping multi-polling.

## Slide 26
Conclusions:
A QoS based enhancement proposal that conforms to the functional requirements and is harmonizable with the joint proposal.
The proposal allows efficient streaming of MM.
Does not rely or use the functionality of any higher layer entities.

## Slide 27
Future Direction:
Evaluation of the proposal vis-à-vis other proposals is being done currently.
We favor harmonizing with any proposal as long as we can achieve
  higher layer independence,
  allow for efficient streaming.
  hidden node problem elimination.