## Slide 1: General Overview IEEE 802.11 WLAN Standard

## Slide 2: Content
Overview of IEEE 802
Current IEEE 802.11 Standards
New Developments within IEEE 802.11
ETSI Cooperation/Harmonization
Industry Promoter Groups

## Slide 3: IEEE Standards Association
Chair
SEC (17)
VOTING MEMBERSHIP (500)
IEEE 802
SPONSOR
US TAG
ISO/IEC
JTC1/SC6
APPEALS
PRESS RELEASES
RULES
COMPUTER
SOCIETY SAB
NESCOM – PARS
REVCOM – STDS
PATENTS
IEEE-SA STDS BD
IEEE-SA BD OF GOV
PUBLISHING
LMSC BALLOTS
SUPPORT
TRAINING
IEEE STDS
STAFF

## Slide 4: IEEE
IEEE Established in 1884 (AIEE & IRE)
IEEE December 1999 Membership was 360,000; 66% USA & 33% Non-USA
IEEE produces 30 percent of the world's published literature in electrical engineering, computers and control technology,
IEEE holds annually more than 300 major conferences and
IEEE has more than 800 active standards with 700 under development.

## Slide 5: IEEE 802 Organization
Executive Officers
Working Group Officers
= Active
= Hibernation
= Disbanded
= Wireless

## Slide 6: IEEE 802.11 Organization Chart

## Slide 7: IEEE 802.11 Projects

## Slide 8: Objectives of IEEE 802
Enable IEEE 802 to develop consensus standards that benefits the World Wide Networked Society.
Maintain the imperative principals of due process, consensus, openness, balance and rights of appeal.
Electronic distribution of standards.

## Slide 9: Current IEEE 802.11 Standard
Wireless Local Area Networks (WLAN)
Medium Access Control (MAC) Layer
Currently includes five Physical (PHY) Layers
  1 – 2Mbps Frequency Hopping Spread Spectrum
  1 – 2Mbps Direct Sequence Spread Spectrum
  1 – 2Mbps Infrared
  11 Mbps in 2.4 GHz
  54 Mbps in 5 GHz

## Slide 10: MAC Layer
Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
Infrastructure Network (Access Point)
Ad-Hoc Network (No Access Point)
Automatic Repeat Request (ARQ)
Power Saving Mode
Wireless Equivalent Privacy (WEP)
  64-bit encryption
MAC Management

## Slide 11: FHSS Physical Layer
2.4 GHz ISM Band
1 and 2 Mbps
2 or 4 level Gaussian FSK
79 channels
Hopping Rate > 2.5 hops/sec.
1 Watt maximum (100 - 500 mW typical)

## Slide 12: DSSS Physical Layer
2.4 GHz ISM Band
1 and 2 Mbps
Differential Binary and Quadrature PSK
Processing Gain: 11 chips per bit.
Three 20 MHz channels in ISM Band.
1 Watt maximum (100 - 500 mw typical)

## Slide 13: 11 Mbps in 2.4 GHz - IEEE 802.11b
Extension to original DSSS
Includes 5.5 and 11 Mbps modes
Backward compatible with original DSSS
Uses Complementary Code Keying (CCK) modulation
Uses Packet Binary Convolution Coding (PBCC) as an optional modulation
Three channels within 2.4 GHz Band
Uses Existing MAC Layer

## Slide 14: 54 Mbps in 5 GHz – IEEE 802.11a
Operates in the U-NII 5 GHz band
Uses Orthogonal Frequency Division Multiplexing (OFDM) Modulation
Information on multiple subcarriers
Many data rates depending on modulation on subcarriers and FEC
  Rates from 6 to 54 Mbps
Uses Existing MAC Layer

## Slide 15: Promoter Organizations
Wireless Ethernet Compatibility Alliance (WECA)
  Wi-Fi certification
  To ensure interoperability between multi-vendor products compliant to IEEE 802.11b 2.4 GHz 11 Mbps standard

## Slide 16: ETSI 5GHz Co-Ordination & Harmonization

## Slide 17: 802.11 New Developments
MAC Layer Enhancements (TGe)
  Add Quality of Service to support time-bounded services
  Enhance Security beyond WEP
Inter-Access Protocol (TGf)
  Define a standard protocol between access points to support features like roaming handoff
Higher Rate Study Group HRb SG
  Increase 2.4 GHz system to > 20 Mbps

## Slide 18: Things to add
Applications
Advantages of wireless
Technical issues
  Range – general coverage
  Interference – BT – portable telephone ????
  Safety issues in the 2.4GHz – 5GHz band
Future beyond current activities…
  More spectrum higher frequencies
  UWB
  Co-existence