## Slide 1: The GSS-API as an 802.11 Security Service
Jesse Walker, Intel Corporation
Bob Beach, Symbol Technologies

## Slide 2: Proposal Summary
Use GSS-API (RFC 2743) to define an abstract service interface for 802.11 security services
Use SPNEGO (RFC 2478) as the mandatory-to-implement GSS-API security negotiation mechanism
Use Kerberos (RFC 1510, RFC 1964) as the mandatory-to-implement GSS-API mechanism

## Slide 3: Agenda
Motivation
Proposals for 802.11
Kerberos Details
Sample Deployments
Proposal 2 and Legacy Privacy

## Slide 4: Motivation (1)
Satisfy the TGe Requirements document
Don’t reinvent the wheel
  Customers won’t deploy new mechanisms that make them throw away old security infrastructures
  Rolling our own will take years to get security right
  Reuse proven technology
Use well-defined tokens that easily fit into existing 802.11 frames

## Slide 5: Motivation (2)
Export security functionality out of 802.11
  KISS: MAC can’t solve the security problem by itself
  Concentrate on how to use security mechanisms, not what the mechanisms are themselves
Level the playing field
  Horizontalize network equipment market by introducing a standard API
  Only mandate algorithms with open source code
Enable opportunities for vendors to innovate

## Slide 6: Agenda
Motivation
Proposals for 802.11
Kerberos Details
Sample Deployments
Proposal 2 and Legacy Privacy

## Slide 7: Proposal 1: Negotiation, Authentication, and Key Mgmt
Negotiation: use SPNEGO (RFC 2478) pseudo mechanism to negotiate actual security mechanism
Mandatory-to-implement authentication: Kerberos (RFC 1510) GSS-API (RFC 1964)
  PKINIT+Kerberos for IBSS
  Free GSS-API Kerberos source code available at http://web.mit.edu/kerberos/www/
Other GSS-API mechanisms are optional

## Slide 8: Architectural Model: Authentication and Key Mgmt
GSS-API
MAC Sublayer Management Entity
MAC Sublayer
MLME_SAP
PHY_SAP
Select Mechanism
GSS-API
Imbed GSS-API tokens in 802.11 Mgmt Frames
GSS-API Mechanism
LLC
802.10SDE_SAP
MAC_SAP

## Slide 9: Proposed Mandatory Implementation: Initial Contact
STA
AP
KDC
GSS_Init_sec_context
GSS_Init_sec_context
Kerberos
Kerberos
GSS_Init_sec_context
KRB_AP_REQ
KRB_AP_REQ
KRB_AP_REP
KRB_AP_REP
KRB_TGT_REQ
KRB_TGT_REQ
KRB_TGT_REP
KRB_TGT_REP
Ticket, Authenticator
GSS_Init_sec_context
Authenticator
GSS_Init_sec_context
SPNEGO
Kerberos

## Slide 10: Proposed Mandatory Implementation: Roaming
STA
AP
KDC
GSS_Init_sec_context
KRB_TGT_REQ
KRB_TGT_REQ
KRB_TGT_REP
KRB_TGT_REP
Ticket, Authenticator
GSS_Init_sec_context
Authenticator
GSS_Init_sec_context
Kerberos

## Slide 11: Proposal 2: Bulk Data Protection
Use GSS_Wrap and GSS_Unwrap as an architectural service interface
  Use GSS_Wrap to produce token from input into the MAC_SAP
  imbed token as data field of an 802.11 data frame
  Use GSS_Unwrap to extract data to output through the receiver’s MAC_SAP

## Slide 12: Architectural Model: Data Protection
MAC Sublayer
MAC_SAP
PHY_SAP
GSS-API
GSS_Wrap
MAC Sublayer
MAC_SAP
PHY_SAP
GSS-API
GSS_Unwrap

## Slide 13: Mapping to Requirements (1)
Mutual authentication (4.1.1): satisified by Kerberos
Accommodation with QoS (4.2.1): satisfied by Kerberos
Access control (4.2.2): GSS-API can be integrated into 802.11 access control model
Data authenticity (4.2.3) and data confidentiality (4.3.1): satisfied by GSS_Wrap, GSS_Unwrap
Key derivation (4.4.1): satisfied by all GSS-API mechanisms
Secrets protected from eavesdroppers (4.4.2): satisfied by all GSS-API mechanisms

## Slide 14: Mapping to Requirements (2)
Security service negotiations (4.5.1): satisfied by SPNEGO pseudo-mechanism
Extensibility (4.5.2): well-defined API producing opaque tokens for us to pass back and forth
One mandatory-to-implement algorithm (4.5.3): Kerberos only mandatory-to-implement security mechanism
Scalability to all 802.11 environments (4.6): Yes; see examples to follow
  Mandatory to implement mechanisms support Enterprise, SoHo
  Add PKINIT or SRP for ad hoc support
  Add SPKM to support public networks

## Slide 15: Agenda
Motivation
GSS-API Proposal for 802.11
Kerberos Details
Sample Deployments
Proposal 2 and Legacy Privacy

## Slide 16: Kerberos Specific Issues
New Authentication Model
IP-less Kerberos
Relationship between AP, KDC?
Time distribution
Roaming optimizations

## Slide 17: “Associate, then authenticate”
GSS-API model allows any STA to associate with any AP
  flips current “authenticate, then associate” model
Unauthenticated STA can send only to AP/KDC
  AP drops frames to other destinations
  AP allows no direct unicast traffic to STA
Unauthenticated STA must authenticate within short time (few seconds) or AP drops its association

## Slide 18: Kerberos without IP
All existing Kerberos implementations run over IP
Proposal encapsulates Kerberos messages in 802.11 Management frames
  GSS-API mechanisms generating messages must use SDE_SAP
Each AP maintains a KDC “Proxy”:
  encapsulates User Kerberos messages in UDP/IP frame
  uses own IP address for these frames
  may filter bogus or malformed Kerberos requests
  protects KDC from unauthenticated users

## Slide 19: Relationship between KDC, 802.11?
Outside the scope of 802.11, but ...
Architecture permits KDC
  in the AP (useful for home, So/Ho)
  outside the AP (useful for enterprise campus)
    contacted directly by AP
    contacted via proxy device (e.g., RADIUS server)
  in the STA (useful for IBSS when combined with PKINIT)

## Slide 20: Time Distribution
Kerberos relies on synchronized time
  Users need current time synchronized with KDC’s time, accurate to within seconds
Two sources: NTP or internal clock in AP
AP broadcasts time on regular basis
  any STA can hear it
  add to beacon?

## Slide 21: Roaming
Can we optimize roaming?
  Possibility #1: All AP’s share an identity with the KDC (the AP service is registered with the addresses of every AP)
  Possibility #2: Distribute a “roaming” key to the APs who distribute it to the STAs

## Slide 22: Agenda
Motivation
GSS-API Proposal for 802.11
Kerberos Details
Sample Deployments
Proposal 2 and Legacy Privacy

## Slide 23: Example: Campus LAN
Centralized Kerberos KDC configured
APs configured to use centralized KDC
STAs send Kerberos ticket request to APs
APs proxy ticket requests from STAs to KDC
APs proxy responses from KDC to STAs
STAs and APs authenticate via tickets returned to STA from KDC

## Slide 24: Example: Home/SoHo LAN
Kerberos KDC embedded in AP
STAs request tickets to APs
KDC within AP responds directly to STA’s ticket request
STA and AP authenticate via ticket issued to STA by the AP’s KDC

## Slide 25: Example: Ad hoc Network (1)
Each STA maintains its own Kerberos “KDC-let”
Ad hoc network users exchange PGP certificates in the clear at a “PGP key signing party”
To establish per-link keys with IBSS peer, run the PKINIT+Kerberos GSS-API mechanism, using PGP certificates to establish Kerberos ticket

## Slide 26: Example: Ad hoc Network (2)
Each STA maintains an SRP database
Ad hoc network participants
  agree on a common password and “username”
  configure their local SRP databases with the password and username
To establish per-link keys with another peer in IBSS, run the SRP GSS-API mechanism

## Slide 27: Example: An Internet Cafe
Step 1: Use SPKM to establish secure link
  STA generates a random session key, encrypts with infrastructure’s public registration key
  sends encrypted key to AP
Step 2: Run XML over secure link to get credit card number from customer
Step 3: Open link to Internet after customer pays
Remark: this emulates the SSL e-commerce model

## Slide 28: Example: Legacy Authentication
Step 1: Use SPKM to establish secure link
Step 2: Use legacy 1-way user authentication (e.g., via 802.1x) over secure link to authenticate STA user to infrastructure
Step 3: Open access to infrastructure network to the legacy authenticated user

## Slide 29: Example: Registration
Step 1: Use SPKM to establish secure link
Step 2: Use EAP (802.1x) over secure link to authenticate user to infrastructure
Step 3: Run CMP, CMC, or CEP Certificate Registration to issue certificate, policy to wireless station or user
Step 4: Use PKINIT+Kerberos to establish per-link keys thereafter

## Slide 30: Example: Credentials Retrieval
Step 1: Use SPKM to establish secure link
Step 2: Run SACRED over secure link to allow user to retrieve credentials from the Internet
Step 3: Rerun SPNEGO to renegotiate link with retrieved credentials

## Slide 31: Where is the Work (1)?
Details of token encapsulation, forwarding, retries, etc. in 802.11 Mgmt frames
Details of access control state machine to allow mechanisms to passes GSS messages as required
Details of GSS_Wrap token encapsulation in 802.11 data frames
Details of rekey
IBSS specific algorithms, e.g., overcoming race conditions on negotiation

## Slide 32: Where is the Work (2)?
Relate (I)BSS name to security mechanisms
Additional information desirable in beacons
Standardize GSS-API parameters to be used with each mechanism within 802.11
Clock synchronization for Kerberos
Negotiate for source code to be truly exportable
Work to get AES incorporated into GSS-API mechanisms

## Slide 33: Anything else within scope worth doing?
Standardized use of legacy authentication?
  If we don’t, market will not take 802.11 authentication seriously. Is it in scope?
Standardized public network mechanics?
Standardized registration, policy distribution?
Broadcast key distribution?

## Slide 34: Agenda
Motivation
Sample Deployments
GSS-API Proposal for 802.11
Discussion
Proposal 2 and Legacy Privacy

## Slide 35: Why use GSS_(Un)Wrap?
The API is already defined and works
  concentrate on using known primitives correctly instead of inventing new schemes requiring their own analysis
  quicker time to interoperability
It will take too long to get key derivation right
Wrap/Unwrap mechanism exportable
  API conformant mechanism can be plugged into crypto-less 802.11 exported overseas
Doing key derivation, security payload formats in 802.11 works moves security back into MAC

## Slide 36: Why not WEP for bulk data?
Datagram service means RC4 key schedule must be recomputed for each frame  bad performance
WEP doesn’t deliver on its promise of privacy
  50% chance of a collision among <key, IV> pairs after only 224/2 = 212 = 4096 frames throughout entire BSS
  And cryptanalysis of RC4 easiest at beginning of output key stream anyway
  WEP applies the easily cryptanalyzed part of the RC4 key stream to known plaintext headers
  IP header id field enables differential cryptanalysis
WEP moves crypto considerations into 802.11

## Slide 37: Conclusions
GSS-API and supporting mechanisms meet the TGe requirements
Proposals has other desirable properties as well:
  simple
  relies on widely deployed security service, Kerberos
  removes crypto considerations from 802.11 per se
  addresses a very large number of deployment scenarios
  levels the playing field from a security perspective
  opens the door to innovation by vendors

## Slide 38: Feedback?