## Slide 1: Suggested PA Model for 802.11 HRb
Mark Webster
Intersil Corporation
September, 2000

## Slide 2: Overview
This presentation describes a power amplifier non-linearity for 802.11 HRb proposal use.
The PA impacts spectral mask.
The PA impacts packet-error-rate.
The model is a fair representation of solid-state power amplifiers.
The model is easy to use.
Used by 802.11a.
OFDM for Wireless Multimedia Communications Richard van Nee, Ramjee Prasad, Artech House, 2000

## Slide 3: Effect of Power Amplifier
11 MHz Chip rate
QPSK Signal
NRZ
Filter
5th Order
Butterworth Filter
Rapp PA (p = 2)
3.5 dB Output Backoff
Power Spectrum
Power Spectrum
after PA
Historical
Signal
Power Spectrum
before PA
Notes: The power amplifier has a nonlinearity which increases the bandwidth of the signal. In fact, this 11 MHz chip rate QPSK signal with a 5th order Butterworth filter is able to just meet the mask for this particular PA with a backoff of 3.5 dB.

## Slide 4: General PA Model
AM/AM
Distortion
AM/PM
Distortion
Matlab
Abs(*)
Matlab
Angle(*)
Amplitude of
Envelope
Phase of
Envelope
+
Power Amplifier
Time-varying
Signal Envelop

## Slide 5: Recommended PA Model
RAPP
AM/AM
Distortion
Matlab
Abs(*)
Matlab
Angle(*)
Amplitude of
Envelope
Phase of
Envelope
Power Amplifier
Fairly Representative of Solid State Amplifiers

## Slide 6: RAPP Model for AM/AM
RAPP Model
for PA
Ref. IEEE802.11-97/123
AM/AM Distortion
0 dB Output
Back-Off from
Full Saturation
Notes: What impact does a power amplifier have on a transmitted signal?
Here we show the Rapp Model which models the nonlinearity of a power amplifier. It is commonly accepted that the Rapp Model with a parameter of p=2 or 3 is a good model for realistic PA’s. The plot shows a linear characteristic.

## Slide 7: Output Power Description: 1 dB Compression Point vs. Full Saturation
-10
-9
-8
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
8
9
10
"p" parameter
Output Power
(dB)
Output Power at 1
dB Compression
Point
Saturation Point
dB Units
Notes: This plot shows the characteristic in dB vs. dB. The bottom right plot shows the saturation point and the 1 dB Compression Point for various values of p.

## Slide 8: How to Specify Drive Level
OPTIONS
1. PA input back-off from 1 dB Compression point.
2. PA output back-off from 1 dB Compression point.
3. PA output back-off from full saturation.
COMMENTS
1 dB compression point is amplifier model dependent.
Output from full saturation is directly usable in link budget calculations.

## Slide 9: Practical Matters
RAPP
Model
Measure
Average
Packet Power
TX
Packet
Add multipath, noise
and send to Receiver
Output Back-off
(OBO) from
Full
Saturation
2x to 4x
over sample
Gain Adjust
for Desired
OBO

## Slide 10: Matlab Code
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% RappPa.m
%
% RAPP model of a power amplifier.
%
% Input: Vector of complex numbers.
% Output: Vector of complex numbers with same dimension as input.
%
% Mark Webster September 18, 2000
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
function y = RappPa( x, p )
denom = (1 + abs(x).^(2*p)) .^ (1/(2*p));
y = x ./ denom;

## Slide 11: Summary
Recommend use of RAPP PA model.
Use p=2 and p=3.
Measure output back-off (OBO) from full saturation to specify the drive level.
Over-sample signal 2x to 4x.
Show influence on spectrum (mask).
Show influence on Carrier Degradation in AWGN.